## Slide 1
Incremental Small Delay Defect Methodology
Swapnil Bahl+, Akhil Garg+, Roberto Mattiuzzo*, Saverio Graniello*, Paolo Cavenaghi*
+STMicroelectronics, Greater Noida, India *STMicroelectronics, Agrate, Italy
{swapnil.bahl, akhil.garg, roberto.mattiuzzo, saverio.graniello, paolo.cavenaghi}@st.com
Introduction to SDD Fault Model
SDD ATPG Flow @ ST
δ=0.6
δ=0.4
δ=0
slack
Max δmax and Limitations
SDD targets each defect to be tested via worst slack path.
A fault is considered to be detected if it is detected via any path within a deviation δmax from the worst path.
Results
Path A
Path B
fault
Path B
faulty
Path B
fault free
Fault delay
clk
Path A
faulty
Path A
fault free
Fault delay
clk
Faults can be targeted via any path within a permissible limit of worst slack path called δmax.
Permits flexibility and optimize the no of patterns.
A higher value of δmax increases the probability of fault detection during fault simulation but may decrease the quality of patterns
Incremental SDD Flow
Smaller δmax values for the faults with lesser slack value
Higher δmax values for the faults with higher slack values
Restricts fault detection during fault simulation through smaller paths
Critical faults are detected close to their worst slack path
Conclusion and Future Work
1.2M gate design
Standard ATPG
Incremental ATPG
Better Fault detection
Fault Escaped
Fault detected
SDD ATPG requires data exchange between multiple tools.
Completely automated flow @ST
New plot to see the quality of patterns
delta-slack plot showing the deviation of detection via colors on the slack histogram
Least deviation is represented by the green color and the higher values are represented with red color
High Quality Patterns
Negligible impact on pattern count
Better ways to quantify pattern qualities need to be investigated.
δ=0.2