## Slide 1: Shapes-based Process Migration and DFM Optimization using Minimum Perturbation Compaction
Ryan Bazinet, Veit Gernhoefer, Michael Gray, Matthew Guzowski, Kevin McCullen, Rani Narayan, Bob Walker, Xin Yuan

## Slide 2: What is “Layout Migration?”
Sometimes called “Process Migration” …
Taking a pre-existing layout and converting to a different set of ground rules (usually into the next process node).
  For example, here we converted an existing 65 nm SOI design into a 45 nm SOI technology.
The schematic is held constant (parameters scale, but the netlist is unchanged.)
Layout Migration is not placement and routing.
This migration path uses “Minimum Perturbation Compaction”
  Not “longest path”. Not area minimization
  The goal is a new design that is as close as possible (given the new ground rules) to the old design.
Migrate “Common Library” elements first, then use newly migrated versions in migration of macros.

## Slide 3: The Keys to Success
A Migratable Technology
  The technology ground rules must “scale.”
    No rule value grows significantly to the others as you move from 65 nm values to 45 nm values.
  The migration tool can swap space around, move shapes back and forth, but it cannot “Create” free space.
  The teams (Litho, Process, Design, Tools) have to hammer out compromises that produce a manufacturable technology that is scalable.
    Rules are proposed and compared to existing layouts using “reverse scaling”
    Take proposed 45 nm value, multiply it by 1/scaling-ratio, DRC check the 65 nm design against these values.
    This shows what layout structures in the 65 nm design will fail 45 nm DRC after scaling.
    Analyze the results to see if there is space for the migration tool to fix the resulting errors in the migrated design.
Migratable Subcells
  Each subcell has to scale in outline, pin positions, and (as much as possible) internal blockages.
Duplo to Lego “Migration”
65 nm to 45 nm Migration

## Slide 4: “Common Library” Migration Paths
Initial 65 nm
PCells
Define boundary
and pin conditions
Rewrite skill code
to meet 45 nm
rules
Final 45 nm
PCells
Final 45 nm
Custom cells
Initial 65 nm
Custom Cells
Scale in X and Y by
master scaling ratio
Freeze cell outline
Freeze pin locations
Ground rule cleanup
Passes with
Minimum Perturbation
Compaction
X/Y/X/Y/etc
Migrated 45 nm
Custom cells
> 99% clean
Manual DRC Cleanup

## Slide 5: Macro Migration
Initial 65 nm
macro
Scale in X and Y by
master scaling ratio
Freeze macro outline
Freeze pin locations
Freeze positions of subcells
Initial DRC snapshot
(for comparison purposes)
Remastering
Rename subcells to 45 nm
versions. For PCells, scale
parameter values by master
scaling ratio
Import data into Cadence
45 nm environment, export
from environment
(to replace subcells)
Ground rule cleanup
Passes with
Minimum Perturbation
Compaction
X/Y/X/Y/etc
Final DRC snapshot
(for comparison purposes)
Migrated 45 nm
Macro
> 99% clean
Manual DRC Cleanup
Final 45 nm
macro
Final 45 nm
Custom cells
Final 45 nm
PCells

## Slide 6: What is “Design for Manufacturability?”
Design for Manufacturability (DFM) is the rules and design principals that are applied to minimize defect-induced yield loss in the design of a chip. It allows for:
  Faster technology and product development because manufacturing sites typically target CA and V1 images at upper specification limits and metal spacing near lower specification limits to prevent open circuits.
  Improved yields because the resulting designs will be less sensitive to the random manufacturing defects that impact yield.
  More chips that fulfill the specifications sooner.
  Fewer process variations, especially for contacts.
  Fewer parasitics and improved circuit performance.
In-house yield-checking software was used to identify areas for DFM improvement.
  Is basically a design rule checker with stricter rule values.
  A score is calculated.
    SCORE = NORM – ERROR / NORM
    ERROR = the number of violations
    NORM = the total number of occurrences
  If the score meets a predefined threshold value, the check passes.
  Priorities are defined for the rule checks.
    Indicate the predicted relative yield leverage
    The prioritization allows for making design trade offs when two changes of differing priorities would be in conflict

## Slide 7: Modifying design for DFM
Design modifications for DFM were done manually and with software
Software was used for systematic improvements such as optimizing silicide resistance, redundant via placement, metal short edge removal, increasing area of small metal islands, and n-well optimization for stress effect.
These systematic improvements were implemented with additive overlay cells at the macro, unit, and chip level of design.
No changes were made to the shapes in the design hierarchy that were created by the designer, router, or migration tool
macro
macro_MSE
A
B
…
…
C
Extra metal in overlay cell to remove a metal short edge

## Slide 8: Modifying Design for DFM
Macro/Unit/Chip
Cover Cells
Merged Design
DFM Tool
Overlay Cell
Merge overlay cell for next DFM Tool
All Overlays
Cover Cells contain blockage shapes – Wiring Contract (i.e. macro has a wiring contract with the unit)
Each DFM optimization takes space so the optimizations are run in order of their prioritization
Each optimization needs the result of the previous optimization

## Slide 9
Reducing resistance improves performance
  Contact + Silicide = total contact resistance
    The narrower the Silicide past Gate  the less squares of Silicide = higher resistance
    Less Contacts  have long runs of Uncontacted Silicide = higher resistance
Effective Silicide + Contact Resistance
 | % Errors Fixed
Silicide past Gate | 99.90%
Uncontacted Silicide | % Errors Fixed
Severity 1 | 0.00%
Severity 2 | 5.08%
Severity 3 | 31.60%
Severity 4 | 13.17%

## Slide 10
Redundant Vias
SOLID RED – Added Vias
SOLID BLUE – Improved Metal Coverage
Cross Thatched BLUE – Corner/Notch Fill
Adding Redundant Vias improves yield, reliability and resistance
  Single Vias identified and another via placed if room by trying first in the metal’s primary wiring direction
  Picks up any opportunities left by the router

## Slide 11: Hollow Metal
Hollow metal is a known failure issue. Increasing metal island dimension reduces failure rate and improves yield
Metal area | % Errors Fixed
1st metal layer severity 2 | 93.60%
1st metal layer severity 3 | 92.85%
2nd metal layer severity 1 | 100.00%
2nd metal layer severity 2 | 84.60%
2nd metal layer severity 3 | 95.17%
3rd metal layer severity 1 | 100.00%
3rd metal layer severity 2 | 99.43%
3rd metal layer severity 3 | 99.60%

## Slide 12: References
Migration of Cell Broadband Engine from a 65nm to a 45nm SOI Technology, Takahashi, et. al., ISSCC 2008
Practical Method of Obtaining a Feasible Integer Solution in Hierarchical Layout Optimization, Tang, et. al., ICCAD, 2007
The Circuit and Physical Design of the POWER4 microprocessor, Warnock, et. al., IBM Journal of Research and Development, January 2002.
A VLSI Artwork Legalization Technique Based on a New Criterion of Minimum layout Perturbation, Heng, et. al., ISPD 1997
US Patents:
  US6189132, US6986109, US7062729, US7120887, US7363601, US7568173, US7490308