## Slide 1: Accelerating DV closure through coverage adaptive techniques for optimal test-suite generation
Authors:
Ashish Chandra, Texas Instruments, Bangalore
Co-authors:
Subir Roy, Texas Instruments, Bangalore
Chaitanya Vaddadi, Texas Instruments, Bangalore
Vasant N Vaghamshi, Texas Instruments, Bangalore
Harsh Setia, Texas Instruments, Bangalore
Sai Komaravelli, Texas Instruments, Bangalore

## Slide 2: Problem statement
DV Closure time α Functional coverage
The “perfect” methodology to achieve 100% coverage in single run still eludes a DV engineer.
Traditional approach
Limitations--
         Less features covered per simulation cycle
         Low bug finding per simulation cycle
         Huge count of testcases and low quality of stimulus per testcase.
         High regression suit runtime and more compute resource wastage, herein
        adversely affecting the DV closure time.
         ‘Duplicate scenarios’ & poor random seed runs
Define coverage grids
Dump testcases
Run simulations
collect missing holes

## Slide 3: What does this paper propose?
A Set of methodologies with focus on:
Agenda?
Reduce the iterations to achiever 100% functional coverage
Expand the local automation to a standardized process for it to be used across projects
  Ease of integration Adaptability to Design
  Time to implement Coding & output dumping
  Ease of use Automation Level
  Compute resource LSF + License usage
  Portability To new Environment

## Slide 4
Method1:Coverage log file grep
FEEDBACK FROM COVERGE REPORT FILE TO TESTCASE GENERATION SCRIPT.
PERL-BASED TESTCASE GENERATION FOR FUNCTIONAL COVERAGE POPULATION
How it does:
Identification of functional coverage grid points:
Generation of coverage log file with all the buckets:
Identification of the macros for each scenario:
Pick suitable macro from configuration file & run simulation
Gains?
--Precisely locate missing holes
--Dump “missing holes” testcases
--Less simulation runs

## Slide 5
Method2:Coverage monitor dumping test suite
How it does:
Extracts scenario information from the monitor code
“Commands” scenario generator to focus on specific randomization around monitor events
Dump complete test suite in single dump
Gains?
--Removes redundancy in testcases
--Smaller test-suite, ‘relevant’ scenarios
--Manifold decrease in coverage closure time
COVERAGE MONITOR FEEDBACK LOOP FOR BETTER STIMULUS GENERATION AND DUMPING
TESTCASES USING A PERL-BASED SCRIPTING ENVIRONMENT

## Slide 6
Method3::Dynamicaly modify testcase during runtime
ADAPTIVE COVERAGE BASED TEST CASES TO ACCURATELY COVER THE REQUIRED COVERAGE GRIDS
How it does:
At runtime, snoop the test randomization w.r.t coverage grids,
Send feedback, modify testcase in pre-randomization stage
Cover “exact” intended grids
Gains?
--Eliminates “duplicity of scenarios”
--Real time feedback, smaller test suite
--Fully automatic, less error prone

## Slide 7
Method4::Dynamicaly modification with high randomization
ADAPTIVE COVERAGE BASED TEST CASE CREATION WITH MULTI SEED RANDOMIZATION
How it does:
At runtime, snoop the test randomization w.r.t coverage grids,
Send feedback, modify testcase in pre-randomization stage
Group missing holes in buckets
Run ‘n’ seed regression to fill missing space
Gains?
--High randomness, even smaller test suite
--Smarter to catch corner case bugs
--Fully automatic, less error prone

## Slide 8: Results/returns & Limitations
Category | Traditional Flow | Automated Flow
Num of coverage events | 83521 | 83521
Iterations to reach 100% coverage | 13 | 4
Testcase count | 1785 | 345
Simulation time/resource usage | 11hrs | 4hrs
Time for creating monitors | 1hr | 2hrs
Method1:Coverage log grep process
TI C55x processor memory subsystem Verification
Method2:Coverage monitor grep
TI C55x processor Instruction set Verification
Category | Traditional Flow | Automated Flow
Num of coverage events | 81,321 | 81,321
Iterations to reach 100% coverage | 13 | 3
Testcase count | 3221 | 76
Simulation time/resource usage | 11hrs | 4hrs
Time to implement | 10weeks | 2weeks
Method3:Automated flow, feedback loop to test case
Standardized process & deployed across TI projects
Considerably reduced Verification cycle time by 10X
Limitations?
--More “coverage specific” testcase & less randomization
--High portability effort, method hooked to environment
Method3:Automated flow, feedback loop to test case with high randomization
Standardized process & deployed across TI projects
Considerably reduced Verification cycle time by 10X
An improvement on Method3 with higher degree of randomization
Limitations?
--Sensitive to changes in constraints
--High portability effort, method hooked to environment
Limitations?
--More “coverage specific” testcase & less randomization
--Closely tied to coverage log file format
Limitations?
--Needs stable monitor code
--Closely tied to coverage monitor format

## Slide 9: Comparison Metrics Method1 Vs Method2 Vs Method3 Vs Method4