## Slide 1: RTL Power Optimization in Sequential Analysis Platforms
Jairam S1, Subrangshu Das1, Mohit Sharma1, Udayakumar H1, Jagdish Rao1, Amit Goldie2, Abhishek Ranjan2
1. Texas Instruments 2. Calypto Design Systems
Email: 1: (sjairam,s-das2,msharma,uday,j-rao)@ti.com
2: (agoldie, aranjan)@ calypto.com
Notes: <number>

## Slide 2: Motivation
Structural clock gating methods have been well integrated to VLSI design flows as a part of synthesis and physical design
Sequential approaches yield substantial power savings over and above structural clock gating
Need an approach to automate these schemes and integrate them into mainstream design methodologies

## Slide 3: Problem Statement
An approach that seamlessly integrates power profiling, sequential clock gating, formal verification and logic simulation into a robust design methodology and helps increase design productivity

## Slide 4: Basic Clock Gating Methods
D
q
CLK
EN
RTL Syn
d
Q
q
d
EN
CLK
Low-Power RTL Syn
D
Q
CG
CG
CGO depends on the loading conditions of the
clock gate and clustering of the flops in a region
Can be performed only at physical design stage to
obtain maximum benefit
Mux-Feedback Loop (MFL)
IO Exclusivity (IOEX)
always @(posedge CLK)
begin
if (EN)
Q <= D;
end
Notes: <number>

## Slide 5: Sequential Clock Gating
A technology that can observe the logic path beyond a clock-to-clock boundary
A very effective method that can help gate combinational logic cones along with the forward/backward Clock-to-Q arcs of flip-flops as well
  Needs flops to be added for forward path traversal
The technology is based on formal reasoning and not just structural semantics
Notes: <number>

## Slide 6: Sequential Clock Gating: Logic Traversals
din
vld
d_1
d_2
dout
vld_1
vld_2
Original RTL
Power Optimized RTL
din
vld
d_1
d_2
dout
vld_1
vld_2
CG
CG
CG
Combinational Analysis
Sequential Analysis
Observability based CG
f_1
f_2
g_1
g_2
dout
din_1
vld_1
din_2
vld_2
Original RTL
Power Optimized RTL
din_1
vld_1
din_2
vld_2
f_2
g_1
g_2
f_1
dout
CG
Combinational Analysis
Sequential Analysis
CG
CG
CG
CG
Backward Traversal
Forward Traversal
Input-Stability based CG
Will Pre-empt all IOEX CG @ Netlist
Will Pre-empt some IOEX CG @ Netlist
Notes: <number>

## Slide 7: Key to Optimization : Clock-Gating Efficiency
Register-level Clock-Gating Efficiency
  Percentage of time a register (clocks) is gated for a given scenario
Registers
R0
Duration
100%
Rn
Registers
Duration
100%
Rn
R0
Average Clock
Gating Efficiency
Block-level Clock-Gating Efficiency
  Average of efficiencies for all registers for a given test bench
Average Clock
Gating Efficiency
Efficiency is the main cost factor for sequential clock gating
CLK
EN
CG
CLK
EN
R0
Registers clock gated = 100%
Clock-gating efficiency = 30%
Efficiency Improvement
Notes: <number>
<number>
<number>
Purpose:
Explain the definition of clock gating efficiency
Main points:
  Measuring the number of registers with clock gates is not sufficient since it does not take into account how long the register is gated (turned off). In this example the register is 100% clock gated, however if you look at the switching activity on the enable (EN) signal you see the enable is low only 3 out of 10 clocks. Consequently the clock-gating efficiency is 30%.
  First Build: If we calculate the clock-gating efficiency for all the registers in a design R0 to Rn, then the average of those efficiencies is the clock-gating efficiency for the design block. This diagram shows both registers with clock gates (red bars) and registers with no clock gating (no bars)
  Second Build: PowerPro CG improves clock gating efficiency by added clock gates to registers not previously clock gated and by extending the duration registers are gated (turn off) by strengthening the enable conditions.
  Clock-gating efficiency is a much better indicator of dynamic power savings from clock gating since it takes into account the switching activity in the design.

## Slide 8: Creating New Enables
RTL Synthesis
or
Low-Power RTL Synthesis
en
CLK
SEL
CLK
D0
CLK
D1
q0
q1
Out
CLK
SEL
CLK
D0
CLK
D1
CG
CG
en
q0
q1
Out
Low-Power RTL Synthesis
32
32
32
32
32
32
always @(posedge CLK)
begin
q0 <= D0;
q1 <= D1;
en <= SEL;
end
assign Out = en ? q0:q1;
always @(posedge CLK)
begin
if (SEL == 1’b1) //PowerPro-CG
q0 <= D0;
if (SEL == 1’b0) //PowerPro-CG
q1 <= D1;
en <= SEL;
end
assign Out = en ? q0:q1;
1
0
1
0
Notes: <number>

## Slide 9: Strengthening Existing Enables
Low-Power RTL Synthesis
Low-Power RTL Synthesis
32
sel
q0
q1
Out
32
32
CLK
SEL
STALL
D0
D1
32
32
CG
CG
CG
32
sel
q0
q1
Out
32
32
CLK
SEL
STALL
D0
D1
CG
32
CG
CG
always @(posedge CLK)
if (~STALL) begin
q0 <= D0;
q1 <= D1;
sel <= SEL;
end
assign Out = sel ? q0:q1;
always @(posedge CLK)
if (~STALL) begin
if (SEL == 1’b1) //PowerPro-CG
q0 <= D0;
if (SEL == 1’b0) //PowerPro-CG
q1 <= D1;
sel <= SEL;
end
assign Out = sel ? q0:q1;
Notes: <number>

## Slide 10: Frontend Power Optimization Platform
Application Scenario
Database
RTL Power Analysis
(Cycle by Cycle)
Power Profile Processing
& Optimization Window
Selection
Automated
Power Optimization
Power Optimized RTL
Source RTL
Power Profiling
Formal Verification
Savings
Confirmation

## Slide 11: Power Profiling
Understand the application requirements
Translate to a tangible simulation test case and test bench requirements
Translate simulation window to an optimization constraint for an RTL power optimization solution

## Slide 12: Sample Power Profiles
Scenario - I
Scenario - II
window selection helps
runtime reduction and decide on a correct snapshot for power optimization

## Slide 13: Debugging Power Profiles
Look at power break-ups of the design
  By Hierarchy (Module by Module)
  By components (Memory, Clock Tree, Sequential etc)
Abnormal distributions of power numbers if found, can then be zeroed in on the respective aspect
Component wise transient power break-up also provides details on which modules can gain through sequential clock gating

## Slide 14: Overview of Calypto Solutions : Power Pro
Automatically generate optimized RTL based on sequential analysis
  Use of vectors for ranking power savings of RTL modification
Modified RTL is formally verified and functionally equivalent to original RTL
Output tuned for Synthesis
  Optimizations are complementary and cumulative to downstream tools
Power
Optimized
RTL
Original
RTL
Gate Level
RTL
System
GDSII
SAIF
SDC
Liberty
Industry Standard
Files Formats
RTL
Synthesis
Notes: <number>

## Slide 15: Interactive Sequential Analysis : Power Advisor
Optimized RTL Design
Original RTL Design
PowerPro
Analyzer
Optimizations
Implemented by
Designer
PowerPro
Reports
db
Implementation of automated CG may not be always possible, due to many reasons
Requires human interaction to guide these optimizations
Power Advisor solution addresses this problem by giving the designer various aids to decide, if a perceived RTL modification needs to be implemented
Sequential CG analysis however remains the same, but now is also equipped with an interactive GUI
Notes: <number>

## Slide 16: Interactive Sequential Analysis : Examples
Feedback to designer: Borrow signal from the upstream block for new enable expression
module top(out, in, s, mode, clk);
assign out = (mode | s_p1) ? ff1 : 8’b0;
always @(posedge clk) begin
ff1 <= in;
s_p1<= s;
end
endmodule
RedundantWrite Domain 1
OBS RW: ff1
Count: 8
Area : 160 -> 170
Efficiency: 0 -> 90
Power : 0.258 -> 0.067
Inputs : mode (no_predicted_val : input)
module top(out, in, s, mode_prev, clk);
assign out = (mode | s_p1) ? ff1 : 8’b0;
always @(posedge clk) begin
ff1 <= in;
s_p1<= s;
mode<= mode_prev;
end
endmodule
module top(out, in, s, mode_prev, clk);
assign out = (mode | s_p1) ? ff1 : 8’b0;
always @(posedge clk) begin
if (ff1_en) // PowerPro-CG
ff1 <= in;
s_p1<= s;
mode<= mode_prev;
end
endmodule
Notes: <number>

## Slide 17: Examples ..cntd..
Feedback to designer: Declare ports/signals as mode signals for excluding them to participate in clock-gating conditions
build_design top.v
create_clock –name CLK –period 1 clk
create_mode –name func
create_mode_constraint –mode func \
-module top \
-signal test –value 1’b0
prototype
insert_observability_logic
write_rtl
module top(out, in, s, test, clk);
assign out = (test | s_p1) ? ff1 : 8’b0;
always @(posedge clk) begin
ff1 <= in;
s_p1<= s;
end
endmodule
RedundantWrite Domain 1
OBS RW: ff1
Count: 8
Area : 160 -> 170
Efficiency: 0 -> 90
Power : 0.258 -> 0.067
Inputs : test (no_predicted_val : input)
module top(out, in, s, test, clk);
assign out = (test | s_p1) ? ff1 : 8’b0;
always @(posedge clk) begin
if (ff1_en) // PowerPro-CG
ff1 <= in;
s_p1<= s;
end
endmodule
Notes: <number>

## Slide 18: Examples ..cntd..
Feedback to designer: Identify correct clock for new enable expression to be generated
build_design top.v
create_clock –name CLK –period 1 clk
set_cgic_cell -user gclk_mod \
-calypto calypto_cgic
prototype
insert_observability_logic
write_rtl
module top (out, in, s, gclk_en, clk);
assign out = (s_p1) > ff1 : 8'b0;
always @(posedge clk)
ff1 <= in;
gclk_mod i_gclk(clk, gclk_en, gclk);
always @(posedge gclk)
s_p1 <= s;
end
endmodule
RedundantWrite Domain 1
OBS RW: ff1
Count: 8
Area : 160 -> 170
Efficiency: 0 -> 90
Power : 0.258 -> 0.067
Inputs : s_p1 (clock_domain : gated)
module top (out, in, s, gclk_en, clk);
assign out = (s_p1) > ff1 : 8'b0;
always @(posedge clk)
if (ff1_en) // PowerPro-CG
ff1 <= in;
gclk_mod i_gclk(clk, gclk_en, gclk);
always @(posedge gclk)
s_p1 <= s;
end
endmodule
Notes: <number>

## Slide 19: Results
# | Design | Efficiency Gain | Power Gain*
1 | A | 83.55% -> 88.29% | 10%
2 | B | 67.02% -> 77.53% | 12%
3 | C | 57% -> 94% | 16%
4 | D | 73% -> 80.96% | 5%
5 | E | 84.62% -> 93.36% | 6%
All designs in 45nm
* Power savings expressed as a part of total dynamic power
Notes: <number>

## Slide 20: Sequential Clock Gating Statistics
Total Vs. Sequentially Enabled flops
New Enables Vs. Strengthened Enables
% Sequentially enabled flops
% Strengthened flops
Structural CG coverage of all designs
greater than 98%
Sequential Strengthening:
The single biggest contributor

## Slide 21: Observations
Small percentage of sequentially enabled flops can result in substantial power savings
Most registers are structurally clock gated (esp. on the ESL based RTL)
  Enable strengthening is the single approach for power optimization
Stability based clock gating requires addition of flip flops to feed forward enables
  Has a greater dependence on application scenario
  Vector less approaches not recommended

## Slide 22: Future Directions
With advances in ESL, sequential clock gating and formal verification become extremely crucial
Sequential clock gating at RTL needs to supplement advances in ESL clock gating
Designers need to analyze their design and make trade-offs in terms of application of Observability and Stability based sequential clock gating
Sequential clock gating to rise further to ESL