## Slide 1: 32nm IBM ASIC Design for Test Methodology
Dave Lackey
Distinguished Engineer, EDA
IBM
delacke@us.ibm.com
IBM STG DFT Methodology
June 2010

## Slide 2: Introduction
At the 32nm technology node, IBM has made major changes in its Design for Testability (DFT) architecture and tool flow
  Converted from Level-Sensitive Scan Design (LSSD) to Mux-scan (Edge-based)
  Enabled greater IP sharing (internally and externally) and jointly developed IP with 3rd parties, used across IBM-internal design teams and ASIC/foundry offerings
  Changed it’s method of BIST insertion from the netlist to the Register Transfer Level (RTL)
  Fully Hierarchical DFT synthesis flow
  Simplified design handoffs between the Front-end, DFT, and Back-end flows
IBM has worked within its EDA organization, and with EDA partners, to incorporate these changes

## Slide 3: LSSD and Mux Scan pros and cons
Factors |  | LSSD | Mux-Scan | Comments
IP Scan Test Interoperability | With 3PIP & Joint IP design | - Difficult to share IP | + | IP sharing is impacted by different scan styles.
 | With IBM server IP | - Partitioned Test | + Interfaces for at-speed test. | 
Test quality | Logic DC | + (slight advantage) | - | Assumes same test focus regardless of scan style
 | Macro Test | = | = | ABIST, SerDes, PLL, etc
 | At-speed | = | = | 
Methodology complexity | Timing Risk to DFT (Test Timing) | + Race-free test, Test timing relaxed | - Test timing across process space | Test-unique hold issues can break test – new methodologies needed
 | DFT/Test planning | + Push button | - Domain aware automation needed | Architecturally mitigate domain crossing issues
 | Reliability Test | + Full Pattern Re-use due to race free test | - Scan timing scaling | Scan hold timing closure to extended voltage/temp
Chip / Core Design | Performance | = | = | 
 | Area | - | + | ~1-2% at chip-level
 | Active Power | - | + | ~17% Clock pwr difference

## Slide 4: DFT Tool Flow – Front end Integration in 32nm
Block-Level
Logical/Physical Synthesis
(No DFT)
Handoff to FEP
TLI
Block-Level FEP
Chip-Level FEP
Handoff to PD
}
~70%
PD &
Timing Closure
Methodology through 45nm
Block-Level
Logical/Physical Synthesis
DFT Synthesis
DFT Rule Check
32nm
Synopsys
Cadence
IBM
TLI
“Integration” FEP
TSV, etc
PD &
Timing Closure
TSV, etc
Cadence (BTS, RC)
IBM
Pseudo-latches
Real latches
Cadence (ET)
IBM (CMOS Checks)
Test Timing across process space
Hold margin for reliability conditions
Handoff to FEP
Handoff to PD
Insertion
Verification
Block-Level FEP
- DFT Synthesis
- DFT Rule Check
Faster turns,
fewer handoffs
Synopsys
Cadence
IBM
Cadence RC
IBM

## Slide 5: Total DFT Synthesis Runtime – Comparison of 90k Flop Design
Improvements realized several benefits
Simplified handoff into DFT synthesis
Out-of-Context block and top processing
Fewer steps (no LSSD clocks)
Elimination of netlist-level MBIST processing (details discussed later)

## Slide 6: 32nm ASIC Mux-Scan Architecture Overview
Scan Architecture
  Mux-Scan Flops
  Lockup latches to support domain crossings in scan chains
  Scan/DFT is inserted bottoms up (cores->RLMs->top), fully out-of-context
  OPMISR+ Compression
Dealing with cross-domain capture race issues
  Clock (on/off) control for each domain
  Fencing supported at input to each domain (supports DC, AC and At-speed requirements)
  Two-step ATPG approach for pattern efficiency
    Test all domains at the same time with domain boundaries fenced
    Test all boundaries (unfenced) – grouping unrelated domains in each test
IBM and Cadence worked together to provide fully-automated fencing support in both RTL Compiler (insertion) and Encounter Test  Automated Domain-Aware DFT insertion and ATPG

## Slide 7: Domain-Aware DFT Architecture
Internal/Output Latches
Internal/Output Latches
Internal/Output Latches
Input Latches
Input Latches
Input Latches
Tested during all tests
Tested one domain/group at a time only
SE (normal flops)
SE + fencing (input flops)
test_clk1
tree
tree
test_clk2
sysclkA
sysclkB
sysclkC
Root Clock Macro
TWGDSK
Macro
TWGDSK
Macro
ASST-tested clock
ASST-tested clock
non-ASST clock
sidescan paths
controls
controls
controls

## Slide 8: Leveraging Domain Awareness in DFT Synthesis, ATPG and Timing Analysis
Design
Blocks
Top
DFT Synthesis
Fencing
Clock Control
Test Structure Verification
Domain Aware
Identifies Domain Crossings Fenced/Unfenced
ATPG
1st Experiment:
All domains/fenced Force X for unfenced
Grouped experiments: Test Unfenced/unrelated domains
Experiment for each group
Each from/to domains
Identify fenced vs unfenced
File Format
Time all scan chains
  All domains
  Include extended voltage/temperature
Time data within domains
Time data between 2 domains only if not fully fenced
RTL Compiler
Encounter Test
Einstimer
DC Testing
AC Testing
At-speed Testing

## Slide 9
Scanin
Ccommon
Ccapture
Claunch
S
Basic Scan Hold Timing Requirement:
Claunch + X(CLK->Q) + S > Ccapture + Y(Hold)
With Margin Applied:
Early_Margin * ( Claunch + X(CLK->Q) + S ) > Late_Margin * ( Ccapture + Y(Hold) )
X
Y
Early and Late Margins applied to Scan Chain
  Dynamic Voltage Screen (DVS) and Burn-In
  Low Voltage Stress Test
Early
Path
Late
Path

## Slide 10: Cu32 Methodology Change for Memory BIST/BISR
Prior methodologies inserted BIST/BISR IP at the netlist level
In 32nm ASICs, IP will be introduced at the RTL Level
  Customers can simulate their in-system usage of Array BIST at RTL level
  Customers’ Synthesis and early floorplanning have visibility to all structures
Formal verification and functional ECO processing are simplified
Restrictions to PD and Timing Closure greatly reduced
  No need to preserve IP boundaries for BIST IP recognition by verification and test tools

## Slide 11: 32nm ASIC flow with RTL BIST/BISR IP insertion
RTL Design with BIST IP
Blocks
Top
Optional Manual approach: Design-in BIST/BISR from the start
Synthesis
& DFT
BIST/BISR interconnect checking
Netlists
BIST/BISR
Blocks
Chip Top
BIST IP Block Equivalence Check
BIST IP RTL Library
BIST/BISR Map File
Flatten to PD Hierarchy
Physical Design
Final Netlist
Final Chip
Equivalence
ATPG
Generate Patterns for Memory BIST & Repair Flow
RTL Design pre-BIST IP
Blocks
Top
User’s
Memory ORG
File
BIST IP RTL Library
BIST/BISR Connection Rules
Atrenta
MBIST – Insert IBM BIST/BISR
SpyGlass – Check interconnect

## Slide 12
32nm Memory BIST/BISR Architecture for a sample Chip – User describes this in the Memory ORG File
CLKCNTL
(Keyboard)
FUSECNTL
ECID
Mem
Wrap
BIST
Engine
BIST
Engine
BISTCNTL
BCxx
BIST
Engine
BIST
Engine
BISTCNTL
BIxx
BIST
Engine
BIST
Engine
BISTCNTL
BCxx
FCxx
FCxx
RROUT
Mem
Wrap
Mem
Wrap
Mem
Wrap
Mem
Wrap
Mem
Wrap
Mem
Wrap
Mem
Wrap
Mem
Wrap
Mem
Wrap
Mem
Wrap
Mem
Wrap
BCxx
BIxx
BIxx
BIxx
BIxx
Cxx, Bxx, Fxx
BIxx
Cxx, Bxx
RRIN
SDOUT
SDIN
SYS_MABIST_GO, DONE
RRIN
SDOUT
SDIN
SDOUT
SDIN
4
1
10
4
10
10
4
4
4
4
1
1
4
1
4
1
20
1
20
20
20
RROUT
SYS_POR_GO, DONE
SYS_POR_GO, DONE
SYS_MABIST_GO, DONE
SYS_MABIST_GO, DONE
20
Cxx, Bxx
FUSECNTL
SYS_POR_GO, DONE
Fuse download (FUSECNTL) and Array BIST (BISTCNTL) can be integrated & operated on a partition basis

## Slide 13: Summary
At the 32nm technology node, IBM has made major changes for DFT interoperability, to simplify Tool Flow, and improve Turnaround Time (TAT)
  Converted from Level-Sensitive Scan Design (LSSD) to Mux-scan
  Changed BIST insertion from the Netlist, to the Register Transfer Level (RTL)
  Fully Hierarchical DFT synthesis flow
  Simplified design handoffs between the frontend, DFT, and backend flows
IBM has successfully integrated these changes in its Front-to-Back ASIC flow, by
  Working within its EDA and Methodology organization
  Working with key EDA partners including Cadence, Atrenta, and Synopsys