## Slide 1
Configurable Sub-system Verification Using Property Based Formal Methods
Supriya Bhattacharjee, Bijitendra Mittra
Interra Systems Inc., Bangalore, India
Subir K. Roy
Texas Instruments Inc., Bangalore, India
DAC User Track 2010 Poster Session

## Slide 2: Motivation
SoC typically consists of many sub-systems.
Each subsystem may contain various functional IPs.
Based on the requirement, some functional IPs may be or may not be required in a particular SOC.
Configurable subsystems enable this level of flexibility needed in a platform SOC
Different parameters values determine the subsystem configurations for different applications, enabling re-use of the same set of generic subsystems across many different applications
The main challenge is to verify such parameterized subsystems standalone, for all possible configurations before integration into the SOC

## Slide 3: Configurable Subsystem – An Example
Test
Pin
Mux
Test Secure Ctrl.
Serial
TAM
Serial
TAM
WIR (8 bits)
Decode
CDRs
Test Mode Controller
PBIST Ctrl + Comb
BI Ctrl + BI Mon
Scan Combiner
DFT Ctrl
DFT IO Ctrl
TestCM Ctrl
TestPRCM Ctrl
DFT Sub-system

## Slide 4: What makes the Subsystem configurable?
Configuration and configurability of a subsystem is defined in a configuration file
  IPs/Modules that get instantiated in a subsystem
  Parameter values for each instantiated IP/Module
We use Veriperl (a mix of Verilog & Perl) to develop generators for both RTL and the verification environment
Veriperl reads the configuration file and generates Verilog RTL for the complete subsystem
Based on the parameters in the configuration file, an IP will be instantiated or ignored.
For each instantiated IP, the configuration of that IP is controlled by the parameter values defined in the config file

## Slide 5: Sample Configuration File
Parameter | User Value | Type | Description | Default Value
bi_ctrl_enable |  | boolean | Include the burnin ctrl. 0 = not included, 1 = included | 1
bi_mon_enable |  | boolean | Include the burnin mon. 0 = not included, 1 = included | 1
scm_enable |  | boolean | Include the scan combiner. 0 = not included, 1 = included | 1
tpm_enable |  | boolean | Include the tpm. 0 = not included, 1 = included | 1
bi_mon_cnt | 32 | Integer | No. of user defined burnin monitor mux input | 7
tpm_pins | 32 | integer | Defines the number of tester channels, 32 or 64 | 32
pmt_comb_cnt | 32 | Integer | No. of user defined PMT combiner input | 8
scm_n_cores | 34 | Integer | Defines the no. of cores to combine | 1
scm_n_channels | 8 | Integer | Defines the no of scm channels, 8 or 16 | 8
scm_n_si_pipes | 3 | Integer | Defines the no. of scanin pipe register required per pipeline | 3
scm_n_so_pipes | 3 | Integer | Defines the no. of scanout pipe register required per pipeline | 3

## Slide 6: Configurability of Sub-systems
Test
Pin
Mux
Test Secure Ctrl.
Serial
TAM
BI Ctrl + BI Mon
Scan Combiner
DFT Ctrl
DFT IO Ctrl
TestCM Ctrl
TestPRCM Ctrl
 | Parameter | User Value | Type | Description | Default Value
 | bi_ctrl_enable |  | boolean | Include the burnin ctrl. 0 = not included, 1 = included | 1
 | bi_mon_enable |  | boolean | Include the burnin mon. 0 = not included, 1 = included | 1
 | scm_enable |  | boolean | Include the Scan comb. 0 = not included, 1 = included | 1
 | tpm_enable |  | boolean | Include the TPM. 0 = not included, 1 = included | 1
 | pbist_ctrl_enable | 0 | boolean | Include the PBIST ctrl. 0 = not included, 1 = included | 1
PBIST Ctrl
not included
in RTL
CONFIGURATION FILE

## Slide 7: RTL Generation from Config File
RTL generators are developed based on Veriperl
Based on parameter values defined in the config file, Verilog RTL for the corresponding module is generated by the Veriperl generator
tpm_pins | 64 | integer | Defines the number of tester channels, 32 or 64 | 32
……….
pl: if ($tpm_pmt_comb) (
input $tpm_pins wpi_pmt;
output $tpm_pins wpo_pmt;
output $tpm_pins wpz_pmt;
………..
………..
input 32 wpi_pmt;
input 32 wpo_pmt;
output 32 wpz_pmt;
……….
…………
input 64 wpi_pmt;
input 64 wpo_pmt;
output 64 wpz_pmt;
……….
If ($tpm_pmt_comb == 1) && ($tpm_pins == 32)
If ($tpm_pmt_comb == 1) && ($tpm_pins == 64)
PMT Combiner RTL with different configurations
Veriperl RTL Generator
RTL
RTL

## Slide 8: Formal Property Generation from Config File
For every module in the subsystem, parameterized formal property generators are developed in Veriperl manually
For a given SOC configuration, formal properties are generated based on the parameter values
pl: if($scm_enable == 1) {
vunit dftss_soc_scm
pl: my $msb = $scm_n_channels+1;
………………………
property select_ser_wpi_scan_intest is
always( dft_sel_bi_prpg_scan == 1'b0 ->
bi_ser_wpi_scan_intest ==
ser_wpi_scan_intest[$msb:2]);
assert select_ser_wpi_intest;
………………………
}
vunit dftss_soc_scm (dft_sacra_core)
{
…………………………
property select_ser_wpi_scan_intest is
always (dft_sel_bi_prpg_scan == 1'b0 ->
bi_ser_wpi_scan_intest ==
ser_wpi_scan_intest[9:2]);
assert select_ser_wpi_scan_intest;
………………………
}
Config
File
Veriperl Property Generator
Generated Property File

## Slide 9: The Automated FV Flow
Generated RTL Files
Config
Files
RTL
Generators
Property
Generators
Veriperl
IFV
PASS
Counter Example
Generated
Properties

## Slide 10: FV Connectivity Verification Suite
Besides functional checks for IPs, we have also developed an automated connectivity verification flow to ensure proper integration of IPs within the subsystem
The connectivity information for all the IPs are populated in an Excel spreadsheet
A Perl based script is used to parse the XLS and generate the connectivity property suite
Perl Script
Connectivity
XLS
Connectivity
Property
Suite

## Slide 11: Results
Flow run on a configurable DFT Subsystem (DFTSS) consisting of IPs like, Power Reset and Clock Management modules, Pin Muxing modules, Data & Control registers, Scan Combiner Module, Burn-in module, Memory and Logic BIST controllers, PLLs etc.
For 4 SOCs
  Functional Checks - # of Configurations: 133, # of Properties: 307190
  Connectivity Checks - # of Configurations: 133, # of Properties: 73657
Fig2: Connectivity Checks
Fig1: Functional Checks

## Slide 12: Conclusion
Fully automatic push button formal verification solution to validate configurable subsystems
Automatic generation of Formal properties and environment
Easy operation of flow
New properties can be added very quickly
Exhaustive verification guaranteed by Formal verification technology itself
Configuration file and connectivity XLS creation is manual, time taking and thus error prone
Need to have a RTL generator which reads the configuration files to generate the RTL