## Slide 1: Bug Hunting Methodology using Semi-Formal Verification Techniques
Bijitendra Mittra, Deepanjan Roy
Interra Systems Inc., India
Subir K. Roy
Texas Instruments Inc., India
Lokesh Babu P.
Cadence Design Systems Inc., India
DAC User Track 2010 Poster Session

## Slide 2: Motivation
A case study (on a complex DMA controller) to evaluate semi-formal verification approaches based on a constraint based hybrid formal verification technology
Share the methodology we have developed to verify the DMA Controller around different user specifiable and controllable hybrid approaches integrated into Incisive Enterprise Verifier (IEV) from Cadence
To showcase the power of user-controllable Semi-formal verification approaches to find extreme corner case bugs for large, complex and data oriented designs

## Slide 3: Introduction to Semi-Formal Technology
Semi-Formal Technology
  Best of both worlds – Simulation & Formal
  Generate a number of simulation traces
  Invoke formal engine many times in the middle of a simulation based verification run, whenever a particular state or a condition is reached
  Two approaches : Constraint Based and Trace Based
Constraint Based Semi-Formal Technology
  Provide behavioral constraints in form of assumptions (SVA/PSL)
  Constraint solver generates multiple random traces honoring the constraints
  Formal Engine is invoked on reaching a pre-specified condition called the Search Point in the form of a property being triggered or a cover statement being satisfied.
DUT
Constraints
Simulation
Traces

## Slide 4: Introduction to the Data Mover IP
IVA-HD iCONT Data Mover (DM) – A Complex DMA Controller
  Data transfer between ICONT internal memories (ITCM & DTCM), External Shared L2 memory and VDMA transversal ports
  OCP transactions supported on Configuration, SL2 and VDMA ports
  4 Logical channel DMA (1 queue per Phy Channel) – concurrent access
  Hardware/Software controlled queuing of requests per Phy channel
  In-order servicing of pending requests – 2D Chronology Matrix
Data Mover
Cadence OCP
AIP
LCH0
.
.
.
.
.
.
.
LCH3
Chronology Matrix
Physical
CH1
Physical
CH2
SL2 Arbiter
DTCM
Arbiter
Config
Port
I
T
C
M
D
T
C
M
SL2
V
D
M
A
SRC
SRC
DST
DST
Pointer Logic
Cadence OCP
AIP
Cadence OCP
AIP
Fig2: Verification environment for the Data Mover
ITCM (W)
DM
DTCM
(R/W)
vDMA
Transversal (W)
SL2 (R/W)
OCP Configuration
Port
Fig1: DM Data flow diagram

## Slide 5: Prior Verification Efforts:
Functionality verified primarily using simulation; OCP compliance checking done with pure Formal Verification; Signed off by both Simulation and Formal verification
DUT had a corner case bug, caught neither by simulation nor by pure FV (due to properties being reported as “explored” in IFV). Caught at the emulation stage.
Unusual OCP behavior (loss of functional data due to over-writing of internal data FIFO) observed during SL2 to VDMA data transfers.
OCP Retraction properties at SL2 and VDMA interfaces should have failed.
SL2
VDMA
RD
WR1
Data #1
Data #2
Data #3
Data #4
WR2
WR3
Data #5
Data Over Write
Assumptions:
SL2 will get access at every alternate cycle
VDMA will receive at least one data in six cycles
4 Deep FIFO
WR4
WR5

## Slide 6: Semi-Formal Verification of DM using IEV
Enabled OCP Retraction properties for SL2 interface (MCmd, MAddr, MData) and VDMA interface (MCmd & MData)
First Step: Random simulation with formal fork-off if a property is triggered
  Prepared two separate environments - one with normal constraints and another with additional constraints leading to convergence of properties during pure IFV formal runs.
  No failures reported by IEV for the 1st environment with normal constraints.
  All 5 properties reported as fail by IEV for second environment --> bug easily reached iff IEV is steered along a proper direction.
Established and followed a two-step methodology for effective usage of IEV
  SimOnly: ‘N’ nos. of random simulation runs for proper “seed” selection
    100 SimOnly runs for each search-point (50 with Scout & 50 with Spy solver)
    Total Simulation Runtime of 8 hrs. for each set of 100 runs
  Semi-Formal: Top ‘k’ seeds are used with different formal invoking methods to disprove each property
    Top 5 seeds selected for each search-point

## Slide 7: IEV Based Bug Hunting Methodology
Verification
Complete
Random
Simulation
“N” Iterations
Seed Selection
Top K seeds (K<N)
Run IEV
FAIL?
Change
Semi-formal Approach
Coverage
Achieved?
NO
YES
YES
NO
Debug
FAIL
IEV Search Mechanisms
  Trigger Based
  Interval Based
  FSM Based
  Cover Based
  Cover with Replay

## Slide 8: Analysis of Different Formal Fork-off Methods
Trigger Based Formal Fork-off
  For explored properties, search up to 5000 cycles could not be completed
  SL2_MCmd and SL2_MAddress properties failed
5000
10 min
Fork-off at: Trigger of Property
Search Depth = 5000
Formal Effort = 10 min
Formal Engine: Bow3
Interval Based Search
  Search of 5000 cycles could be completed; Runtime decreased to 24 hrs. per property
  VDMA_MCmd property failed
5000
20 min
Fork-off at: Specified Time Interval
Search Depth = 5000
Time Interval = 150 cycles
Formal Effort = 20 min
Formal Engine: Bow3
150
cycles
150
150
150
150

## Slide 9: Analysis of Different Formal Fork-off Methods contd.
FSM State Based Search
  All automatic FSM checks [Reachability AFAs] with max pass depth of 14 (reachable)
  Both the SL2_MData and VDMA_MData properties were explored
Cover Property Based Search
  Cover statement written with the help of debug info from previously failed properties
  Got failures for all three properties already falsified before.
  SL2_MData & VDMA_MData still explored
Cover With Replay Method
  Got a failure for SL2_MData
  More covers based on debug info from SL2_MData failure written to converge VDMA_MData
  Observed all 5 failures in a single trace

## Slide 10: Results
Retraction Property | Semi-Formal Search Approach | # Top Seeds | Semi Formal Run (Hrs) | Formal Effort (Min) | Simulation Depth | Formal Depth
SL2_MCmd | Trigger Based Cover Based | 5 | 48 | 10 | 232, 5288 184 | 31, 31 30
SL2_MAddr | Trigger Based Cover Based | 5 | 48 | 10 | 760, 612, 262, 374 184 | 31, 31, 31, 31 32
SL2_MData | Cover Based [with additional covers] | 5 | 24 | 15 | 524 | 32
VDMA_MCmd | Interval Based Cover Based | 5 | 24 | 20 | 932 184 | 32 32
VDMA_MData | Cover with Replay Method | 5 | 48 | 10 | 524 | 28

## Slide 11: Future Scope of Work
Tool related usability issues to be taken care of by the vendor
Extend existing methodology as well as develop newer methodologies to handle complex, large data dominant multimedia IPs
Leverage the power of Semi-Formal for Processor Verification
Develop flow to validate environmental constraints around IEV Constraint solver
Come up with Bug Hunting recipes for new IPs

## Slide 12: Conclusion
Eliminates capacity issues faced with IFV incorporating the pure formal approach
Can handle data dominant, sequentially deep and complex IPs
Bugs sitting deep in the design can be uncovered
Bug Hunting becomes easy if tool is driven in the proper direction
In-depth knowledge of design is necessary to write useful covers. Often, designer’s insight is required
When to stop verification??
  No explicit notion of completion of verification effort in absence of bugs. Separate coverage analysis needs to be resorted towards making a judicious decision
No available documentation on recipes to be followed for different types of designs