## Slide 1
A Smart Debugging Strategy for Billion-Gate SOCs
Namdo Kim, Junhyuk Park, Byeong Min, K.M. Choi, *Kyuho Shim, *Seiyang Yang, Design Technology Team, System LSI division, Samsung electronics Co., Ltd. *Dept. of Computer Eng., Pusan National University, Korea nd.kim@samsung.com

## Slide 2
<number>/10
- 100% visibility is essential for debugging
- However, 100% visibility in HDL simulation comes with very high cost. Simulation time slows down significantly
Trade-off
High Visibility
Fast
Simulation
Simulation performance vs. visibility
The problem (1/2)

## Slide 3
<number>/10
Full signal dump requires longer simulation time, at least 2~4x
It’s hard to handle large dump data with commercial waveform viewers
Slow simulation time
Large dump data
“Partial signal dump” often fails to dump data with right signals necessary for debugging, and results in additional simulation runs
Repetitive simulation
Simulation run might stop due to lack of HDD capacity
Lack of HDD capacity
Full signal dump is impossible !!
Repetitive simulation runs with partial signal dump is painful !!
Due to very long simulation time & limited HDD capacity
Due to long simulation & no guarantee that target dump area holds appropriate signals
Obstacles for simulation with billion-gate SOC
The problem (2/2)

## Slide 4
<number>/10
- On-demand full signal visibility with only a few re-simulation
- Fast turnaround time between simulation process and debugging process
- Minimal usage of storage space for full signal visibility
Smarter debugging strategy for billion-gate SOCs
Project objectives

## Slide 5
<number>/10
Signal re-construction [Mar98]
and visibility enhancement [Hsu06]
- During a simulation run, dump essential signals (all primary inputs and outputs of storage elements) only
- Interpolate the missing non-essential signals, i.e. outputs of combinational logics, from the essential signals by re-construction
Idea
- There are too many essential signals, so the simulation is still slowed down considerably
Problem
Previous solution

## Slide 6
<number>/10
SSi-1: Two-pass Simulation for Debugging Acceleration
- Simulation time slightly increases by our unique checkpoint technology
Checkpoint Simulation (1st Pass)
cp
cp
cp
cp
cp
cp
cp
cp
cp
cp
cp
* cp : checkpoint
- No need for re-simulation from simulation time 0
- Once re-simulation of any single slice is done, actual debugging process can start
Slice Re-Simulation (2nd Pass)
cp
cp
cp
cp
cp
cp
cp
cp
cp
cp
cp
Time saved
Smarter Simulation with SSi-1 is two-pass simulation based on unique design state checkpoint and re-start
Our Solution (1/3)
restart

## Slide 7
<number>/10
Traditional simulation with full dump
t_f0
Traditional simulation with multiple partial dump
Simulation time = t_f0
Simulation time = t_p0 + t_p1 + … + t_pN
New simulation with SSi-1
Checkpoint simulation
(1st Pass: t_s1)
Slice Re-simulation with dump
(2nd Pass: t_s2)
Simulation time = t_s1 + t_s2
Simulation faster than traditional full or partial dump !!
Our Solution (2/3)
t_p0
t_p1
t_p2
t_pN
...
t_s2
t_s1
restore
Skip ( time saving )
to any checkpoint

## Slide 8
<number>/10
Traditional (simulation state) checkpoint and re-start vs. SSi-1
 | Traditional checkpoint and re-start | SSi-1
Checkpoint | Simulation state (Simulator's entire binary image) | Design state (DUT's input and internal register/memory values)
File size of one checkpoint | Very large, Giga bytes for very large designs | Very small, Mega bytes even for very large designs
# of checkpoints made | Small number | No limit
Simulation time for re-start | Still long | Very short
Foreign module support through PLI/VPI | Manual only | 100% automatic
* Traditional checkpoint : Built-in feature of most commercial HDL simulators. Traditional checkpoint command lets users save simulator’s entire executable binary image to hard disc during the simulation, and reload it later for re-simulation
Our Solution (3/3)

## Slide 9
<number>/10
Target: RTL & Gate-level simulation
Simulator: NC-Verilog
 |  | Design 1 (gate-level) | Design 2 (gate-level) | Design 3 (mixed) | Design 4 (RTL)
# of total states (reg or UDP) |  | 270M | 30M | 62K | 20k
Simulation time | No Dump Simulation Execution Time | 39,644 | 12,329 | 10,952 | 3,676
 |  | Ratio [1.00] | [1.00] | [1.00] | [1.00]
 | Full Dump Simulation Execution Time | 68,477 | 26,317 | 28,393 | 10,984
 |  | Ratio [1.73] | [2.13] | [2.59] | [2.99]
 | Checkpoint Simulation Execution Time | 50,481 | 14,760 | 16,312 | 6,626
 |  | Ratio [1.27] | [1.20] | [1.49] | [1.80]
 | Simulation time reduction rate (Full dump vs. checkpoint) | 26% | 44% | 43% | 40%
Hard disk space | Full Dump Simulation Disk Usage | 165 | 21 | 46 | 29
 |  | Ratio [43.19] | [53.19] | [20.75] | [14.58]
 | Checkpoint Simulation Disk Usage | 3.82 | 0.40 | 2.21 | 2.02
 |  | Ratio [1.00] | [1.00] | [1.00] | [1.00]
 | Hard disk space reduction rate (Full dump vs. checkpoint) | 98% | 98% | 95% | 93%
Experimental result
Time (sec) / Hard disk space (GB)

## Slide 10
<number>/10
- Fast checkpoint simulation (1st pass)
- (On-demand based) slice re-simulation (2nd pass)
Achieving reasonable simulation performance with full visibility for billion-gate SOC simulation
- Eliminating repeated, long re-simulation for obtaining signal visibility
Achieving fast debugging TAT
- During the simulation
- After the simulation for back-up purpose
Saving hard disk space for dump data storage
Conclusion