## Slide 1
Utilizing Assertion Synthesis to Achieve an Automated Assertion-Based Verification Methodology for Complex Graphics Chip Designs
Prosenjit Chatterjee Saad Godil Peter Nelson pchatterjee,sgodil,pnelson@nvidia.com
Nvidia Corporation
Yuan Lu yuan@nextopsoftware.com
NextOp Software Inc.
Notes: <number>

## Slide 2: Manual Assertion-Based Verification (ABV)
Simulation
  Assertions: catch bugs -> localizing the bugs
  Coverage: guides verification progress and closure
Emulation
  Assertions: improve debug capability
Formal verification
  Assertions: property target for the tool to prove
  Coverage: property targets for the tool to cover
Notes: <number>

## Slide 3: Issues In Existing ABV Methodology
Not enough assertions:
  Writing high quality assertions and coverage properties is time consuming
  Required assertion density is hard to achieve
    One assertion per 10/100 lines of code
Benefits of more assertions:
  More assertions = Better propagation of bugs
    Hitting a bug in random is useless if it isn’t reported
  Missing coverage holes = missed bugs
    Constraint Random Testing relies on good coverage
    Hard to come up with all possible corner cases manually
Notes: <number>

## Slide 4: BugScope: Assertion Synthesis Tool
Generate properties representing design functionality
  Takes design and tests as input and generates properties
  A property is an assertion/checker if it should be always true
  Otherwise, it reveals a coverage hole that need to be targeted by writing additional tests.
Intuition: synthesized assertions reveal verification quality
New idea: synthesized assertions jump start assertion based verification
Notes: <number>

## Slide 5: Assertion Synthesis Flow For GPU
BugScope is part of the block level flow:
  Initial test suit drives BugScope properties
  Synthesized coverage properties drive extension of test suit
  Extended test suit drives creation of more BugScope properties
Synthesized properties drive Full-chip, Emulation and formal Verif flows
GPU
Block
Notes: <number>

## Slide 6: Improved ABV Methodology
constraints
FVE
B
assertions
A
checker
direct /
random
tests
BVE
direct
tests
A
B
C
checker
random
tests
testbench
chip verification environment
assertion
synthesis
assertion
synthesis
direct /
random
tests
BVE
B
checker
Notes: <number>

## Slide 7: BugScope Property Classification: Sample Statistics
Module Name | RTL Lines | Total Properties | Good Assertions | Good Coverage | Uninteresting | Review Time (hr)
ctrl | 22922 | 374 | 221 59% | 41 11% | 107 29% | ~ 5
queue | 3073 | 109 | 61 56% | 29 27% | 19 17% | ~ 0.75
entry | 4327 | 42 | 37 88% | 4 12% | 0 0% | ~ 0.5
glue | 38672 | 145 | 94 65% | 28 19% | 23 16% | ~ 2.75
77% properties are useful
  Either assertion or coverage property

## Slide 8: Bug Scope Coverage Properties: Sample Statistics
Module Name | Cover Properties Found | Coverage Holes in Full Regression
ctrl | 41 | 37
queue | 29 | 9
entry | 4 | 1
glue | 28 | 16
Cover properties were found by running ~1500 Tests (~ 38 hours)
These cover properties were then run against the full regression of over 100K Tests (1 week long) to find the coverage holes

## Slide 9: BugScope Property Assertions: Sample Statistics
Module Name | RTL lines | Manual Assertions | Assertions Reproduced | Total Synthesized Assertions | Assertions/ RTL ratio
ctrl | 22922 | 46 | 22 | 219 | 1%
queue | 3073 | 4 | 2 | 61 | 2%
entry | 4327 | 3 | 0 | 37 | 1%
glue | 38672 | 220 | 122 | 94 | 1%
Synthesized assertions reproduced >50% manual assertions
  Added a lot more new assertions and replaced some with high quality ones

## Slide 10: Example Synthesized Assertions
Cover Properties | Comment
h1_su_valid & hX_su_valid, where X=6, 8, …, 16 | Certain sequence of SU doesn’t happen in simulation
sum(hX_valid_spY) >40, where X=2..7 and Y=0..7 | Burstness of hX_valid_spY in tests is not enough
defer_reason_prt_full & defer_vld | Need to see FULL and VLD together
Assertions | 
sum(portX_dst_bitmap) <= 1, where X=0,1,3,5 | Odd dst_bitmap is mutual exclusive
onehot0(valid_sp_sel) | sp_sel can only select one at a time
opcode == @opcode ¦-> opcode != 3’h3 | Opcode 3 is not sticky
replace[rptr] ¦-> (age0¦age1¦age2¦age3) & 4’h8 != 4’h8 | Replace can only happens when MSB is not aged
Notes: <number>

## Slide 11: Reuse Across Formal Verification
Benefits of Synthesized Properties
  Synthesized Assertions include much smaller cone of logic
    Much easier to converge than human written assertions
    BugScope assertions once proven, can be used as lemmas to prove other assertions.
      BugScope assertions a->b, b->c, once proven can be assumed to be true and in turn help proving a more complex assertion a-->c.
      Model checkers do take advantage of lemmas (either user guided or auto inferred).
  Synthesized Cover properties help to debug constraints
    Formal tool must hit these coverage holes, if it can’t then the block is over constrained
Key idea: Instant benefit from both synthesized assertions and coverage properties
Notes: <number>

## Slide 12: Formal Verification Using Synthesized Properties: Sample Statistics
A parameterized FIFO with sophisticated credit control mechanism
  ~10K lines RTL
BugScope generates 83 properties
  38 are assertions and 45 are coverage properties
Used semi-formal tool to prove the assertions while covering the cover properties
  21 assertions are proven within 5 hours
  24 cover properties are covered within 48 hours
  The end-to-end checker doesn’t converge
A bug is found while the formal tool is patching the cover properties
Notes: <number>

## Slide 13: Limitations in the Flow
BugScope requires a significant amount of disk space
  This limits the number of modules and the length of the tests
BugScope cannot synthesize properties across module boundaries (including child modules)
  We are limited to selecting only those modules that contain significant portions of logic and cannot apply this flow to highly modular code where the logic is spread across many different module instances

## Slide 14: Conclusion
It is key to automate assertion based verification to meet tight schedule
  Synthesized Assertions take less time than manual assertions
Assertion synthesis provides a low hurdle for adopting ABV
  Synthesized assertions are objective with good density
ABV benefits multiple flows:
  Block level
  Full Chip
  Emulation
  Formal Verif
Notes: Bullets points on assertion benefits.
<number>