## Slide 1: Poster Structure
<number>
Slide 1
Slide 2
Slide 3
Slide 4
24 X 18
24 X 18
12 X 18
12 X 18

## Slide 2
How
Challenges
<number>
ECO
How
When
Pre-Mask Netlist
Post-Mask Netlist
Conformal ECO
Automated Pre and Post-Silicon Functional ECO Flow
Ganesh Prabhu C (ganesh.prabhu@st.com), Bhanu Prakash (bhanu.prakash@st.com)
STMicroelectronics. Home Entertainment Division, India
Problems seen in default Conformal ECO flow
Buggy Netlist
Bugfixed Netlist
ECOed Netlist
Complex to do ECO across boundaries
Iterative and time consuming
Difficult to locate the bug
Non-ECOable corner cases seen due to boundary optimizations
An unplanned fix which have to be absorbed in the design without repeating the complete flow
Manually
Functional Bug free design
Minor functional Enhancement to capture market
Why

## Slide 3
100
High
50
Med
0
Low
Manual ECO
Default Conformal ECO Flow
Enhanced ST ECO Flow
Design (%) Knowledge Dependency
Seamless across stages (Complexity)
Timelines (Days)
Surety (%)
Limitations
ECO are always not smarter as manual ECO
ECOed new flops will not be in scan chain
Enhanced STMicroelectronics ECO Flow
Conformal ECO
Flattened Buggy Netlist
Flattened
Bug-fixed Netlist
Flat ECOed Netlist
Future Enhancements
Replacing encounter with RC Physical to make it a cost-effective solution
Power aware ECO
Recreating hierarchy in ECOed netlist
Hierarchical Buggy Netlist
Using def compare
feature of SOC encounter
Hierarchical ECOed Netlist
Conformal ECO
SOC Encounter

## Slide 4
Conformal ECO
Default Conformal ECO Flow
Conformal LEC
Identify modules for ECO
Create Change file for each ECO module
ECOed Hierarchical Netlist
Bug fixed frontend netlist
Buggy Post / Pre
Mask netlist
In the default flow the buggy netlist is compared with the bug fixed netlist.
Conformal ECO identifies the difference between these netlists and the logic difference is applied over the buggy netlist to make the buggy netlist equivalent with the bug fixed netlist making it bug free.
The major problem seen in the flow is
Works only module by module
ECO in boundary optimized cones are not possible on all cases.
ECO in backend netlist are mostly impossible due to extra hierarchical module ports of high bufferization.
Approximately 50% success rate
Logic pull across hierarchy
Bug fix in enable logic, has cloned Clock Gating cells across hierarchy
As the backend netlist has extra ports, hierarchical ECOs are not possible in majority of cases.
Hierarchical constraints has to be generated for each ECO module before doing ECO
The above practical design scenarios proves the default hierarchical flow is not applicable in all cases.
Its possible only if the tool can create the difference file(patch logic) considering the boundary optimizations happened across the design.
D
Q
D
Q
Notes: <number>

## Slide 5
Conformal ECO
Post-Mask ECO
SOC Encounter
Buggy Post / Pre
Mask netlist
Flatten both netlists
Create Change file
Spare cells
Sparecell mapped patch using RTL Compiler
ECOed Flat Netlist
ECOed Hierarchical Netlist
Floorplan def
Bug fixed frontend netlist
Enhanced STMicroelectronics ECO Flow
Aim:
An automatic ECO solution that can handle all ECO cases even across boundaries
The ECOed netlist should be hierarchical.
100 % success in all cases
ST’s innovation in methodology
The design is flattened so that the boundary optimizations are not seen while doing ECO.
The hierarchy in ECOed netlist is recreated using defcompare feature of SOC encounter
Step 1: Doing ECO
Design is flattened.
All the differences for the tool are seen within a single module
ECO is done using conformal ECO
As the design is flattened before doing ECO, the output ECOed netlist is also flat
Conformal ECO
D
Q
SOC Encounter
D
Q
defCompare
D
Q
D
Q
D
Q
ECOed Hierarchical Netlist
Buggy Hierarchical Netlist
ECOed Flat Netlist
Buggy Flat Netlist
Bug fixed Flat Netlist
Step 2: Re-Creating Hierarchy in ECOed Netlist
A dummy def is created for the flat ECOed Netlist and Buggy hierarchical netlist
Hierarchy of ECOed netlist is recreated using Encounter’s defCompare feature
Design is flattened and no hierarchical boundaries are seen
Dummy def of Buggy hierarchical netlist
Dummy def of Flat ECOed netlist