## Slide 1: Systematic Architecture Exploration Through High-Level Synthesis
Raj S. Mitra *, Praveen K. Tiwari ‡, Mahesh Mehendale *
(Contact email: rsm@ti.com)
* Texas Instruments
‡ Interra Systems

## Slide 2: Architecture Exploration
Objective: To define System / Sub-system / IP Architecture
  Meeting performance goals – latencies, throughput
  Optimizing Area / Power
  Task Partitioning between software and hardware
This involves tradeoffs
  Memory (height/width, ports), mux size, bus width, resource (area, latencies), resource pipelining, data pipelining, …
  These are inter-related, changing one affects another
    E.g. Combining two related functions may reduce the combined area, but increases latency, which increases number of cycles
    Parallel processing reduces latency, but increases parallel memory accesses
  Hence the process is very iterative
    Take feedback from software and IP teams
    Experiment with different options and parameters
    Ideally – Implement prototypes and validate the metrics

## Slide 3: Architecture Exploration – State of Affairs
PPA (Performance / Power / Area) is more influenced by architectural decisions, than by implementation decisions
  The scope of design improvements get severely restricted by the architectural decisions already taken
  Difficult to carry out architectural explorations at RTL, since the code is at a very low level and not very flexible to changes
However, today most architectural decisions are taken based on spreadsheet calculations and traffic models
  The data in these calculations are based on architects’ intuition
  These calculations are often inaccurate due to gross aggregations
    Do not capture the finer details of component interactions
    Incapable of factoring in backend (Place & Route) considerations
  The process of determining the optimal architecture is highly unstructured, iterative, and largely based on intuition
Hence – we need a methodology to systematically explore different architectures of a module, based on accurate data
Notes: <number>
<footer>
<header>

## Slide 4: High Level Synthesis (HLS) – Scope
HLS is typically thought of as a synthesis tool with the benefits of flexibility and scalability
  Sarkar et al [IEEE Design & Test, July 2009] showed that significant gaps exist in adopting HLS as a purely implementation tool
  The high level of modeling abstraction often prevents fine user control over micro-architectural decisions on the implementation
However, this does not mean that HLS has no benefit
  The high level of abstraction can be used to explore and measure the effects of architectural decisions
Hence, the usage of HLS can be considered separately:
  For architecture exploration – this is the topic of this paper
  For implementation – this was discussed in detail in [Sarkar et al, 2009]
  These two usages can be separated – use HLS to explore architectures, but subsequently implement by manually coding RTL
Notes: <number>
<footer>
<header>

## Slide 5: Design Phases
Efficient Silicon
Synthesizable Model, Area Upper Bound, Functional tests
Functional/Executable Model, Performance/Latency targets
Paper Spec
Macro-Arch Definition
Micro-Arch Definition
Functionality, Performance Definition
PPA Optimization, Full Verification
Func C
Manual RTL
HLS C
Traditional RTL flow
Traditional HLS flow
Optional HLS flow
Implementation
Architecture Exploration
Algorithm Exploration

## Slide 6: Using HLS for Architecture Exploration
Currently, modeling for Architecture Exploration is typically restricted to creating non-synthesizable C++ models, to:
  Serve as a golden reference
  Model traffic patterns
Our proposal (in this paper) is to:
  Use HLS models to get accurate data on the PPA, thereby influencing the architecture to be selected
    We define a methodology to be followed, and enumerate lessons learnt from our experience with Architecture Exploration on a new generation of Video Accelerator
  However, we de-link the Architecture Exploration phase from the Implementation phase – the same models may or may not be used by both phases
    This provides the benefits of HLS for Architecture Exploration, while not succumbing to the limitations of HLS
Notes: <number>
<footer>
<header>

## Slide 7: Proposed Flow for Architecture Exploration with HLS
Draft initial Spec for
Macro-Architecture, with PPA targets for each IP component
Hardware Implementation
& Software
Constraints
Create HLS models for the component IPs
Run HLS to get actual PPA numbers
Confident about optimal result from HLS?
Refine HLS model
Architecture goals met?
Refine architecture or refine PPA targets for the IP components
N
Y
N
P&R Problems?
Synthesize RTL to gates, and run P&R, to early detect major bottlenecks
Y
Handoff models to software team (for virtual prototyping), to verification team (to act as a golden reference), and to design team (for final implementation).
[Optional] Optimize the same models and generate RTL through HLS
N
Y

## Slide 8: Results
Explored different architectures of a video accelerator module
  Primarily data-path modules (e.g. video encoder), which are ideally suited for application of HLS tools
  Quick exploration – each “model creation to validation” turnaround time is about a week
    Time is smaller (2 days) when only incremental changes are made – exploring “what if” scenarios and their impact on PPA
    Hence, about 5 architectures explored in the span of 2 months, leading to significant project impact

## Slide 9: Process
PPA of HLS is not expected to be as good as manual
  This was a lesson learnt from [Sarkar et al]
  Decision to use HLS only for exploration, not for implementation
  However, inaccurate PPA data would lead us on exploration of a bad architecture. Hence, choice of a good tool was still essential
    Selected the HLS tool that provided the best comparative results with existing manual RTL
    Ease of use of tool also a major factor in tool selection – need to be able to specify micro-architecture details (user hints)
    Tool runtime also critical ~ 5-15 minutes on each module
PPA largely depends on quality of HLS model
  Hence, several iterations needed for creating / refining a model
Architectures | Initial Area | Final Area | % Improvement
Arch-1 | 50k | 34.1k | 31%
Arch-2 | 25k | 14.7k | 42%
Arch-3 | 100k | 53.8k | 46%
Arch-4 | 80k | 62.7k | 22%
Arch-5 | 144k | 80.8k | 44%
  These are minor model adjustments – typically takes a day to iterate once

## Slide 10: Process (contd)
When to stop model refinements and try a different architecture?
  Errors in the process – HLS inefficiencies create errors in the PPA estimates – are corrected partially by model refinements
  Decision depends on target set by architect – has to be realistic
  During the process, efficient coding styles were evolved, which reduced the number of model refinement iterations
Although HLS was not used for final silicon, one pass of Logic synthesis and P&R was run
  To detect the presence of major choke points - large muxes, cross-bars
  This prevents late surprises
Model handoffs
  Same model used as golden reference for verification, sequential equivalence checking (formal), and virtual prototyping
  Hence, adhere to coding styles for these users

## Slide 11: Typical Model Refinements
Optimize functional model
  E.g. Use optimal bit-widths for local storage
  E.g. Do not clip already clipped variables
  E.g. Change “if-else-if” to “switch”, if priority is not needed
  Such information is engrained in the semantics of the model, the tool cannot do such optimizations
Modify computations
  E.g. Change average function from “(a+b+1)>>1” to “(2a+1)+(2b+1)>>2”, and then to “((a<<1)|0x1 + (b<<1)|0x1)>>2”
    This reduces number of adders, but increases width of adder
    Will help if the function is in the critical path
Moving Mux before operations
  Will reduce resources, but increase Mux – tradeoff

## Slide 12: Typical Model Refinements (contd)
Move iteration (on array elements of input) from DUT to TB, by repeated calls to DUT
  This eliminates extra logic in DUT
Common Sub Expression (CSE) elimination
  Sometimes, doing this explicitly in model, instead of relying on HLS tool to do it, gives a better result
Reuse computations where possible by storing values from previous iteration
  Tradeoff between registers and computation
  This may enable further changes and optimization (e.g. reduce array sizes) – since one level of computation is decreasing
  Note: This changes the structure of the algorithm (code readability decreases)
Tool dependent
  Follow tool-friendly coding style – e.g. do not use globals
  Experiment with different tool options

## Slide 13: Conclusion
HLS provides valuable and near-accurate data to influence architectural decisions
  Enables exploration of a large variety of architectures in a short time
  Does not compromise silicon quality, since it is not necessary to use HLS for implementation also
However, use this data with judgment and discretion
  Model refinement may change the data – know what changes to make for getting accurate data
    Most of these refinements are what would be done for a typical manual RTL also, except that these can be done much quicker for HLS models
  Decide on how much effort to put in for model refinement
    HLS is used as a vehicle for exploration, but architect still needs to make judgments on which path to pursue and what is the target (entitlement) to be achieved
  Use the right HLS tools – for PPA, runtime, ease of use