## Slide 1: Developing synthezisable IP from TLM 2.0 descriptions A TDIP methodology case study
Christian Sauer & Felice Balarin
Cadence Design Systems
{sauerc | felice}@cadence.com
DAC User Track, Anaheim, June 2010

## Slide 2: System design challenge
Many models and analysis environments
  For algorithm developers, for SW developers, For system architects, for HW developers, …
  Takes a lot of time and effort to develop and maintain
Hopes for unification
  High-level synthesis enables common language (C/C++/SytemC)
  SystemC TLM standards enable interoperable (virtual) platform
But, there is an abstraction gap between virtual platform models and synthesizable SystemC needed for high quality results
Our approach
  Proposing a methodology to bridge the gap: TLM-driven design IPs
  Presenting a case study showing costs and productivity gains

## Slide 3: Outline
TDIP methodology
Case study
  DMA controller
  Model refinement
  Results
Lessons learned

## Slide 4: A TLM driven D&V methodology
Levels of abstraction
  To serve for algoritm, HW, SW development ...
Verification tasks for each level
  Every issue verified at the highest level at which it is exposed
Refinement steps between levels
  Manual or automatic
Supported by tools and IP
  Leveraging existing verification methodologies
  Leveraging HLS technology

## Slide 5: TDIP: Levels of abstraction
Computation TDIP
Interface
Algorithmic – for algorithm development
  Single-threaded C/C++/SystemC
Architectural – for system architecture and SW development
  Registers and basic process defined
  No protocol details
  Similar to SystemC TLM 2.0 LT
Micro-architectural – for HW devel and system architecture
  Protocol-specific transaction-level interfaces
  Data transfers and buffering exposed
  Similar to SystemC TLM 2.0 AT
RTL
  Created by C-to-Silicon using communication TLM-design-IP (TDIP)
Algorithm
TLM 2.0 blocking
To CtoS
To virtual platform
TLM Protocol-specific
Communication TDIP
Reusable for multiple computation cores
Protocol specific
TLM  signals
(synthesizable SC)
Protocol specific Signals
Interface

## Slide 6: Methodology case study – a TLM 2.o DMA
cpu
M #1
DMA
TLM 2.0 b_transport( id, delay)
Slave interface cfg writes (cmd), status reads
Block transfers, i.e. burst reads and writes
‚done‘
M #2
Inter connect
AMBA 2TLM
TLM2AMBA
TLM 2.0 virtual platform
-- uses AMBA-PV
-- deploys TLM 2.o IP
Implement the TLM 2.0 IP
-- refine for higl-level synthesis
-- maintain sim env for verification
test bench
TLM DUT
Refinement step 1
functional correct & transaction-precise

## Slide 7: Step 2 – Interface refinement
cpu
M #1
TLM 2.0 b_transport( id, delay)
Slave interface cfg writes (cmd), status reads
Block transfers, i.e. burst reads and writes
‚done‘
M #2
Inter connect
AMBA 2TLM
TLM2AMBA
DMA
test bench
TLM DUT

## Slide 8: Step 2 – Interface refinement
cpu
M #1
M #2
Inter connect
AMBA 2TLM
TLM2AMBA
T2 - T1GP
T1GP - T2
test bench
TLM DUT
Model has: TLM 2.0 IFs optimized for simulation speed
Synthesis needs: Pin-level IFs and IO protocol (timing)
Refinement step 2a
Protocol-agnostic TLM If (TLM1GP)
- simple_target_socket<name, BUSWIDTH, tlm_base_protocol_types> tlm_s;
- simple_initiator_socket<name, BUSWIDTH, tlm_base_protocol_types> tlm_m;
- virtual void b_transport( tlm_generic_payload& , sc_time& );
- virtual bool get_direct_mem_ptr( tlm_generic_payload& , tlm_dmi& );
- virtual unsigned int transport_dbg(tlm_generic_payload& );
+ sc_export < tlm1_gp_if > tlm_s;
+ sc_port < tlm1_gp_if > tlm_m;
+ virtual tlm_generic_payload_t transport( const tlm_generic_payload_t&);
+ virtual void reset_transport();
b1
b2
Refinement step 2b
Protocol-specifc TLM If (TLM1AXI)
M
S
m1
s2
b5
b4
b6
b3
Refinement step 2c
Protocol-specific transactors (SIGAXI)
S
M
s1
m2
DMA
syn-top

## Slide 9: Step 3 – Adding Clocks and resets
cpu
M #1
M #2
Inter connect
AMBA 2TLM
TLM2AMBA
T2 - T1GP
T1GP - T2
test bench
Wrapper
Model has: Unclocked threads, vars & events, implicit resets
Synthesis needs: Clocked threads, signals, explicit resets
Refinement step 3a
clocked threads
Refinement step 3b
events to signals
shared vars to sigs
M
S
Refinement step 3c
explicit resets
S
M
DMA
syn-top
clk, rst
T2 - T1GP
T1GP - T2
- unsigned char m_ctl; /* declaration */
- sc_event m_start;
+ sc_signal<unsigned char> m_ctl; if ((*write_data_ptr) & START) { /* producer */
- m_ctl |= START; m_start.notify(d);
+ m_ctl.write( m_ctl.read() | START, PRIO);
}
while(1) { /* consumer */
- wait(); // wait for m_start
+ while (!(m_ctl & START)) { wait(); } // wait for clock
...
}
- SC_THREAD( transfer);
- sensitive << m_start;
+ SC_CTHREAD( transfer,clk.pos());
+ reset_signal_is( rst_n, false);

## Slide 10: SystemC Synthesis
Refined code is synthezisable with Cadence C-to-Silicon
Generated verilog netlists were synthezised with RTL compiler (RC)
Out-of-the-Box
90nm TSMC technology
Reasonable initial QoR (depends on protocol configuration)
Microarchitecture exploration may follow
Synthesis Results | 
Area | 18k-28k
Speed | 333 MHz (3ns)
CtoS timing analysis

## Slide 11: Modeling effort (LoCs without comments and blank lines)
Case study project
  3920 LoCs in 23 files
  687 TLM model
  3233 Syn. model and libs
Canged code by the refinement
  413 LoCs (add/remove/change)
Module |  |  | TLM2.0 |  | SYN
DMA Module |  |  |  |  | 
 | IP module |  |  | 249 | 288
 | Synthesis top |  |  |  | 54
 | Sim wrapper |  |  |  | 167
Reusable Library |  |  |  |  | 
 | Bridges |  |  |  | 306
 | AXI Transactors |  |  |  | 1669
 | TLM functions |  |  |  | 296
Simul. Env / VP |  |  |  | 438 | 453
tb/env (3%)
top-level (13%)
wrapper (40%)
(automatable)
Model (44%)
Functional changes
5%
Module interface
7%
Clocking & reset
7%
Events & signals
11%
Synthesizability
14%

## Slide 12: Simulation performance
Model | Description | Rel. Exec time | per DMA transaction
TLM 2.0 | Virtual prototype with b_transport() interfaces | 1.0 | 1.0
TLM1GP‘ | Refined TLM interface, events replaced by signals, no clock | 1.13 | 1.68
TLM1GP‘‘ | Synthezisable, clocked, with TLM1GP interfaces | 2.42 | 54.23
SIGAXI | Synthezisable, clocked model at the pin-level and its wrappers | 5.52 | 129.01
System runs multiple sets of 22400 DMA transfers
  Several TAs per transfer: setup, read /write, status, verification
Report relative increase in execution time (OSCI simulator)
  Only 5.5X slowdown for overall application
  Depends on ratio of interarrival time of events and the clock period
Notes: Can we run, just the clocked model, without the AXI stuff?

## Slide 13: Lessons learned
Methodology is feasible
Good quality of results achieved
    Disciplined refinement in 3 main steps functionally correct and transaction precise, TLM 2.o to protocol-specific signal interface refinement, clocked processes with resets
Acceptable simulation speed degradation
    Refining TLM 2.0 models down to TLM level appropriate for synthesis causes slowdown of only 2.4X (with clock, without clock by 1.13X)
    Adding re-usable, signal-level transactor costs another 2.3X, (which is still faster, but much closer to RTL simulation speeds)
    Significant slowdown in refined communication (100x) may lead only to moderte slowdown overall (5x)
Total design effort significantly reduced
    < 15% of the refined platform model is design-specific code
    Automation can reduce this further
    Key is re-use of transactors for conversion between transactions and signals