## Slide 1
Results
Total distribution latency is 4 times less sensitive to VDD variation than would be true of a silicon-delay dominated distribution
Robust Variation-Tolerant Clock Routing
Joseph Kozhaya, Phillip Restle, Haifeng Qian, Jan Feder, Mehmet Yildiz
IBM STG & IBM Research
Key Message
PVT variations significantly impact chip performance.
  Minimizing clock skew, both nominal and variation induced, is critical
For robust clock distribution, minimize total latency and maximize wire-delay component.
  High drive strength buffers
  Long wires on top thick metal layers
Methodology involves an automated tuning utility that iterates between routing and simulation.
  Clock router supports specialized wiring topologies
  Simulation engine is SPICE-accurate
Root Adjustment
Initial Routing
Skew: 13.4 ps
Skew: 1.7 ps
Skew: 4.2 ps
Chip Y
Chip Y
Chip X
Clock Latency
Trunk Lengthening
Middle trunk Multiplier: 2.5
Skew: 5.2 ps
Middle trunk Multiplier: 4.0
Skew: 2.0 ps
Initial Routing
Skew: 13.4 ps
t = 0
Routing Topologies
Binary Routing
Star Routing
VDD | 0.8V | 0.925V | 1.0V | Ratio (0.8/1.0)
Skew | 3.3 ps | 3.1 ps | 3.0 ps | 1.1X
Wire Delay | 143.8 ps | 145.7 ps | 146.4 ps | 0.98X
Buffer Delay | 77.8 ps | 62.5 ps | 59.2 ps | 1.31X
Latency | 221.6 ps | 208.2 ps | 205.6ps | 1.078X
Highlights
Robust variation-tolerant clock distribution achieved:
  Minimizing buffer delays
  Maintaining electrical symmetry
Methodology involves:
  Clock router that supports unique wiring topologies
  SPICE-accurate simulation engine
  Tuning wrapper which iterates between routing and simulation until target skew is achieved
Outlined methodology promises significant productivity improvements in clock distribution design.
  Skew reduced from 30.20 ps to 3.10 ps in ~ 30 minutes