## Slide 1: RAPIDS: Post Routing Timing Closure
Michael Kazda
IBM Corporation
East Fishkill, NY
kazda@us.ibm.com
William Dougherty
IBM Corporation
Pittsburgh, PA
wedough@us.ibm.com

## Slide 2: A Typical Design Cycle
Synthesis/Placement
Routing
Post-Route Timing and Fixup
Noise Analysis and Fixup
Checking
HDL
RIT

## Slide 3: A Typical Design Cycle
Synthesis/Placement
Routing
Post-Route Timing and Fixup
Noise Analysis and Fixup
Checking
HDL
RIT
RAPIDS

## Slide 4: Motivation: Causes and Effects of Post-Routing Fixup
RAPIDS
Post-routing design fix-up costly
  Wire delays dominate path delays
  Via resistances have increased dramatically
  Impact of coupled capacitance induced violations requires post-wire fix up strategy
  Variation effects (metallization, negative bias temperature instability, etc.) are not known until later in the process
  Manual intervention on detail routed data is tedious and costly
    Complex feedback of parasitic and coupling impacts to the timing and routing required
Clearly, a role for automation to play
Synthesis/Placement
Routing
Post-Route Timing and Fixup
Noise Analysis and Fixup
Checking
HDL
RIT
Design Time
Notes: Cut down on the number of designs in first chart
Can make the point that this takes a long time without all this stuff
Overall flow, corresponding to bar chart above
Start simple and then move into details
This space is important and IBM has a tool there
It is often the case that following the detailed routing part of the design cycle, a fixup strategy is employed
ad hoc scripting
manual fixes
There is human cost in each and inaccuracies within each approach. Each typically fail to make decisions with variation and parasitic effects properly modeled, which has been shown to cause further iterations. Placement of circuits is often done without knowledge of timing and often causes degradations due to effects like placement in a region of congested wires. Capacitive coupling effects cannot be known until after some form of routing has been performed. Further, variation effects (metallization, negative bias temperature instability, etc.) are not known until very late in the process and netlist changes cannot guarantee that they will entirely solve the problem without some of this information fed back into the decision making.
Post routing optimization can be a manually intensive operation to correct designs in this fashion. One pass of the current manual process takes days for a 5.5 million net design.
Quite often, these corrections create fluctuations and require multiple passes to be corrected.
In one example
1 Logic Engineer, 1 PD Engineer took 5 days to perform one iteration and needed 6 iterations to close the design (~30 days)
RAPIDS was able to do work equivalent to one pass in 24 hours

## Slide 5: RAPIDS Approach to Post-Route Timing Closure
High accuracy, Incremental, lazy-evaluated timing and extraction
  Only extract a net when the load/resistance is required by timing
  Only time when invalidated data is required for computation
  RICE, 2.5d shapes extraction, coupling analysis
Borrowed optimizations from physical synthesis
  Buffering, resizing, cell movement, vt optimization etc.
Additional routing-specific optimizations
  Timing aware scenic net re-wiring
  Layer/wire-code re-assignment for degrading signals
Enforce minimal perturbation
  Disturb only cells, wires that are necessary to effect change
    Reuse detail routes when appropriate
  Optimizations applied in order of increasing disturbance in terms of routing/extraction data
    Try to size cells in place, before we ripup/rebuild buffer trees
Use global routes for intermediate wire represenation
  More accurate than Steiner route w/r/t reality, e.g., layers/congestion
Produce legal placement and legal routes
  Choose non-overlapping placement locations by design, no explicit legalization
  Integrate global and detail router in combined process
EC routing
  “Quick” intermediate detail route after local optimizations
  DRC-clean EC routing as final step
Setup Timing Env
(Sign-off/RLM/Unit)
Parasitics and coupling analysis
Global Routing
(analyze congestion)
Local Optimization
(incremental placement,
incremental global wiring,
Incremental extraction)
Detail Route
(complete opens/globals left
behind by local opts)
Parasitic Extraction
Coupling Analysis
(Identify noise induced by aggrs,
Compute delay & transition effects)
Repeat as necessary to close
Final EC Routing
Kazda, Michael, et. al. 2009. System and method for sign-off timing closure of a VLSI chip. U.S. Patent 7,581,201, filed February 28, 2007, and issued August 25, 2009.
Notes: RAPIDS runs a subset of optimizations from the larger physical synthesis suite
Extended to support incrementally legal placement and routing subsystems.
It begins with an initial pass of routing only optimization that reroutes the worst scenic nets and performs layer reassignment before moving into optimizations affecting gate and pin locations.
These begin with a recovery phase for area and vt.
Area recovery, consisting of powering down gates and removing unnecessary buffering, can be used to enlarge the contiguous space in the design, as well as reduce overall power consumption (along with vt recovery) where pessimism in physical synthesis has hyper-optimized the gates.
Electrical violations are addressed next, using gate resizing, buffering, movement, and vt optimization.
These optimizations are re-applied to optimize the design using a slack based cost/benefit function.
Coupling induced problems
RAPIDS will increase the power level of the driving gate on the victim net, and /or reduce the power level of the aggressor net.
Earl mode padding
Physical synthesis tools use pessimism to minimize surprise effects from scenic routing, but detailed routes that are faster than expected can create early mode timing problems. RAPIDS addresses these by inserting delay buffers along existing routes.
Re-routing
Global routes are used to estimate changed wires until a new pass of detail routing is performed
Net priorities are used to manage degradations
Timing sometimes degrades from post optimization expectations due to routing factors on optimized nets (congestion, etc.) or due to collateral damage on innocent bystander nets

## Slide 6: RAPIDS Approach to Post-Route Timing Closure
High accuracy, Incremental, lazy-evaluated timing and extraction
  Only extract a net when the load/resistance is required by timing
  Only time when invalidated data is required for computation
  RICE, 2.5d shapes extraction, coupling analysis
Borrowed optimizations from physical synthesis
  Buffering, resizing, cell movement, vt optimization etc.
Additional routing-specific optimizations
  Timing aware scenic net re-wiring
  Layer/wire-code re-assignment for degrading signals
Enforce minimal perturbation
  Disturb only cells, wires that are necessary to effect change
    Reuse detail routes when appropriate
  Optimizations applied in order of increasing disturbance in terms of routing/extraction data
    Try to size cells in place, before we ripup/rebuild buffer trees
Use global routes for intermediate wire representation
  More accurate than Steiner route w/r/t reality, e.g., layers/congestion
Produce legal placement and legal routes
  Choose non-overlapping placement locations by design, no explicit legalization
  Integrate global and detail router in combined process
EC routing
  “Quick” intermediate detail route after local optimizations
  DRC-clean EC routing as final step
Setup Timing Env
(Sign-off/RLM/Unit)
Parasitics and coupling analysis
Global Routing
(analyze congestion)
Local Optimization
(incremental placement,
incremental global wiring,
Incremental extraction)
Detail Route
(complete opens/globals left
behind by local opts)
Parasitic Extraction
Coupling Analysis
(Identify noise induced by aggrs,
Compute delay & transition effects)
Repeat as necessary to close
Final EC Routing
Kazda, Michael, et. al. 2009. System and method for sign-off timing closure of a VLSI chip. U.S. Patent 7,581,201, filed February 28, 2007, and issued August 25, 2009.
Notes: RAPIDS runs a subset of optimizations from the larger physical synthesis suite
Extended to support incrementally legal placement and routing subsystems.
It begins with an initial pass of routing only optimization that reroutes the worst scenic nets and performs layer reassignment before moving into optimizations affecting gate and pin locations.
These begin with a recovery phase for area and vt.
Area recovery, consisting of powering down gates and removing unnecessary buffering, can be used to enlarge the contiguous space in the design, as well as reduce overall power consumption (along with vt recovery) where pessimism in physical synthesis has hyper-optimized the gates.
Electrical violations are addressed next, using gate resizing, buffering, movement, and vt optimization.
These optimizations are re-applied to optimize the design using a slack based cost/benefit function.
Coupling induced problems
RAPIDS will increase the power level of the driving gate on the victim net, and /or reduce the power level of the aggressor net.
Earl mode padding
Physical synthesis tools use pessimism to minimize surprise effects from scenic routing, but detailed routes that are faster than expected can create early mode timing problems. RAPIDS addresses these by inserting delay buffers along existing routes.
Re-routing
Global routes are used to estimate changed wires until a new pass of detail routing is performed
Net priorities are used to manage degradations
Timing sometimes degrades from post optimization expectations due to routing factors on optimized nets (congestion, etc.) or due to collateral damage on innocent bystander nets

## Slide 7: RAPIDS Approach to Post-Route Timing Closure
High accuracy, Incremental, lazy-evaluated timing and extraction
  Only extract a net when the load/resistance is required by timing
  Only time when invalidated data is required for computation
  RICE, 2.5d shapes extraction, coupling analysis
Borrowed optimizations from physical synthesis
  Buffering, resizing, cell movement, vt optimization etc.
Additional routing-specific optimizations
  Timing aware scenic net re-wiring
  Layer/wire-code re-assignment for degrading signals
Enforce minimal perturbation
  Disturb only cells, wires that are necessary to effect change
    Reuse detail routes when appropriate
  Optimizations applied in order of increasing disturbance in terms of routing/extraction data
    Try to size cells in place, before we ripup/rebuild buffer trees
Use global routes for intermediate wire representation
  More accurate than Steiner route w/r/t reality, e.g., layers/congestion
Produce legal placement and legal routes
  Choose non-overlapping placement locations by design, no explicit legalization
  Integrate global and detail router in combined process
EC routing
  “Quick” intermediate detail route after local optimizations
  DRC-clean EC routing as final step
Setup Timing Env
(Sign-off/RLM/Unit)
Parasitics and coupling analysis
Global Routing
(analyze congestion)
Local Optimization
(incremental placement,
incremental global wiring,
Incremental extraction)
Detail Route
(complete opens/globals left
behind by local opts)
Parasitic Extraction
Coupling Analysis
(Identify noise induced by aggrs,
Compute delay & transition effects)
Repeat as necessary to close
Final EC Routing
Kazda, Michael, et. al. 2009. System and method for sign-off timing closure of a VLSI chip. U.S. Patent 7,581,201, filed February 28, 2007, and issued August 25, 2009.
Re-route scenic nets
Intermediate EC Route
Area recovery
Resize cells in-place for EVC
Intermediate EC Route
Reduce Vt for LM slack
Intermediate EC Route
Resize cells in-place for slack
Resize w/displacemt for slack
Intermediate EC Route
Intermediate EC Route
Insert buffers for slack
Intermediate EC Route
Insert buffers for EVC
Intermediate EC Route
Intermediate EC Route
Insert delays for EM slack
Re-assign layers on
Degrading signals
Notes: RAPIDS runs a subset of optimizations from the larger physical synthesis suite
Extended to support incrementally legal placement and routing subsystems.
It begins with an initial pass of routing only optimization that reroutes the worst scenic nets and performs layer reassignment before moving into optimizations affecting gate and pin locations.
These begin with a recovery phase for area and vt.
Area recovery, consisting of powering down gates and removing unnecessary buffering, can be used to enlarge the contiguous space in the design, as well as reduce overall power consumption (along with vt recovery) where pessimism in physical synthesis has hyper-optimized the gates.
Electrical violations are addressed next, using gate resizing, buffering, movement, and vt optimization.
These optimizations are re-applied to optimize the design using a slack based cost/benefit function.
Coupling induced problems
RAPIDS will increase the power level of the driving gate on the victim net, and /or reduce the power level of the aggressor net.
Earl mode padding
Physical synthesis tools use pessimism to minimize surprise effects from scenic routing, but detailed routes that are faster than expected can create early mode timing problems. RAPIDS addresses these by inserting delay buffers along existing routes.
Re-routing
Global routes are used to estimate changed wires until a new pass of detail routing is performed
Net priorities are used to manage degradations
Timing sometimes degrades from post optimization expectations due to routing factors on optimized nets (congestion, etc.) or due to collateral damage on innocent bystander nets

## Slide 8: Local Optimization Use of Global Routing, Detail Routing, Extraction and Coupling Analysis
Net A
Net V
1. Start with detail routes,
There’s a coupling-induced fail on Net A caused by Net V
2. Power down source increasing transition time.
Pin locations have changed, RLC/Timing invalidated,
3. Detail routes deleted, Replaced with global routes
Estimated extraction, timing to choose solution
4. Lay down detail routes along global, allowing shorts
Reanalyze coupling
Check timing
Problem solved!!
Minimize Disruption
Few localized routes, if zero displacement, extraction can be retained

## Slide 9: Buffering and Layer Assignment
Buffer and layer assignment are performed simultaneously to provide elasticity in the wiring and gate domains for optimization.
Cost functions
  Load/transition time violation
  Late timing misses
Applied in a two step method:
  Insert buffers along existing detailed routes reusing routes to preserve integrity
  Rip-up and rebuild existing buffer trees, plan new routes with global wires to avoid congestion
Following the existing routes and reusing existing wires can lead to a less disruptive solution
Inserting buffers along red net for EVC
Without wire reuse
With wire reuse
Majority of route reused
Buffers inserted
Buffers inserted
New buffers must fit in existing placement holes
New buffers must fit in existing placement holes
buf
before
after

## Slide 10: Layer Reassignment and Wire Code Optimization
Problem: failing slacks or transition time violations due to high resistance
How: Re-route the detail routes of the net on less resistive layers (thicker)
  Improves downstream transition times and wire delays
  If higher layers are less congested, route solution may be closer to Steiner length, reducing via count
  No placement impact
Beneficial when:
  Technology dependence on routing layers
  Long detail routes
Design A
Design B
Design C
Trans. at driver
Trans. at sink
degrading
Trans at sink
Trans at driver
improved
Wire codes
Layer Reassignment
28% Improvement
10% Improvement
32% Improvement
7% Improvement
11% Improvement
Notes: Do we have the data around to show the number of vias?

## Slide 11: Coupling Fix Up
Slack is directly affected by capacitive coupling
  Delta-delay and delta-transition time
Only concerned with coupling impact on negative slacks and/or electrical violations
Methods
  Indirect coupling fixup
    Coupling capacitance remains the same but is not a timing issue
    Resize cells, Vt opt, Insert buffers, Power-down aggressor nets
  Direct coupling fixup
    Reduce coupled capacitance
    Assignment to more widely spaced or shielded wire codes
aggressor
victim
10 ps delay impact from coupling
Delay of victim increases
Victim
Aggressor
Aggressor

## Slide 12: Optimizing for Variation Effects
Enable statistical static timing analysis
  Model slacks as probabilistic distribution functions instead of deterministic values
  Each variation effect is a adder/subtractor to the base slack
  Applied in RAPIDS to increase accuracy over top of physical synthesis
    Earliest use of statistical timing for optimization within the methodology
Optimizations see a projected value to make comparisons
  Use block-based statistical timer for incremental update within optimizer
*D. J. Frank et al, Symp. VLSI Tech., 1999
Litho-induced variability
Random dopant effects
Oxide thickness
Interconnect CMP effects
Slack (ps)
-400
-300
-200
-100
0
100
200
Single Corner
Exhaustive Corner Analysis
3 Sigma Analysis
Yield (%)
100
80
60
0
40
20
300
Pessimism
Reduction
Full Process
Coverage
Parameter | Delay Impact
BEOL metal (Metal mistrack, thin/thick wires) | 15 %
Environmental (Voltage islands, IR drop, temperature) | 15 %
Device fatigue (NBTI, hot electron effects) | 10%
Vt and Tox device family tracking (Can have multiple Vt and Tox device families) |  5%
Model to hardware uncertainty (Per cell type) |  5%
N/P mistrack (Fast rise/slow fall, fast fall/slow rise) | 10%
PLL (Jitter, duty cycle, phase error) | 10%

## Slide 13: Results: ASICS
Larger designs, hundreds of thousands to several million nets
Lower frequencies: < 1 GHz
Reducing the design TAT significantly through its automated post routing fix up
  Average 58% reduction in post routing closure phase
  Late cycle improvements
QoR of RAPIDS runs
  One run of RAPIDS equivalent to multiple (3-4) rounds of manual fix up
  Averages over these 4 designs
    66% improvement in worst slack
    90% reduction in number of negatives
    58% reduction in transition time violations
    68% reduction in cap violations
Design ECOs
Place & Route
Re-Time
Examine Timing
Reports
Repeat until closed
RAPIDS
Vs.

## Slide 14: Results: Processors
Smaller designs: tens to hundreds of thousands nets
Higher frequencies: > 2 GHz
Heavy emphasis on LVS and DRC clean up
QoR of RAPIDS runs
  25% improvement in worst slack
  74% improvement in number of negatives
  78% improvement in transition time violations
  All DRC errors fixed
All results contained were obtained under specific configurations and are presented as an illustration. Performance obtained in other configurations or designs may vary.
Group B: 49 Designs
Group A: 19 Designs
Notes: Increase font size on charts

## Slide 15: Future directions
Improve predictability of re-routing
  Reduce unexpected scenic routes or collateral rip-ups which degrade expected optimization results
  Tune global routing to better align with detail routing
Include more optimization programs available in physical synthesis
Utilize modified-RAPIDS approach before detail routing
  Eliminate gross problems after the global routing phase
  Guide the global routes to a better detail route solution
  Less to repair in the more expensive detail routed environment
Metal only change support
  Reuse of spare cells and rewiring optimizations
Run time improvements

## Slide 16: Summary
RAPIDS provides an effective means to automate post routing timing closure
  Integrates placement, routing, timing, and synthesis in a single timing closure environment
    Works on fully detail routed design or partially detail routed design
  Emphasizes minimal disruption
  Utilizes high accuracy timing closure
  Provides significant productivity boost over the previous methods using manual fixing or ad hoc scripts
    Manages complex feedback of parasitic and coupling impacts to the timing and routing required
    One iteration of RAPIDS yields better QoR in much less time than early manual iterations