## Slide 1
<number>
  Timing flow quality feed back using on product path delay tests.
Shweta Latawa, Lionel Riviere, Rick Woltenberg
Freescale semiconductor
Austin, TX USA
DAC 2010: Paper #
Note to reviewer(s) : Intended to be run with animation (presentation mode)
Actions/FeedBack on reviews
Comment>Slide21: Can you elaborate on the false positives results and how can these false positive can be reduced ?
> Added definition of “false positive” =statistical error of rejecting the null hypothesis
Comment>Slide 4 - can't read words at bottom of graph (under Process)
> Done. Should now be compatible in ppt 2007
Comment>Slide 11 - not sure of significance of 'not common clock' section.
Are you saying that when analyzing path Fmax results, you have to consider differences between types of path logic, and also between types of clock path logic? That makes some sense, but I think I'm missing something here (because you make a bigger point of the clock path on slide 18). There should also be a 'not common clock' block between the 'common clock' and the launch flop for the path. How does that affect the analysis?
> The oral presentation will be more explicit.
Here is some information:
“clock bifurcation” = the last node of the common clock (in the slide , where blue and red nets separate )
“non common clock ” = portion of the clock that goes from the clock bifurcation to the capture flop. ( red color in the slide)
“ clocked logic” = [portion of the clock that goes from the clock bifurcation to the launch flop ] + [launch flop to capture flop ]
When analyzing path timing inaccuracy, that is path slack inaccuracy, the differences between “ clocked logic” and “non common clock ” are considered ( common clock inaccuracies auto cancel between the “non common clock ” and “clocked logic” )
Comment>Slide 18 - I don't understand. Sounds like property 'P' is a physical property of the paths, related to metal topology. But you also say it is measured as delta between data branch - clock branch. And how do you know that property P explains the double clusters?
> The oral presentation should clarify this.
Here is one example . In this example, there is a systematic error on the resistivity of fat metals ( fat metals are faster than expected ). If path has more fat metal on the “ clocked logic” than on the “non common clock ”, slack will be systematically increased. If path has more fat metal on the “non common clock ” than on the “ clocked logic” slack will be systematically reduced . So for what concerns timing slack accuracy, systematic error is a function of the delta of the property “fat metal length”.
Returning to the slide17, it “happens” than the slack inaccuracy double cluster is also a very good match to some of the properties clusters. From a statistical point of view, because of the large number of path analyzed, the probability for this to be a “false positive” is very low.
Comment>>Adding simple path delay information to help with timing analysis.
> The oral presentation (slide 10) should clarify this.
Comment>>The title of the presentation is "on-product path delay test" , however I don't see the explanation on how the "on-product" measurement is done. Maybe some additional slides can be added to explain the details of the on-product circuitry and measurement.
> Moved slide 22 to slide 8. The oral presentation (slides 8 to12 ) will explain that test scan flops are inserted in the Test Vehicle and product logic in order to enable this “on product” timing test
Comment>Reasonable good. Need to describe remaining issues and future works.
> Added slide24 on current developments.
Notes: <number>
Timing: 25sec
Main message:
Introduction of the authors.
Introduction of the paper

## Slide 2
<number>
Outline
Motivation
Path delay scan methodology
Measurement results
Results data mining
Conclusion
Notes: Timing: 15sec ( cum 40sec)

## Slide 3
<number>
Motivation
Path delay scans methodology
Measurement Results
Results data mining
Conclusion
Notes: Timing: 2sec

## Slide 4
<number>
Process approximations = evolving process
Spice models approximations = models, test structures, phys effects,…
Extraction approximations = layout, phys effects,…
Characterization approximations = .lib format, spice engine, process corners,…
Timing approximations = STA, Temperature & Vdd gradients, …
Flow inaccuracy
DESIGN WASTE
YIELD LOSS
Problem
Notes: Timing: 26sec ( cum 68sec)
Main message:
- Design flow accumulates approximation. This lead to design waste or yield loss.

## Slide 5: Test vehicles limitations
<number>
Actual silicon
Spice models
Extraction
Characterization
Timing
Test Vehicles
Test Vehicles
Design space
Validated by test vehicle
Actually used
Notes: Timing: 20sec
Main message:
- Test vehicle only enables control of some specific elements of the flow.

## Slide 6: Solution  Product Feed back
<number>
Actual silicon
Spice models
Extraction
Characterization
Timing
PRODUCT RESULTS
Flow inaccuracy
Notes: Timing: 18sec ( cum 86sec)
Main message:
- Quality feed back loop enable control of the flow inaccuracy.

## Slide 7
<number>
Motivation
Path delay scan methodology
Measurement Results
Results data mining
Conclusion
Notes: Timing: 2sec

## Slide 8
<number>
Node interception
PROCESS DEVELOPMENT
PROCESS QUALIFICATION
IP QUALIFICATION
PRODUCTS
PATH DELAY TESTING
Notes: Timing: 55sec ( cum 647sec)
Main message:
Path delay testing is a complement to Test vehicle testing.
It intercepts node during the IP qualification phase.
It enables continuous improvement during node lifetime  limit need for new test vehicle

## Slide 9: “Robust” path delay scan concept
<number>
Clk
Expected
Measured
Pass
Path Logic
Path Logic
Path Logic
Path Logic
SCAN IN
PATH TEST
SCAN OUT
Notes: Timing: 30sec
Main message:
- Robust path delay enables energizing of specific paths in product.

## Slide 10: Fmax measurement
<number>
Path Logic
Path Logic
Path Logic
Path Logic
Clk
Expected
Clk
Measured
Pass
Fail
Decrease Period to Fmax (0 slack)
Failing Path
Notes: Timing: 13sec
Main message:
- Clock frequency increase enables Fmax measurement for each path.

## Slide 11: Slack measurement
<number>
Path Logic
Common Clock
Test pattern
Test results
PASS
FAIL
PASS
SLACK
MEASURED SLACK
Reduce Clk Period
Reduce Clk Period
Mass Path delay scans + PLL frequency increase enables slack measurements
Non Common Clock
Notes: Timing: 44sec ( cum 175sec)
Main message:
- Frequency scan enables the measurement of path slack.

## Slide 12: Why “on product”
<number>
Path timing data enables 11 comparison to timing report.
On 20% of product paths

10-100K paths 
Representative coverage of design space
Notes: Timing: 40sec ( cum 215sec)
Main message:
The “on product” data collection + the very large number of paths testable enables a representative and rather exhaustive measurement of the design space.

## Slide 13
<number>
Motivation
Path delay scans methodology
Measurement results
Results data mining
Conclusion
Notes: Timing: 2sec

## Slide 14: Slack inaccuracy
<number>
2200 paths tested / 6 minutes per die
Typical process / dies across multiple wafer locations
FASTER than expected
SLOWER than expected
Predicted slack from timing report.
Measured slack ( average of 30+ dies ).
±10% Clock Period
OVER DESIGN
FAR OUT…
Learning = Timing flow inaccuracy
Notes: Timing: 80sec ( cum 297sec)
Main message:
Collected data enables measurement of timing flow inaccuracy = a comparison of measured slack to predicted slack.
The slack data is displayed as a comparison to a “perfect accuracy slack prediction” => red zone = faster then expected, blue =slower than expected
This data set shows: a cluster of paths that are overdesigned ( potential for power saving) a group of paths that are much slower than expected ( functional risk ).
Understanding what causes inaccuracy would enable optimal design margining.

## Slide 15: Fmax Variability
<number>
PathX Fmax
Die1
Die2
Die4
Die3
Die5
Die6
Die7
Die8
Die9
Die10
Die11
DieN
Fmax spread
Fmax
Die1
Die2
Die4
Die3
Die5
Die6
Die7
Die8
Die9
Die10
Die11
DieN
PathY Fmax
Fmax spread
Stable paths
3%
7%
8%
9%
2%
6%
5%
4%
Variation sensitive paths
Fmax relative variability ( Inter quartile range across 30+ dies ).
Learning = Process sensitivity
Notes: Timing: 57sec ( cum 354sec)
Main message:
Collected data enables measurement of path Fmax fluctuation across various dies = sensitivity to process variations.
This data set shows path Fmax variability goes from 2 to 9%
Understanding what causes immunity or sensitivity to process variation would enable “robust” design practices. .

## Slide 16
<number>
Motivation
Path delay scans methodology
Measurement Results
Results data mining
Conclusion
Notes: Timing: 2sec

## Slide 17: Making sense of the data
<number>
Path Inaccuracy
Path variability
Path properties extraction
tentative root causes
Validated root causes
Data Mining
Test specific paths
Validation
Mining
Find paths with minimum / maximum density of root cause
Path tests data
Refine margining hypotheses
Validate OCV tables
Guide yield bring Up
Design flow corrections
Notes: Timing: 83sec ( cum 440sec)
Main message:
Product collected data enables refinement of the margining hypothesis + provides direction for yield improvement.
Path inaccuracy / variability observations are analyzed in relation to path properties ( electrical and physical properties ).
Some correlation are found between inaccuracy / variability and path properties.
Additional / directed tests can be implemented to verify that correlations are causalities (and not statistical analysis flukes)
Flow ( models / extraction scripts / simulation scripts / timing methodologies ) is adjusted based on found root causes

## Slide 18: Example1: Inaccuracy cause
<number>
Property “P” ( related to path metal topology ) is a good fit to the observed slack inaccuracy double clusters.
Path Logic
Not Common Clock
Com Clock
Path property “P” is measured as delta between data branch – clock branch
+ : P > threshold, x : P < threshold
Predicted slack
Measured slack
Notes: Timing: 60sec ( cum 500sec)
Main message:
For slack inaccuracy analysis, the path properties are analyzed as a difference between the data brach and the non common clock branch.
The graph provides an example of a property (related to path metal topology ) that match the slack inaccuracy observed clusters.

## Slide 19: Example2: Variability cause
<number>
Very stable paths
stable paths
typical paths
variable paths
very variable paths
Property “P”
Mean (95% confidence interval)
Highly variable paths tend to have high value of property “P” ( related to standard cells layout ).
Notes: Timing: 50sec ( cum 549sec)
Main message:
Paths are grouped in “variability groups”. Path properties are analyzed to check if statistical differences exist between groups
The graph provides an example of a property (related to the layout of cells used in the path ) that is statically different between the variable/highlyVariable groups and the other groups of paths.

## Slide 20
<number>
Motivation
Path delay scans methodology
Measurement Results
Results data mining
Conclusion
Notes: Timing: 2sec

## Slide 21
<number>
In order to minimize data mining “false positive”, use a ratio of paths / properties > 20 With typically >500 path properties extracted  data collection on >10000 paths  1 hour test per die ( 5MHz frequency steps )
Test compression needs to be bypassed in order to disambiguate what paths are measured.
“testable” frequency range is limited by PLL capabilities. Data stitching sometime needed depending on the PLL ranges.
Path properties extraction requires advanced scripting. Some limitations related to back end tools capabilities to aggregate information at “path level”.
Practically…
Notes: Timing: 41sec ( cum 592sec)
Main message:
Massive data collection is needed to enable success of data mining.
Fmax detection will depend on PLL structure.
Some limitations of back end tools put limits on “extractable” path properties.
Smart datamining enable faster discovery process.

## Slide 22
<number>
In order to minimize data mining “false positive”, ( statistical error of rejecting the null hypothesis ) use a ratio of paths / properties > 20 With typically >500 path properties extracted  data collection on >10000 paths (1 hour test per die)
Test compression needs to be bypassed in order to disambiguate what paths are measured.
“testable” frequency range is limited by PLL capabilities. Data stitching sometime needed depending on the PLL ranges.
Path properties extraction requires advanced scripting. Some limitations related to back end tools capabilities to aggregate information at “path level”.
Practically…
Notes: Timing: 41sec ( cum 592sec)
Main message:
Massive data collection is needed to enable success of data mining.
Fmax detection will depend on PLL structure.
Some limitations of back end tools put limits on “extractable” path properties.
Smart datamining enable faster discovery process.

## Slide 23
<number>
Path delay measurements enable ON PRODUCT verification of the timing design flow ( stack of models, spice extraction, spice simulation, RC extraction, STA ).  VALIDATION OF THE ACTUAL DESIGN SPACE.
It also enables measurement of variability at path level:  LEARNING FOR MARGINING + DESIGN FOR YIELD
Comparison of collected to data to paths physical-electrical properties enables identification of inaccuracy/variability root causes.
 DESIGN FLOW CALIBRATION AND IMPROVEMENT.
Conclusion
Notes: Timing: 50sec ( cum 717sec)
Main message:
On product Path delay measurements enables
  Validation of the actual design space for timing.
  Validation of the margining and design for yield hypotheses
When this data is cross analyzed compared to path electrical/physical properties, the root causes of excessive inaccuracy/variability can be identified  improvement of the design practices.

## Slide 24
<number>
Expand the methodology from “PATH” to “TRANSITION delay” test patterns.
Benefits:
  REUSE of qualified production test patterns
  Integration in the test PRODUCTION ENVIRONMENT.
  Data collection & analysis on 1000+ DIES.
Challenges:
  Convert AMBIGUOUS information from “transition delay fail at x MHz” to “path ABC fails at x MHz”.
Future