## Slide 1
Results
Incremental Via Filling was used on “Lincroft” (Next generation System On Chip for Intel® Atom™ processor)
70% density violations were removed in a DRC aware fashion with reasonable runtime
Many of the density errors were contributed by KOR layers in the layout
An Incremental, Correct by Construction Approach of Addressing Via Density
Dibyendu Goswami, Swami Gangadharan, Albert Holguin
Intel Corporation
Host Machine: 4CPU Xeon(R)5150@2.66GHz, 66GB RAM
Runtime: 15hrs 30mnts
Via | Via Count |  | Local Min Density Errors |  | Comment
 | 1st Pass | 2nd Pass | Input | Output | 
Via3 | 3.8m | - | 528 | 29 | There is no 2nd pass for via3
Via4 | 3.6m | 2.7k | 174 | 40 | 40 Via4 Violations. No KOR.
Via5 | 3.1m | 25k | 89k | 60k | Many of the remaining density errors were due to KOR layers in the design that prevented v5 fills in certain regions
Via6 | 1.7m | 12.2k | 43 | 10 | 10 Via6 violations. No KOR.
Via7 | 141k | 6k | 92k | 800 | Many of the remaining density errors were due to KOR layers in the design that prevented v7 fills in certain regions
Conclusions and Future Work
Incremental Via Filling can address stringent via density in UDSM node in a DRC-aware fashion
Metal, Via fills are grown in DRC correct by Construction
Two types of Via filling based on timing and reliability
Three types of metal fill stitching schemes to maximize on Via filling
2nd pass filling contributes to 8% more via fills
Pseudo-Iterative filling wherein 2nd pass metal, via fills are grown at the 1st pass itself improves on runtime by ~11%
3rd Pass Via filling: to address the rest of the density errors is a potential option
Via fills maximized by employing different metal fill stitching schemes (1st Pass Via Filling):
  Metal Fill to Upper pwr, gnd (f2up) Stitching
  Metal Fill to Down pwr, gnd (f2dp) Stitching
  MetalX Fill to Metal(X+1) Fill (f2f) Stitching
    Via fills at the intersection MetalX and Metal(X+1) fills of same polarity
Fill to Upper Power Stitch: V4 Fill that stitches M4 Fill with M5 VSS
M5 VSS
Fill to Fill Stitch: V4 Fill that stitches M4 Fill with M5 Fill
Fill to Down Power Stitch: V4 Fill that stitches M5 Fill with M4 VSS
M4 VSS
Different stitching schemes during 1st Pass Via Filling
Metal Fill Stitching Schemes
Extremely stringent via density rules in UDSM nodes
  Conventional Via filling by stitching metal fills with power, ground buses is not enough
Tremendous increase in number and complexity of DRCs
  Poses challenge to make Via fills DRC aware
  Additional constraint for via fill patterning – limits the no of via fills
Interconnects becoming taller, thinner and closer
  Significant increase in cross-coupling capacitance
  Maximize Via fill to reduce IR-drop
“Single pass” Via filling often results in “density Violation”
Motivation
Still not Enough!! Need more Vias!
Root Cause: Presence of excessive signal metals resulting in sparse metal fills (“3X DR” space)
Via density rules are checked on 1st pass metal, Via fill inserted layout
2nd pass metal fills: Metal fills that are created at “1X” distance from signal metals
2nd pass Via fills: Stitch 2nd pass metal fills by employing all three types of stitching schemes
Pseudo-Iterative Filling: Both 2nd pass Metal and 2nd Pass Vias are grown in the 1st pass itself
Via5 density violating window Only 2 more V5 fills required
A
M5 power/gnd bus
M5 signal
Via5 Fill
V5 Density Violation after 1st pass Via Filling
Incremental Via Filling
Metal4 Fill Pattern
3X DR
3X DR
1X DR
M4 Power
M4 Signal
Metal4 Fills
Metal fills are based on pre-defined “fill grids”, at 3X DR (Design Rule) from Signal and 1X DR from pwr, gnd buses
DRC-cleanliness: Min-length, min-width checks with “Metal Fill Segmentation”
Via Fill polygons are grown by Group Selection Boxes (GSBs)
Additional restriction on Via fills due to Via Patterning Issues
GSB
Via can’t be placed here
Floating Metal fill
Stitched Metal fill
VCC
VSS
VCC
VSS
TYPE 2 Via Fill TYPE 1 Via Fill
VCC
VSS
VCC
VSS
Metal, Via Fill Pattern
Special treatment to ensure DRC Correctness!
2nd Pass Metals can be thrown or retained in the end based on density violations
  They should not result in DRCs in either case
“3X KOR (Keep Out Region) Box”:
  to grow 2nd pass metal fill
  To legalize metal fills (min length)
2nd Pass Metal fill is discarded if it is:
  Outside of Via Density violated window
  Doesn’t contain any Via fill
Section of discarded 2nd pass metal fill is retained
  To ensure min length of 1st pass metal fills
  To legalize enclosure of 1st pass Via fills
Pseudo-Iterative Filling saves runtime with a little bit more memory and compute overhead
2nd Pass Metal Fill violating min length
3X KOR Box incremented horizontally to satisfy min length
1X DR
3X DR
3X DR
Min Length + 1X Space
3X DR
Section of discarded 2nd pass Metal fill could get retained to satisfy via enclosure, min length requirement of the 1st pass metal
3X KOR Box adjustment
Pseudo-Iterative Filling
Signal to Fill Space:
Final 1st pass metal fill = “3X Dr”
Provisional 2nd pass metal fill = “1X DR”
1st and 2nd pass Via fills are grown by f2up, f2dp & f2f Stitching
Combined 1st and 2nd pass metal/via fills must be DRC-clean
Provisional 2nd Pass Via Fills are retained separately, not combined with 1st pass final via fills
2nd pass metal fill outside of via density violated window thrown away
Floating 2nd Pass metal thrown away
The Flow Chart