## Slide 1: Verifying Multi Protocol Wireless SoC using ESL DAC – 2010
eInfochips Confidential
Technology Design Services & Solutions
Software | Embedded System | ASIC/FPGA
Nilesh Ranpura (Project Manager-ASIC)
eInfochips
nilesh.ranpura@einfochips.com

## Slide 2: Confidentiality Notice
<number>
This document is authored by eInfochips and is eInfochips intellectual property,
including the copyrights in all countries in the world. This document is provided under a
license to use only with all other rights, including ownership rights, being retained by
eInfochips. This file may not be distributed, copied, or reproduced in any manner,
electronic or otherwise, without the express written consent of eInfochips.
Copyright (c) eInfochips. - All rights reserved
Notes: <number>

## Slide 3: Overview / Background
eInfochips Confidential
  < Please provide information here>
<number>

## Slide 4: Multi Protocol Verification Environment Challenges
Filter
Filter
Configurable Base band
for
GSM, EDGE,
HSDPA,
&
WLANi
JTAG
TEST
Tuner
Correl
GPS
ME
Processor
TCXO
32.768kHz
POR
PMU
Analog
Processor
ICU
ROM
SRAM
ARM SS
PATCH
DMA
WD
TIMERS
DEBUG
Bluetooth
MAC
UART
SLIMbus
I2C
GPIO
PTA
PCM/I2S
SCU
LPO
PLL
Clock
BT-BB
Tuner
Correl
FM
ME
State machine
Interface
eInfochips Confidential
Technology: Analog-Digital boundary
Type: DA converter, PAs, Analog control block, Modulation
Details:
Connectivity path verification only
Verification completion at FPGA board level and pre-silicon validation level
AMS mode of simulation
Technology: GSM, EDGE, HSDPA
Type: Configurable(Software driven) HW
Details:
Configurable Tx, Rx based on modulation technique
Works as OFDM, QPSK depending on configuration
Basic building blocks are IFFT, Correlation filters, encode, decode
Verification challenge:
Verify each DSP sub block for each parameter of Modulation, power, speed
Ensure Tx-Rx pair and multi-pair modes
Each configuration of GSM, EDGE, HSDPA need to verify functionality wise and Performance wise
<number>

## Slide 5: Multi Protocol Verification Environment Challenges (Continue)
Use of System modeling tools, their integration and tool complexity
  Analog blocks, all DSP and modulation blocks were modeled and simulated in MATLAB.
  Bluetooth MAC, HSDPA MAC, WLAN MAC, GSM were SystemC models to validate specification compliance and SystemC was selected to run C++ software / firmware on them.
  Running Boot loader firmware and base functional software using ARM RVDS3.0 tool set and debugging of software bugs while ASIC Verification is going on.
Clarity on Migration Guideline
  Test bench was maintained in Verilog and C++ with directed testing since long.
  Uncertainty about migrating to OVM as it was getting stabilized between 2007-2008, new features were semi-stable. (i.e. ports)
eInfochips Confidential
<number>

## Slide 6: Right Solution, Not unique Solution approach: Multiple methods of VE / ESL
Right usage of all “strength” of all tools
  All IP level test bench in SV using IUS82, migrated from Verilog, VHDL
  All reference model for GSM, 802.11, EDGE, HSDPA in SystemC
  All cluster and chip level test bench using SV top level test bench, coverage model and SystemC for MAC level drivers.
  Complete chip level model in MATLAB to have reference data path
“Migration requirements” from Legacy to OVM
  Legacy environment was in VHDL, Verilog, C, and different language sub-sets. Multiple IP with different verification approaches developed across the years.
  No strong focus on advance verification methodology, features, and reuse like CDV, randomization, error injections
  Time to market was key issue impacting (a) execution time (b) maintenance of verification environment and (c) extendibility
Migrating “limitations” of solution to validation/FPGA prototyping
  All analog interface at base band level was simulated using analog models and AMS, but it can not be accurate to ensure functional correctness. Hence equivalent Hardware ASSP chips, FPGAs are being used to model system.
  Complete System was partitioned on multiple FPGA board using Xilinx Virtex-5 series representing one wireless set. Such two set will work as two devices.
eInfochips Confidential
<number>

## Slide 7: Detailed view of VE, Process and Solution
Challenge:
  Specs are continuously changed as it was in draft phase at IEEE. “evolving specs” are properly tested by teams at system specification level and DV level.
  IP level test benches needed evolution as they were derived from IP group and legacy environment. Configurable Radio was complex IP to verify with lots of directed test cases.
Solution:
  Unified flow was identified to ensure complete verification “right” from System team  DV team  Pre-silicon team. This is unique decision and systematic approach instead of evolving approach.
    Result : Complex process viewed simple by different teams (diagram in next slide)
  Phase wise migration from legacy to SV-OVM based verification environment. This is to bring “Coverage based verification” and randomness in verification.
    Result : more bugs was found and ensured clean silicon
  Ensure following simultaneously
    Functional correctness at IP and Chip level
    System Performance
      Result: System was functioning at RTL and FPGA level matching “system spec”, performance numbers (i.e. speed, power, software execution)
<number>

## Slide 8
18-Dec-2008
<number>
System Performance Analysis
Design Verification (Simulation)
Design Verification (Emulation)
System Verification (Pre-Silicon)
System Validation (Post-Silicon)
Bit-matching with system model
Untimed-Timed RTL verification
Verification Requirements
Algorithm & Architecture Specification
Test vector interoperability
ADS for circuit-level RF specs
C/MATLAB/Simulink for link-level fixed/floating point specs
ADS/Cadence
NC-Sim
FPGA Platform with black RF transceiver
- Interoperability test with 11n devices
- Interoperability test with legacy devices
- Algorithm verification in real-time environment
- Network-level performance optimization and
cross-layer analysis (data rate adaptation)
- Verification of key product requirements (range
extension with STBC)
FPGA Platform for digital HW/SW
- HW-SW Integration
- RTL functional validation
- Cross layer (PHY-MAC-APPL) integration
Detailed view of VE, Process and Solution (Continue)
<number>

## Slide 9: Detailed view of VE, Process and Solution (Continue)
IP level test bench view
  Each sub-block is verified independently and re-used at block and cluster level.
  Scoreboard/Test point at each sub-block, block level and compared with MATLAB models and FPGA models. This ensures functional and system performance.
<number>

## Slide 10
Test bench for
Configurable Base band
for
GSM, EDGE,
HSDPA,
&
WLANi
Channel Model-MIMO
eInfochips Confidential
Soft Radio-Cluster Verification Environment
Processor
Configure
through
Firmware
Test bench for
Analog FEM
Config
Model
Matlab
Analog FEM
Matlab model for
Configurable Base band
for
GSM, EDGE,
HSDPA,
&
WLANi
Matlab
Analog FEM
Matlab model for
Configurable Base band
for
GSM, EDGE,
HSDPA,
&
WLANi
data
data
data
data
<number>

## Slide 11
OVM based SoC Environment
The OVM test bench environment consists of reusable verification environment/components. Full chip verification was partitioned as
  IP verification at the block level
  Sub-system verification
  full chip (system) verification
  We designed them to be encapsulated and ready to use with a consistent architecture. Three verification components were mapped to OVM as block level test benches
A WLAN and peripheral block test bench was designed using the same approach. HSDPA and other block level test benches followed the same approach with a SystemVerilog layer
  Results
  Build() and create_component() functions are important ones to ensure the OVM multi sequencer is the right combination for the OVM factory
  Built-in phases to handle all phases in run-order, as shown below
    new() , build(), connect() , end_of_elaboration(), start_of_simulation(), run(), extract(), check(), report()
  In fact, the HSDPA block test bench was a typical Verilog model to generate base traffic and model the HSDPA functionality.
  The OVM library on top of it added “messaging”, “component structure”, ovm_threadhandler, ovm_sequencer
  The HSDPA verification IP was modeled as an ovm_component with all the OVM features
Detailed view of VE, Process and Solution (Continue)
<number>

## Slide 12
Legacy View:
  ARC sub-system testing was created reusing a legacy environment. ARC sub-system comprised of ARC CPU core, AHB matrix, WLAN device, HSDPA device, and peripherals like UART, I2C etc. ARC sub-system was verified using normal C (firmware programs) running on ARC CPU using ROM image.
  This C program performs
    Initialization of memory, registers, and devices
    Basic data read/write
    Dumping data values to memory to compare with actual values
  Thus scoreboarding was done at the memory data level by ARC. This is called a “Soft-Scoreboard.”
Results OVM conversion:
  AHB SV VIP and ARM model in C++ replaced legacy system.
  An OVM compliant AHB monitor is hooked with AHB RTL, while this ARC sub-system verification is performed.
  This ensures that if anything goes wrong on AHB bus, assertions will be triggered. All C programs ran on ARC reference models.
  Actual ARC sub-system and results were compared through a script in batch mode. Each RTL block on ARC-Soft-Scoreboard was verified using this mode.
  The top level scoreboard was linked with the scoreboard of the Peripheral verification environment and Soft-Scoreboard derived from the ARC ROM.
Detailed view of VE, Process and Solution (Continue)
<number>

## Slide 13: Detailed view of VE, Process and solution (Continue)
<number>

## Slide 14
Detailed view of VE and solution- Results
Legacy block in Verilog, C, VHDL | SV converted block | Matlab Models | FPGA based verification (To validate) | Results
 |  | (a)DSP Sub blocks (FFT, iFFT, Viterbi decoders, scrambler, convolution endec ) (b)Analog blocks (ADC, D/A, Mixer, Modem blocks, Switches) | Each block fine tuned on FPGA to ensure BER, S/N Ratio, Noise margin, no. of Taps, floating point blocks, ADC margin | Optimized, verified and silicon validated DSP sub-block (matching matlab results) Flexible System fine tuning methods and test point Direct link with Matlab through simullink
AHB, Bluetooth, I2C, PCM, GPIO, FM, GPS | All blocks of legacy converted in to SV VIP with CDV, ABV and randomness | Not Applicable | Each IP is validated to ensure end to end (host to host) connectivity mainly for protocol driven datapath | Simulation performance up by 2.5x due to SV (single language) 40 IP level bugs found, made SoC level verification smooth.
Full chip environment at Chip level | All monitors, scoreboard in SV with CDV, ABV | Not Applicable | Complete chip partitioned on three FPGAs and doing sanity system level tests to ensure functional and system properties | SoC verification got limited do “datapath” and more “performance centric”. TTM was saved by 40% Silicon tape out on 45nm
<number>

## Slide 15
Multiple wireless protocol complexity
  Configurable technology, but meeting same performance and functional requirements
  Increases test bench complexity, with lot of accuracy
  Mobile architecture (multi-protocol) are not just SoC level, they represent System level view
    Software
    IP
    Performance, application
Verification complexity
  Mobile platform group has many test benches
    Existing VHDL, C++ and MATLAB models
    New SV based for incremental protocols
    Migrating Test bench (OVM) and matching requirement is crucial decision as TTM in mobile market is cutting edge..!!
    Risk mitigation  Who thinks ? It’s time for verification lead to keep watching this factor.
  Evolution of ESL in practically all wireless/Mobile platform, which is good news for maturity of ESL.
    Suggestion/Learning:
    ESL /Modeling tools are lagging behind “Specification update” and hence users have to design their own model/method till it comes from vendor.
    Most of mobile architecture SoCs move forward on “WLAN, Bluetooth, GSM, HSDPA” advance and draft standards, so ASIC team need to move forward with their own methods/VE instead of only relying on ESL/Validation/Verification tools. This calls for customized flow  Right solution and not unique flow..!!!
    Multi-language environments calls for “performance bottleneck” improvement and multi-language skills too..!!, hence migrating to OVM (support for all language) in long run is best shot.
Summary
<number>

## Slide 16
Thank you
India Headquarters 11/A-B, Chandra Colony, Off C.G. Road, Ellisbridge, Ahmedabad 380 006 Tel: +91-79-2656 3705 Fax: +91-79-2656 0722
US Headquarters 1230 Midas Way, Suite# 200, Sunnyvale, CA 94085. Tel:+1-408-496-1882 Fax: +1-801-650-1480
Pune : 91-20-41402525
Austin : 1-408-621-4634
Boston : 1-508-870-0500
Chicago : 1- 847 387 7225
Dallas : 1-214 641-9293
UK : 44 1189 566 660
Germany : 49-160-741-8940
Japan : 81-3-5789-5854
www.einfochips.com
<number>
Notes: 81-3-5789-5854