## Slide 1: Hard IP Integration – From Analog to SoC Integration James McCollum, Steve Klass June 15, 2010
DAC 2010 – Anaheim, CA
Notes: [filename or description]_Rev
Page <number>
SMSC CONFIDENTIAL

## Slide 2: Context & Motivation
Corporate movement to increase and improve IP reuse
  Older internally-developed IP was difficult to reuse
  Having no real “IP Catalog” also hampered reuse
  IP quality was not known or measured
Hard IP reuse committee
  Defined requirements and recommendations for views
  Developed standards and metrics for IP
  Corporate-wide team of IP providers and end-users contributed
Use of externally-procured IP is increasing
  Time to market
  Staffing
  Analog expertise for specific blocks
Design Automation Conference – June 2010

## Slide 3: SoC team integration requirements for hard IP
Top-level place/route capability
  Liberty-specified cell timing/power/etc.
  Library/cell/pin attributes
  FRAM/LEF functionality and accuracy
  Techfile consistency (All IP used in SMSC libraries need to use a common set of SMSC techfiles for layers, contacts, etc.) Working with existing IP
Physical verification enabled at top-level
  Provide DRC logs from processing time (that can be referred to)
  All IP must be LVS clean to the SMSC official PD decks at processing time
  No connect by colon, no split gate reduction, no hcells file, etc.
Need to run using existing IP releases for validation
Design Automation Conference – June 2010

## Slide 4: IP tool requirements
Provide a consistent data structure when building IP releases for analog vs. mixed-signal vs. digital
Consistency checks (particularly with pins)
Ensure any generated or derived views/data maintains consistency with input data
Work with multiple types of IP (analog, mixed-signal, digital)
  Blocks (including memories)
  I/O libraries
  StdCell libraries
Enable IP to work with SoC teams using tools from multiple vendors
  Synopsys ICC/Astro
  Cadence SoC Encounter
Design Automation Conference – June 2010

## Slide 5: IP tool requirements (continued)
Be capable of using multiple vendors as required
  Physical verification using Mentor tools
  Milkyway library generation using Synopsys tools
  LEF generation using Cadence tools
Enforce SMSC Hard IP specifications
  Naming, attribute requirements, versions, etc.
Perform basic tests to ensure SoC usability
Support metrics
Be usable by IP providers and end-users
Low-cost
Use as much automation as possible
Design Automation Conference – June 2010

## Slide 6: IPGen – an application in Python
Decision: Develop IPGen in-house
  Several IP packaging and generation tools were evaluated
  None met enough of the requirements to justify using them
This tool was developed using Python because:
  Object-oriented, open-source
  Team python language expertise
  Capability to drive EDA tools direct from Python
  Improved testability due to this functionality
IPVerify – the underlying core on which IPGen is built
  IP validation and IP generation will see the same messages
  Enables the IP generation process to run as a cycle
Design Automation Conference – June 2010

## Slide 7: Verification Methodology to check IP (IPGen)
IPGen establishes a systematic methodology to provide the necessary collateral to the SOC integration teams in a consistent and verified manner.
GDS
Verilog
Liberty
Netlist
smscIPVerify
GDS
Verilog
Liberty
Netlist
LEF
MW lib
…
GDS
Verilog
Liberty
Netlist
LEF
MW lib
…
smscIPGen
Release to Perforce
Design Automation Conference – June 2010
Notes: Q1 2007 Conf Call Slides_Rev 5
Page <number>
SMSC CONFIDENTIAL

## Slide 8: New Hard IP Process (Internal/External)
Benefits
  Quality Audit up front can be informational to both the IP Consumer and IP Provider.
  Scalable inputs - can be as little or as many as delivered.
  Issues are known early and can be fed back to procurement.
Process
  Internal IP can be pushed into perforce by IP providers or by the Hard IP Team.
  External IP can be pushed into perforce by sending a request email to the Hard IP Team.
  A bug and issue tracking request email to Hard IP Team is required for Bugzilla support and to establish a point person for IP.
  Process is facilitated by the IP Providers or the “Hard IP” Team including Design Automation.
Design Automation Conference – June 2010

## Slide 9: IP processing cycle (Health)
Design Automation Conference – June 2010
IPGen first will run health checks on views provided
  Health checks only occur once per view
On a successive loop, completed checks are skipped
One output of the Health cycle involves metrics
  Rates the IP against the Hard IP Specifications
  This data will be available in the IP catalog
Example: Liberty model metrics

## Slide 10: IP processing cycle (Verify)
Design Automation Conference – June 2010
Defined tests/validations for IP
  For most runs, when criteria are met, the job will start
  Pin validation is special, it runs each cycle as more views are assimilated
    Existence, direction, P/G
  Mentor CAA and CFA supported
  GDS sanity check
    GDS layers used
    Cell name lengths
  Milkyway-Verilog integration test
    Places cells, autoroutes, validate bus order, FRAM
  XOR stream out of MW lib (testing against the source GDS)
Example: smscIPCHK

## Slide 11: IP processing cycle (Generate)
Generated/derived views given IP
  The tool will work with whatever inputs are provided
  e.g. If a GDS is available, and LEF is not, LEF will be generated
  e.g. When GDS, LEF, and LIB are available, MW will be generated
  Verilog views in generation built from pin validation data
  Verilog_stub used in place of V2LVS
  Verilog_pgv used for power/ground tests
  All Liberty DBs are compiled within IPGen to ensure consistency and eliminate issues arising when designs point at DBs that were compiled with different versions of Library Compiler
  Milkyway libraries are built to minimize human error in the complex BPV and FRAM generation stages
Design Automation Conference – June 2010