## Slide 1
At frequency range of our interest, synthesis method resulted in better area efficiency due to
  Built-in IP has shown significant gains vs. manual design for arithmetic circuits.
  Tool is able to pick up area optimized implementation depending on slack.
  Library cell enhancements for datapath synthesis implementation
Area savings results may differ for very high frequency designs beyond a couple of GHz and also for non-arithmetic type logic.
Library cell content plays a significant role in design optimization as indicated by larger area gain w/enhanced library under same synthesis tool conditions.
Synthesis vs. Hand design: A Case Study on an Arithmetic Datapath Design Sreekanth Madgula, Subramaniam Maiyuran, Nowjand Attaie, K K Ram Ramakrishnan Intel Corporation, Folsom, CA 95630 Email:<First Name>.<Last Name>@intel.com
Key QOR Metrics: Area, Power and Performance
Pre-pipeline: 36% lower area for similar performance w/Synthesis
Post-pipeline: 27% lower area for similar performance w/Synthesis
Power, measured as device width, has improved only marginally (2%) w/Synthesis
Note*: Device widths in flip-flops were not included in hand design for post-pipeline case.
Context
Design Methods
Quality of Results Comparison
Analysis of Results
Technology Library
Tools & Built-in IPs
Conclusions
Further Work
Critical datapath in modern processing cores often targeted for hand design approach for better area /power /performance optimization.
Manual design often not sustainable because of late design changes due to continuously evolving external specs and short time to market driven by mobile/CE segments.
Our goal was to assess QoR tradeoffs of synthesis compared to hand design in light of recent datapath synthesis tool advances.
And then adopt an efficient design methodology for datapath that is nimble enough to absorb late changes but not leave area/power/performance on the table
Synthesis method
  RTL coding for arithmetic datapath
  Logic synthesis
  Auto pipelining
  Timing driven placement/optimization and routing
Manual/Hand design method
  Schematic design
  Structured placement (for minimizing interconnect)
  Combinational datapath optimization for best timing
  Manual insertion of latch/flop stages
Datapath Synthesis has made several advances in last few years
  Optimized arithmetic algorithms provided as built-in IPs with the tool
  Automatic pipelining for insertion of registers and re-timing for better area/latency tradeoffs
  Exclusive arithmetic optimization techniques in tool’s datapath engine
  Support for industry standard RTL instead of proprietary custom languages
  Bringing in well established optimization methods from regular synthesis: operator merging, resource sharing and gate level sizing etc.,
Synthesis multiplier (left) and hand drawn multiplier (right), plotted to same scale.
Built-in multiplier IP synthesis component is 45% smaller than hand design.
Significant portion of the design uses many instances of same multiplier.
Adder areas are compared over bit widths of 20 – 60 bits
Synthesis built-in IPs for adders show 55 – 60% lower placed area
Note the gains are higher with high bit widths as more space wastage with alignment of cells in higher MSBs.
Arithmetic IP: Multipliers
Arithmetic IP: Adders
Efficient design space exploration by using wide variety of cells from library in synthesis (30 families) vs. limited cell usage by human designer (12 families)
Mix-n-match of area-efficient full adders/half adders/compressors with delay efficient XORs/MUXs.
Further work in optimizing sequential cell count is in progress.
  Sequential cell count tends to be higher in synthesis with auto-pipelining vs. manual pipelining in hand design.
  RTL re-coding, low level constraint directives for tool guidance etc., being explored.
Datapath Synthesis Tools
Significantly lower area with Synthesis for similar timing.
Synthesis produced area-efficient design w/enhanced library containing full adders/half adders and compressors.
Contribution of Library vs. Tool in Design Optimization
Observations on inefficiencies of hand design:
Space wastage from longer rows dictated by structured placement of cells for vertical alignment to minimize wire length
Identical cells repeated in multiple rows showing fairly limited cell family usage vs. rich usage in synthesis.
Adder bit width | Cell Area (post synthesis Area) gain | Placed area gain
20 | 33.43% | 55.11%
25 | 37.58% | 58.44%
30 | 45.41% | 61.65%
34 | 37.18% | 57.06%
51 | 40.32% | 58.83%
60 | 41.60% | 60.10%
Tool: Advances in datapath synthesis tools w/better IPs and datapath-specific optimizations
Library: 1.Wide variety of cell family selection in synthesis vs. limited selection by human. 2. Rich cell content in library to enable area-optimized cells in non-critical paths and delay-optimized cells in critical paths for synthesis.
How much Tool vs. Library?: Experiments done to determine the influence of library vs. tool in design optimization so that we can make right tradeoffs in selecting library cells.