## Slide 1: SystemC-based High-Level Synthesis of an AVC/H.264 Intra HDTV Encoder
Takayuki Onishi, Koyo Nitta,
Hiroe Iwasaki, and Kazuto Kamikura
NTT Cyber Space Laboratories
Nippon Telegraph and Telephone Corporation, Japan
DAC2010 Tuesday User Track Poster Session
2U.26 P
Notes: Thank you Mr. Chairman.
Today I would like to talk about a Multi-Reference and Multi-Block-Size Motion Estimation with Flexible Mode Selection for Professional 4:2:2 H.264/AVC Encoder LSI.

## Slide 2: Outline
Motivation and challenges for high-level synthesis of video encoders
Hardware design
  Workflow
  Timing analysis and estimation
  SystemC coding & debugging
Results
  Lines of code, verification time
Outcome
  Encoder specifications
Conclusion and future work

## Slide 3: Motivation
Encoder complexity explosion
Productivity and verification efficiency have become critical for modern video encoder development
ENC-C/-M (’95)
(HotChips7)
SuperENC (‘98)
(HotChips10)
SuperENCII(‘00)
MPEG2 H.264
SARA* (’07)
(HotChips19)
VASA (’02)
(HotChips14)
SDTV HDTV
Transistors
140,000,000
60,000,000
5,800,000
High-level design could be a lifesaver?
Effectiveness (coding overhead, verification time)
Adaptability to heavy tasks (4:2:2 12-bit HDTV video encoding)

## Slide 4: Challenges
High-level synthesis of encoder blocks working in “real-time” – no busy at the pixel input
  Larger macroblock (MB) processing loop than the decoder
  Tighter latency restrictions
Mux/Buf
Predict
Predict
Predict
Predict
Sel
DCT
Quant
De
quant
IDCT
Reconst
current pix
neighbor pix
neighbor pix
CAVLC
bits
Encoder
MB loop (< 256 cycles)
Decoder
CAVLC
bits
IDCT
Reconst
De
quant
Predict
Mux/Buf
current pix
neighbor pix
neighbor pix
MB loop (< 256 cycles)

## Slide 5: Workflow
Ref
C++
Timing analysis & estimation
FPGA
Synplify Pro
Quartus II
Cynthesizer
OSCI SystemC
Behavior Simulation
SystemC
RTL Simulation
Verilog RTL
Verilator, VCS, Cynthesizer RTL_C
Feedback
Coding

## Slide 6: Timing analysis and estimation
Analyze overall encoding operation and data flow
Determine required paralleling, pipelining and latency in each computational block to meet 256 cycles/MB as a whole
Example 1: Luma 8x8 DCT
Eight pixels input & transform per cycle
is required to achieve overall operation in 17 cycles

## Slide 7: Timing analysis and estimation
Example 2: Luma 8x8 Predict->Sel->DCT->Quant->Dequant->IDCT->Reconst
Ideal latency is estimated to be 45 cycles ( < 64 cycles required for real-time)

## Slide 8: SystemC coding
Divide reference C++ functions to sub-modules
  Advantage: Pipelined hardware synthesis, less compile time
  Drawback: Increased coding burden (headers, constructors, reset, I/O protocols)
I/Os and latency directives are set as determined by timing analysis
Some modules need deeper division and addition due to synthesis tool limitations
  Dummy input creation and dummy output elimination in order to achieve pipelined data draining
  Avoid bugs in synthesis tools
do {
wait();
} while ( conditions );
Input
Processing
Output
output stops
dummy input
output continues

## Slide 9: SystemC coding
11 sub-modules
Example: Luma 8x8 Predict->Sel->DCT->Quant->IQuant->IDCT->Reconst

## Slide 10: Results: Lines of code
Line increases mainly due to sub-module division
  (headers, constructors, reset, I/O protocols)
More advanced synthesis with no need to divide will lead to more coding efficiency
[*1] Written codes + templates
[*2] Written codes + generated codes

## Slide 11: Results: Verification speed
OSCI SystemC and Verilator are mainly used due to shorter verification time
Sub-module division may cause prolonged SystemC verification time

## Slide 12: Outcome
Video format
Color format
Color depth
Prediction
Entropy coding
Picture structure
Output format
Output bit rate
Frequency
1920x1080 59.94i
4:2:0 / 4:2:2
8 / 10 / 12 bit
Intra 8x8, 16x16
CAVLC
Field coding
AVC/H.264 ES / MPEG-2 TS
105 - 125 Mbps
Core 67.5 MHz,
Peripheral 27, 74, 81MHz
12-bit 4:2:2 HDTV AVC/H.264 Intra Encoder

## Slide 13: Conclusion and future work
Complex design of 12-bit 4:2:2 AVC/H.264 HDTV intra encoder is successful with high-level synthesis
  Division to sub-modules is required due to synthesis tool limitations, adaptability of tools to larger scale / more complex synthesis is preferred for modern encoder design
Future work may include more speed-demanding CABAC binary arithmetic coding module with SystemC design
  With higher clocking and shorter feedback loop