## Slide 1: Layout Automation in a Full-custom Design Environment
Productivity enhancement tools and investigation on OA-based flow
Yoshi Kawamura (yoshiharu.kawamura@amd.com)
Sze Tom (sze.tom@amd.com)

## Slide 2: Introduction
Layout design is a time-consuming, labor-intensive step in the processor design environment.
It is thus critical to assist layout engineers by providing various automation tools to facilitate design entry, improve quality, and accelerate time to market.
In this work, EDA vendor layout tools and in-house layout automation tools are integrated as a design cockpit. This customized design cockpit is used in AMD’s industrial full-custom microprocessor design projects.
Also, recent feasibility studies were done on OpenAccess (OA)-based flow construction using Ciranova PyCells.

## Slide 3: Customized environment for productivity enhancements
Our CAD environment uses the Cadence Virtuoso design entry tool, which provides schematic-driven layout and parameterized cells (pcell).
  On top of this environment, we customize the features and added on in-house tools developed with the SKILL programming language.
Integration of feature-rich custom pcells and auto-router integration make the platform a “design cockpit” and enhanced designer’s productivity.

## Slide 4: Customized environment for productivity enhancements (continued)
Some of productivity enhancement tools in the environment:
VXL: Schematic-driven layout creation, “’generate/select’-from-source,” Virtuoso native capability, plus AMD internal methodology overrides.
Transistor pcells: Created in-house for each process node, supports sophisticated auto-abutment and customized contacting algorithms.
Gate pcells: Gate-level pcells (inv, nand, nor as pcells), created in-house.
Via droppers and via pcells: Pcells for custom vias, and tools to drop vias automatically at the metal intersections.

## Slide 5: Customized environment for productivity enhancements (continued)
Power grid pcell: In-house custom power grid structure created as a pcell for macro internal power grid generation.
CSR device router: Automatic router, Cadence tool, and customized routing methodology integrated into AMD internal flow.
Auto decap placer: Finds white spaces and places decoupling capacitor cells.
OA database for schematic & layout (EDA vendor tool integration, export/import to connect CAD flows), PyCells (Python implementations of pcells for easier OA inter-operability)

## Slide 6: Flow for custom macro layout using productivity enhancement tools
DRC/LVS/
ERC/YRC
(Mentor Calibre)
Auto-routing where applicable. Random logic, non-timing critical nets are routed by CSR router.
DRC/LVS/ERC/YRC checks using Mentor Calibre, integrated into the design cockpit.
DRC: Design rule checks
LVS: Layout versus schematic checks
ERC: Electrical rule checks
YRC: Yield rule checks
Starting from schematic, VXL layout generation. Transistor layouts are auto-generated by pcells from schematics. Logic primitives (e.g., Inverter) also generated by gate-level pcells from schematic. Hand placement for optimal compaction. To compact the layout, the auto-abutment feature of the pcell is used, along with folding and sharing. Also, in-house auto-compactor/alignment tool is used to assist quick compaction.
Power grid is also generated by pcells and placed to hook up device power. Vias can be dropped by via dropper.
VDD
VSS
VDD
VSS
A
Z

## Slide 7: Results
Enhancements | Results
Gate-level pcells | 10 layout steps reduced to 1 step for creating most often used gates. Layout time down to seconds from minutes.
Custom power grid pcell | Instantly generates custom power grids with process, design spec, saves 1 day of hand work.
Auto decap placer | 30-sec. run saves 1 day of hand work for big macros.
CSR device auto-router | 2-min. run on custom macro saves 2 full days of hand-routing work.
Via dropper | A run of a few minutes saves more than 1 day of hand work.

## Slide 8: Investigation of an OpenAccess-based flow and its benefits
We have also explored Ciranova PyCells for better inter-operability with the OA environment and ecosystem.
PyCells are pcells based on the Python language, which can be plugged in to an OA database.
  This allows direct evaluation of pcells from applications that are OA-based.
  PyCells can also be disk-cached as evaluated pcells for those applications that do not have pcell-read capability.
Evaluating PyCells directly on OA allows us to avoid creating disk image files, and eliminates the need to worry about revision differences between current OA data and evaluated disk images, as well as saving run time and disk space.
  It is a preferable way to interact with various OA-based tools as well as internal tools.

## Slide 9: Investigation of an OpenAccess-based flow and its benefits (continued)
We replaced the described productivity enhancement pcells with PyCells and verified that all capabilities work well.
Examples of inter-operability using PyCells we investigated were:
    Standard functionality, such as gen-from-source
    CSR device router with PyCells
    Mentor Calibre run on OA designs built from PyCells
    OA database conversion to in-house database format with direct evaluation

## Slide 10: Investigation results
Each operation resulted in faster run time because no disk cache file needs to be created.
  Instead, direct evaluation of PyCells within OA-based tools simplify the CAD flow, because we no longer need to create sub-steps to export/import disk cache files of evaluated pcells, nor do we need to create LEF/DEF or GDS to connect to tools.
Also, PyCells allows EDA vendor-agnostic integrations of CAD flows because it is based on the OA pcell plug-in mechanism and is provided royalty-free from Ciranova, Inc.
Next figure shows investigated flow using PyCell and OA-database.

## Slide 11: PyCell-based OA inter-operability study
Schematic Entry
Layout Entry
OpenAccess
PyCells
CSR Router
OpenAccess
(Routed Layout)
PyCells
Calibre DRC/LVS
In-house Database Converter
In-house Database
Further constructions and optimizations

## Slide 12: Example use of the customized design cockpit Custom layouts in a six-core AMD Opteron™ processor (45-nm SOI process, 904 million transistors, 346 mm²)

## Slide 13
Trademark Attribution
AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. Other names used in this presentation are for identification purposes only and may be trademarks of their respective owners.
©2010 Advanced Micro Devices, Inc. All rights reserved.