## Slide 1: Optimizing License and Hardware Expense DAC 2010
Jarrod Stykes
02/26/2010

## Slide 2: OBJECTIVES
Optimize Corporate Hardware Deployment
  Establish HW Benchmarking For Comparisons
  Standardize HW At All Sites
  Establish Policy For HW Upgrades
Optimize EDA License Allocation
  Track Shortages And Overages
  Use Load Sharing Software To Optimize Wait Time On More Costly Licenses
Notes: January 11, 2002
8
The goal of this endeavor is to get the maximum return on investment (ROI) your hardware and license expense. To achieve this, we need to establish a means of measuring the ROI.
The quickest way to reduce License expense is to remove unused licenses. Unused licenses must be tempered by peak usage.
Another way to reduce license expense is to increase hardware expense. Running all jobs on faster hardware should result in the licenses being used less and therefore less demand for the licenses.
Hardware purchases must be tempered by the expense of continued replacement.
To address these issues, Cypress monitors metrics related to license/hardware usage as well as time waiting for jobs to run and jobs denied due to license outages.
The hardware replacement policy must be determined on an individual basis, but should be based on a consistent factor achieved from benchmarking which we refer to as CPU Factor (CPUF).

## Slide 3: Hardware VS Benchmark
Vendor 2 Cost
Based Prioritization
Core i7 CPUs
Released
non-interactive target
Pentium4 3.2GHZ: 20.6
Opteron 250: 40.6
Core2 Duo 3.16GHZ: 67.4
Xeon E5450 3GHZ: 64.1
New Hardware
Core i7 940 3.2GHz: 75.4
Sun Ultra 80: 2.6
Sun Ultra 5: 1.9
Notes: This slide shows what is available in the industry with the top blue line.
It also shows the utilization of our best hardware by various vendors’ features.
Upon tracking this metric, we prioritized an expensive feature from Vendor2 in order to achieve significant run time reductions.
The reduction in run time lead to less license demand and we were able to reduce our spending.
Hardware needs will vary for each company, but consideration should be given to getting faster processors and giving expensive features priority on those processors.

## Slide 4: Process Flow
License
Usage File
SamSuite or
FlexNet
SQL DB
HW
Bench-mark
LSF usage
data
Db Cleanup /
Metric
Generation
License Metric
Spreadsheets
Each EDA Vendor has a
WorkBook. Each WorkBook has a
sheet for each Feature.
CPUF From
Previous Slide
Internal code parses sql database
to generate metrics.
HW Wait /
HW Run Time /
License Wait
Feature Use Time / User /
Machine Ran On
Notes: January 11, 2002
3
There are 3 inputs to the process:
Raw license usage files (which are read by other software)
HW Benchmark data which provides a basis for comparing machines (CPU Factor)
LSF Usage data, which indicates how long users’ jobs sat idle waiting for hardware as well as licenses
Internal code parses the data and from these sources we know the following:
How long each job waited for Hardware
How long each job waited for License
What machine it ran on
The comparitive power of that machine (CPUF)
How long it ran on that machine
Knowing these elements we can determine all of our metrics.
The process generates a workbook for each EDA vendor with the data summarized in separate spreadsheets broken down by usage in the last: week, month, quarter, half- year and year.
Each summary page presents the number of uses in that time period and other metrics. Additionally the summary points out which licenses can be reduced or should be supplemented.
Each feature in the summary page has its own individual page with charts for more in-depth analysis.

## Slide 5: Summary Sheet
All features
from vendor
Green = Reduce
Feature Count
Clear = Good
Red = Increase
Feature Count
Periodic Summaries
Feature Details
Notes: This is a sample of the Summary sheet. The names on the left are the Features and clicking on the cell will take you directly to the supporting detail page.
At the bottom you can see there are periodic summary sheets as well as Feature detail sheets.
The summary page shows the metric data for each feature in that period.
Additionally it gives a color coded recommendation of what to do with specific feature counts:
Green means that this feature count should be reduced
Yellow indicates that investigation is required
No coloring means that the license count is just what it should be
Red means that this feature needs more licenses. Having a higher number in the max used than owned probably means of the following:
In the time interval you used to own more but have reduced that feature count
The code doesn’t understand the location of a server
The vendor has provided temporary keys at some point in the interval
The return on HWROI is used to justify prioritization or reservation of better machines for more expensive licenses. It uses available license capacity and available hardware to calculate the value of better run times through faster HW.

## Slide 6: Feature Detail Sheet 1 of 2
Summary sheet showed that we only need
12 keys for this license, here we see that
14 were needed at one time this year
Notes: The feature detail sheet contains the data for all periods of time and introduces charts that allow investigation as to why the usage may be askew.
By looking at these metrics you can observe if any license shortages are due to short term peak usage and therefore not act on the data.
For example on this license, Feature_8, our week/month/quarter/half year usage indicate we only need 12 licenses. Our year license needed indicates that we need all 14 keys that we need. Either, the last six months of use have been a period where this feature is used less or our overall usage patterns have decreased and we can eliminate two licenses for $5K savings per year.

## Slide 7: Feature Detail Sheet 2 of 2
Feature 22 was red on the ½ year summary
Page. Here we see that we removed
that license in the last month
Notes: In this case the program sees that we’ve used more keys of the feature than we have and thinks that we need to purchase more.
Instead, we’ve stopped using this feature in exchange for a comparable feature and no longer use this feature.

## Slide 8: Relative Frequency Distribution
The Relative frequency for 1 month shows we only need 34 keys
Looking over the last quarter shows we have needed 46
The summary sheet shows we’ve used as many as 50 and recommends 48
Reducing count by 7 is $35K savings
Quarterly Data
Monthly Data
Notes: January 11, 2002
3
Relative frequency distribution is the percentage of time that N licenses are used at the same time.
As with most of our metrics we track weekly, monthly, quarterly, semi-annually, and annually.
This is so we can detect temporary spikes and take corrective actions for short term issues or observe actual trends in the change of company feature usage.

## Slide 9: Cumulative Frequency Distribution
The summary page shows we own 20 copies of Feature_25 and only need 4.
Cumulative frequency shows that our usage could be met by only 4 keys in this interval.
Notes: January 11, 2002
3
The cumulative Frequency Distribution is the sum of relative frequency distribution from 0 to N, where N is the number of licenses in use at that time.
When generated over the same intervals as relative frequency this illustrates the max license usage in that interval.

## Slide 10: License Usage Over Time
For Feature_17 we own 9 and are recommended 8. But, it is coded yellow.
Usage over time shows a significant down trend in early December
After investigating, as recommended by Summary, we reduced count to 5 and saved $40K
Notes: January 11, 2002
3
License usage over time is the maximum number of licenses used per unit time over an interval of time.
This metric can be used to identify certain days or even times in the day when peak usage occurs.
Perhaps it can be related to a specific design or designer whose license usage can be improved.

## Slide 11: Wait Time Stats
Possibly the most noticed metric by the users
Targets will vary based on use model for feature
For Feature_18 we expect short runs and can’t accept more than 1s delay.
If F_18 was a long run moving to 10minute delay could save (240-210)*3.3K
= $100K
10m requires 210 licenses
1s requires 240 licenses
Notes: January 11, 2002
3
The wait time charts shows the probability that the wait to checkout a feature will be less than the time specified in the given line in the specified time interval.
For example, in the last week, with 121 licenses, you have nearly a 0% probability of checking out a license in one second or less.
However, with 121 licenses, you have a nearly 75% probability of checking out that feature in under ten minutes.
If that is acceptable delay for the feature in question, then you might be able to reduce the license count.

## Slide 12: Average Use – Hours
Need to check these users job counts, machines used, run times, etc…
Notes: January 11, 2002
13
This slide is essentially a summary of the next two slides. High averages should be verified.

## Slide 13: Average (Max) Usage Over Time
This chart shows peak use times.
In some occasions you can change usage to get better performance
In this case, we reduced licenses by averaging out the times when jobs were launched.
Peak decreases and average goes up.
Notes: January 11, 2002
3
These charts show the average number of licenses in use at a certain point in time.
The information can be used to try to get better distribution of when jobs are started.

## Slide 14: Total Number / Use
These charts help point out deviations in expected feature use model.
A user with low job count and high license usage should be investigated.
In this case we found that the user had submitted a job that was stuck in a loop
Releasing that license improved our wait times.
User HSX has run a small number
of jobs and used a large amount
of license Time
Notes: January 11, 2002
13
This shows the number of times a user has used this feature in the last time interval.
Users with high counts may benefit from guidance to use the feature more efficiently, thus reducing demand.
In conjunction with the previous slide, this slide shows heavy use of the feature.

## Slide 15: H/W Efficiency
Likely ran on a machine that
didn’t have a CPUF in the
database
These users should utilize better HW. In another feature we were
able to remove one key by forcing the feature onto faster HW.
Notes: January 11, 2002
3
Chart indicates those users who if ran with better H/W would make a significant reduction in the time they have the license key checked out.
If your metrics indicate that you are short of licenses, then these users should be convinced to run their jobs on better machines.
Most likely the user showing 0 HW Efficiency are on machines not registered with the program, therefore their CPUF is nil.
For inexpensive licenses, this metric may not be a concern.
For expensive licenses, below 0.7 should be corrected