## Slide 1: 200X Combinational Scan Compression Enabler For Test Cost Scaling
<number>
Peter Wohl – peter.wohl@synopsys.com
Frederic Neuveux –frederic.neuveux@synopsys.com
Synopsys R&D
Sarveswara Tammali – sarvesh@ti.com
Rajesh Gottumukkala – rajesh.g@ti.com
Wireless Design, Texas Instruments, Bangalore

## Slide 2: Outline
<number>
Goal
200X Compression Architecture
  Dual Codec
  Other Architectural features
Challenges
Hybrid ATPG exploration
  Protected by provisional patent application
X-source root-cause analysis
Results
Conclusions

## Slide 3: Goals and Means
<number>
Goal: Test cost scaling with die cost
  New fault models (SDD, Path delay and bridging)
  Higher compression required
  200X compression with combinational DFTMAX
Challenges encountered:
  Implementing 200X compression
  Default X-tolerant configuration on X-clean design
Solutions developed:
  Hybrid ATPG methodology
  X-source analysis and X reduction

## Slide 4: DFTMAX Architecture
<number>
XOR unload compressor
MUX load decompressor
Load mode
controls
Shift data inputs
Default X-Tolerant
DUT
(unchanged)
XOR unload compressor
MUX load decompressor
Load mode
controls
Shift data inputs
DUT
(unchanged)
unload
control
Unload enable
decode logic
AND unload selector
Fully X-Tolerant
8 inputs, 8 outputs  max 1024 chains
VTS 2007
ITC 2007

## Slide 5: DFTMAX Codec Configuration for 200X Compression on Video Core
<number>
Design statistics
  240K flip-flops
  70 SRAMs
  6 million gates
  45 nm technology
Dual Codec Configuration:
200X – Default X-tolerant
100X – Fully X-tolerant
Area overhead
  0.3%
Congestion impact
  DC-Topographical based codec generation used to help congestion

## Slide 6: Impact of X’s on Compression- X-Tolerance Benefits
<number>
Table-1: Stuck-at Test Coverage read point = 99.28% (Codec faults removed) |  |  |  | 
Test | Chain length | Patterns | Test coverage (max) | Benefit (-loss)
100X full XTOL | 257 | 3392 (5074) | 99.28 (99.34) | 
200X default XTOL | 142 | 7694 | 99.28 | -25.3%
Table-2: Stuck-at Test Coverage read point = 98.98% (Codec faults included) |  |  |  | 
Test | Chain length | Patterns | Test coverage (max) | Benefit (-loss)
100X full XTOL | 257 | 3584 (5095) | 98.98 (99.03) | 
100X default XTOL | 257 | 5037 | 98.98 | -40%
Conclusion: 100 X full XTOL gives better compression

## Slide 7: Key Observations
<number>
Performance of X-tolerance ATPG is superior to default X-tolerance even with only 9 X-sources
  40% pattern inflation in 100 non X-tol over 100X X-tol
  25% pattern inflation in 200 non X-tol over 100X X-tol
Two option are pursued based on results
  Hybrid ATPG
  X source analysis to reduce Xs

## Slide 8: Hybrid ATPG Exploration
<number>
Hybrid ATPG can also be called as multi-compression ATPG
Coverage crossover Definition
  Test coverage that is achieved with minimal tester cycles using the first codec (200X default XTOL) and is the right coverage point to switch over to the other codec (100X full XTOL) to achieve best test time overall
ATPG run1
(200X default XTOL)
atpg(testcoverage1,testtime1)
ATPG run2
(100X full XTOL)
atpg(testcoverage2,testtime2)

## Slide 9: Coverage Cross-over Point
<number>
Hybrid ATPG is better than either of 100X alone or 200X alone ATPG
Even with small number of X sources, 100X is doing better than 200X
  9 R14 violations (X-sources)
  1 R15 violations (unblockable X-sources)
Multiple ATPG runs to determine optimal coverage cross-over point
  97% for stuck-at run
  90% for TFT run

## Slide 10: Test Time Benefits of Hybrid ATPG
<number>
Compression architecture | Test coverage | # scan patterns 100X | # scan patterns 200X | Test and data reduction
Stuck-at ATPG (Coverage cross-over point = 97%) |  |  |  | 
100X full XTOL | 99% | 5568 | - | -
100X + 200X hybrid | 99% | 2496 | 2177 | 33%
Transition Fault ATPG (Coverage cross-over point = 90%) |  |  |  | 
100X full XTOL | 92.2% | 30747 | - | -
100X + 200X hybrid | 92.2% | 14648 | 23713 | 10%

## Slide 11: Hybrid ATPG - Observations
<number>
Suitable for designs with X-sources
Coverage cross-over is identified based on multiple run results
  Work in progress to identify ideal cross-over from ATPG log file
Percentage gains of test time reduction on TFT run is lower than stuck-at run
  33% stuck-at run
  10% TFT run
Effort of hybrid ATPG may be high in pattern validation, silicon bring-up, silicon debug

## Slide 12: X-Source Root Cause Analysis in Tetramax
<number>
After run_drc, you can invoke X chain analysis
TEST-T> analyze_compressor –xchain_analysis
Chain = 11 #cells =121 avg_x_capture_probability =0.83 (1 X-cells, first_id= 3983086, x_prob= 100)
Chain = 13 #cells =80 avg_x_capture_probability =1.25
(1 X-cells, first_id= 3962117, x_prob = 100)

## Slide 13: GUI Based Debug of X-sources
<number>

## Slide 14: X Sources Due to Pipeline Flops
<number>
Pipeline flops
Pipeline flops
Tetramax pipeline modeling controlled through command
  set_simulation –pipeline_cell: simulates pipeline flops
  May fail parallel VCS simulation (pipeline flops simulated as X)
Internal scan chains are of two categories
  Core chains
  Core wrapper chains
Core wrapper chains remain in shift mode during capture due to input bounding
  Captures Xs in first flip-flops of core wrapper chains
Core chains
Core wrapper
chains

## Slide 15: Results of 200X Compression After Fixing X-Sources
<number>
Compression architecture | Test coverage | # scan patterns | Chain length | improve- ment
Stuck-at ATPG |  |  |  | 
100X full XTOL | 99% | 5120 | 257 | -
200X default XTOL | 99% | 5568 | 142 | 40%
Transition Fault ATPG |  |  |  | 
100X full XTOL | 92.28% | 27247 | 257 | -
200X default XTOL | 92.28% | 41706 | 142 | 15%
There is no coverage loss in 200X default XTOL over 100X full XTOL
Overall test time and hence test cost reduction due to 200X on this design is ~20%

## Slide 16: Theoretical Vs Achieved Compression
<number>
Compression architecture | Test coverage | # scan patterns | Chain length | Test and data reduction
Stuck-at ATPG run |  |  |  | 
1X | 99% | 4103 | 27565 | 1x
100X full XTOL | 99% | 5120 | 257 | 86x
200X default | 99% | 5568 | 142 | 143x
Transition Fault ATPG |  |  |  | 
1X | 96% | 22298 | 27565 | 1x
100X full XTOL | 96% | 26258 | 257 | 80x
200X default | 96% | 45279 | 142 | 95x
Highest achieved compression is much lower in transition fault ATPG than stuck-at ATPG (95x vs. 143x)
Number of patterns in transition fault ATPG is typically 3x-5x of stuck-at patterns
Hence architecture trade-off (area, congestion, effort ) vs. test time gains should be done based on transition fault ATPG

## Slide 17: Optimal Compression Architecture
<number>
Design and implementation dependent
  Must be analyzed early.
Tool should analyze design and optimize compression architecture
  User inputs
    External input/output channels (tester channels)
    Range of internal core chains
    Scan replaced netlist
    Fault model ( can be multiple)
  Outputs should be compression codec configuration
    Optimal number of internal core chains
    Toggle activity in shift and capture (Indicative of power)
Work in progress on this feature

## Slide 18: Conclusions
<number>
Designs with Xs: Full X-Tolerant outperforms default X-tolerant
  Even few Xs impact QoR in high compression (>100X)
X-clean design: Default X-tolerant preferred
Hybrid approach
  Significant test time benefits in designs with Xs
  Multi-codec configuration
  Coverage cross-over point is key
X-source analysis helps achieve best results
Architecture trade-offs (area, congestion, effort )
  Based on transition fault ATPG
  Automate optimal compression analysis