## Slide 1: Using Calibre PERC for Full-Chip Detection of Unintentional Forward-Biased Diodes
Amir Grinshpon
Amir.Grinshpon@freescale.com
Adam Segoli Schubert
Adam.SegoliSchubert@freescale.com
Ziyang Lu
Ziyang_Lu@mentor.com

## Slide 2: Outline
Slide <number>
Introduction – Problem’s scope and Challenges
Hierarchical Verification using PERC
Multi-Stage Filtering
Results
Conclusions

## Slide 3: Outline
Slide <number>
Introduction – Scope of the Problem and Challenges
Hierarchical Verification using PERC
Multi-Stage Filtering
Results
Conclusions

## Slide 4: The Detection of Unintentional Forward-Biased Diodes
Unintentional forward-biased diodes can lead to:
Power leakage
Malfunction of the chip
The detection of such a condition is a very challenging task, especially on full chips. Therefore, an in-house solution would be:
Expensive
Time-consuming
High percentage of failure to perform a full chip analysis
Slide <number>

## Slide 5: Circuit Diodes
Slide <number>
A silicon P-N junction

## Slide 6: Forward-Biased Diodes in a Mux Cell
Slide <number>
Nmos mM8:d (xb) voltage can be lower than mM8:b (d0b)
Pmos mM7:b (d0b) voltage can be lower than mM7:d (xb)
Nmos mM9:d (xb) voltage can be lower than mM9:b (d1b)
Pmos mM10:b (d1b) voltage can be lower than mM10:d (xb)

## Slide 7: Detecting Unintentional Forward-Biased Diodes
Slide <number>
Verify that all diodes are “turned off” during the functional operation of the design

## Slide 8: What Needs to be Checked?
Slide <number>
Verify that the following conditions are always met:
S
G
D
B
B ≤ S AND B ≤ D
G
D
B
S
B ≥ S AND B ≥ D
A
C
A ≤ C
1. Intentional Diode Device
3. NMOS diodes
2. PMOS diodes

## Slide 9: Challenges
Slide <number>
Detecting if forward-bias can occur is a complex problem:
Several voltage levels can be propagated to the same terminal of a device.
Difficulty in determining which of the scenarios are logically valid.
The problem is NP-complete
Logical pruning can be reduced into the Boolean satisfiability problem.
mp1
mn2
mn1
Transistor mn2:
The bulk net can be at VDD
The source can be at GND
Can a forward-bias occur?

## Slide 10: Outline
Slide <number>
Introduction – scope of the problem
Hierarchical Verification Using PERC
Multi-Stage Filtering
Results
Conclusions

## Slide 11: PERC – Programmable Electrical Rule Checker
Slide <number>
Mentor’s Calibre® PERC is an integrated schematic/layout verification tool. It provides a TCL API layer, with an infrastructure for implementing topology-based checks.
The key features, critical to our work include:
    Hierarchical processing - for full-chip capacity
    Net types - for defining pad voltage sets
    Path types - for propagating voltage sets
    Netlist traversal - for logic pruning
Results are highlighted on the schematic/layout

## Slide 12: Signature-Based Hierarchical Approach
Slide <number>
PERC computes cell placement signatures for every cell in the design.
A cell placement signature describes the characteristics of a cell placement.
For each cell in the design hierarchy, PERC finds all of its placements and computes their signatures.
For each unique signature, PERC picks a placement in the highest level of the design hierarchy as its representative.
Instead of analyzing all the flat instances, PERC only examines the representative cell placements.

## Slide 13: Outline
Slide <number>
Introduction – scope of the problem and challenges
Hierarchical Verification using PERC
Multi-Stage Filtering
Results
Conclusions

## Slide 14: Multi-Stage Filtering to Identify Forward-Biased Diodes
Slide <number>
mp1
mn2
mn1
Filter 1
The first filter uses the pre-set Propagated Sets. Considering the constraints defined in the preceding section, we iterate over all potentially erroneous devices and filter out those that under no circumstances might be at a forward-biased state.
Transistor mn2:
The bulk net can be at VDD
The source can be at GND

## Slide 15: Multi-Stage Filtering
Slide <number>
mp1
mn2
mn1
Filter 2
Inspect the Propagated Set, taking into consideration some logical constraints. For every possible erroneous device detected by Filter 1, we perform two independent traversals, one from each device terminal to the voltage source origin. As the traversal progresses, we set logical values on the traversed nets and on their adjacent nets.

## Slide 16: Multi-Stage Filtering
Slide <number>
mp1
mn2
mn1
Filter 3
The traversals from devices’ terminals to the voltage source origins are performed simultaneously, assuring that both paths can indeed co-exist.
Logical Conflict

## Slide 17: Two-Step Rule Checking with Calibre PERC
Single rule approach is not practical: Calibre PERC would apply Filter 2 and Filter 3 on too many devices, increasing the number of required netlist traversals.
We code the filtering mechanism into two PERC rules. While each rule has the same basic functionality (applying the three filters to each device), they have different path traversal policies.
Slide <number>

## Slide 18: Two-Step Rule Checking
First Rule:
Calibre PERC checks devices cell by cell. Whenever the traversal reaches a cell's boundary port, it stops and refers to it as a voltage source origin based on its preset Propagated Set. This hierarchical mode runs fast and filters out the majority of devices. Any devices failing the filters in the first rule are saved into a lookup table, to be checked again in the second rule.

## Slide 19: Two-Step Rule Checking
Second Rule:
Calibre PERC runs the filtering with the whole chip traversal policy, but only checks the (small number of) devices stored in the lookup table.
Hashing: whenever a net is traversed, we form a key that captures the current combined logical values assigned. If the same net is hit again, the traversal can skip it if it has already been visited under the same logical assignments
Lookup Table
Device 1
Device 7
Device 23
Device 40

## Slide 20: Outline
Slide <number>
Introduction – scope of the problem and challenges
Hierarchical Verification using PERC
Multi-Stage Filtering
Results
Conclusions

## Slide 21: Results
Slide <number>
Design | # Devices | CPU runtime (hh:mm:ss) | # Violations
Analog Block A | 403,206 | 00:00:59 | 12
Analog Block B | 207,780 | 00:00:61 | 19
Analog Block C | 1,181,050 | 00:23:05 | 12
Network Processor | 121,235,846 | 02:11:36 | 44
Application Processor | 48,946,987 | 02:15:26 | 357

## Slide 22: Outline
Slide <number>
Introduction – scope of the problem and challenges
Hierarchical Verification using PERC
Multi-Stage Filtering
Results
Conclusions

## Slide 23: Conclusions
Slide <number>
We presented a practical approach for full chip analysis of unintentional forward-biased diodes using Calibre PERC. Our work shows that, with some creativity, one can use Calibre PERC to solve complex circuit analysis problems. As a result, it reduces the need to build custom in-house tools from scratch, enabling better use of company resources.