## Slide 1: A Practical Approach to Thermal Modeling and Validation of 3D ICs
Miroslav Cupak1, Herman Oprins1, Geert Van der Plas1, Pol Marchal1, Bart Vandevelde1, Adi Srinivasan2, Edmund Cheng2
1 IMEC vzw, Leuven, BELGIUM 2 Gradient Design Automation Inc., Santa Clara, CA, USA
Thermal Simulation Methodology
Introduction/Motivation
Conclusions
Increasing power density in transistors and ICs
  Miniaturization of components
  Increasing proximity of heat-generating components
Power dissipation might lead to excessive temperature
  Degraded electrical performance and reliability
Thermal challenges become even worse for 3D
  Vertical integration of different layers
  Use of poorly conductive materials
  Thinned stacked dies
  TSVs, Cu nails, complex interconnection
Verify thermal distribution at fine granularity
1
2
3
4
5
6
Two different physical length scales
Perform detailed simulation in die stack only
Use macro model for region outside die stack
Package model extraction options
  Thermal resistance values from data sheets
  Extract from thermal FE model of package and board
Create a “thermal tech file”, specifying for each layer
  Layer thickness
  Thermal properties
  Temperature dependent properties
New IC electro-thermal simulator
Adaptive resolution to match device scale
Based on detailed design file (layout, power)
Loosely coupled electric – thermal analysis
Steady state, transient
Extending simulation technology to 3D layer stack
2D to 3D layout translation
Thermal analysis data preparation
Thermal Simulation Results
1
Simple model
Rtot = 21.44 K/W
Rbot = 24.67 K/W
Rtop = 351.5 K/W
Rfront= 649.7 K/W
Rback = 649.7 K/W
Rleft = 649.7 K/W
Rright = 649.7 K/W
2
3
4
5
6
DAC 2010 User Track, June 15th, 2010.
Methodology and tool available to perform detailed thermal analysis of 3D-ICs
  Including TSVs, BEOL and interconnection between dies
  Compatible with existing design flow
Demonstrated on a two stacked die structure in a BGA package
Results validated with silicon
Region for detailed thermal simulation
Abstracted part -> package model
50 x 50 µm² heaters
100 x 100 µm² heaters
no TSVs
11 x 11
7 x 7
[source: Gradient DA]
no TSVs
11 x 11
7 x 7
Validated with chip measurements
BGA type package
Discretized approach with multiple solvers
Steady state thermal analysis
Parameterized Resolution (0.1 µm ; 0.05 °C)
Ambient temperature (27°C)
Top die: thickness 25 μm, TSVs
Bottom die: thickness 250 μm
Full 3D FE model of the package and PCB
Representation of the boundary conditions applied on the simulation domain
7x7 TSV array with heater and monitors
Validation of temperature in diodes in Si
Good agreements between simulations and experiments