## Slide 1
<number>
Leveraging Formal Techniques for Packet Based Designs
B. A. Krishna (FV)
Chelsio Communications Inc – bkrishna@chelsio.com
Anamaya Sullerey (Design)
Chelsio Communications Inc – anamaya@chelsio.com
Alok Jain (CAD)
Cadence Design Systems – alokj@cadence.com
Design Automation Conference 2010
Notes: <number>
www.chelsio.com
<number>

## Slide 2
<number>
Verification alternatives at ASIC block level
Traditional approach
  Block level DV/simulation
  Only specific modules FV’ed based on feasibility
  Short-comings:
    Lack of confidence in coverage
    DV insufficient to prove lack of starvation etc.
Our approach
  FV primary verification tool for increased confidence
  Start early, influence design & “End to End” FV
  Allow DV to happen in parallel
  Goal - generate proofs & find all issues using FV
  Compare results across FV/DV
Overview
Notes: <number>
www.chelsio.com
<number>

## Slide 3
<number>
Block is a L2 ethernet packet switch
Block is fairly big, of high complexity ~ 650k gates
Motivation for FV:
  critical IP – in middle of ASIC data path
  components require liveness (unbounded in time) guarantees
  components have FIFOs with no backpressure mechanism
Design consists of 18 modules, 14 (most complex) FV’ed
Overview
Notes: <number>
www.chelsio.com
<number>

## Slide 4
<number>
Typical FV challenges
Reachable state space too large
  Can properties be made tractable under model checking?
Confidence in legality of assumptions and assertions
  Are our assumptions exhaustive and not over-constrained?
Composing sufficient assertions
How do we address these?
Start design/FV collaboration early
Influence design to render logic cones tractable
Iterate between designer/FV to obtain rigorous specs
Use FV/design insights to abstract away design complexity
Overcoming FV hurdles
Notes: <number>
www.chelsio.com
<number>

## Slide 5
<number>
Block’s design guide-lines
Make modules highly parameterized
Careful Interface Design
  Clear/Crisp Interface definitions
  Logically and temporally simple transaction rules
  Handful of assertions should capture all functionality
Isolate components with ‘liveness’ guarantees
Isolate components with FIFO characteristics
Breakdown Architectural invariants into module level assertions
Reuse code (e.g., Free List Manager, arbiters, aligners )
Iterate on interface spec until deemed rigorous
Re-partition design based on Formal tractability
Designing for Formal
Notes: <number>
www.chelsio.com
<number>

## Slide 6
<number>
The Page Manager Module
Manages pages associated with packets on Rx path of L2 Ethernet switch
Supports high level switch primitives
  Allocate, Enqueue, Duplicate, Dequeue & Discard
Consists of
  Free List Manager (Maintains list of free pages)
  Life Count Memory (Reference count on a per page basis)
Why this case study?
Very ‘stateful’ since state maintained per page
Exhibits ‘liveness’ (behavior not bounded in time)
Critical component – failures can cause hang or data corruption
FV technique uses manual abstraction to avoid state explosion
Such modules often classified as un-FV’able
Case Study
Notes: <number>
www.chelsio.com
<number>

## Slide 7
<number>
Input/Output sequences
Input: Allocate
Input: Enqueue (Lcnt:={1,2,3})
Input: Deallocate (Lcnt decremented)
...
Input: Deallocate (Lcnt decremented)
Output: Page Free (Lcnt := 1->0)
Path1:
Alloc, ENQ(lcnt=1), DLC, Free
Path2:
Alloc, ENQ(lcnt=2), DLC, DLC, Free
Path3:
Alloc, ENQ(lcnt=3), DLC, DLC, DLC, Free
Enqueue: Lcnt initialized to: {1,2,3}
Dequeue: Lcnt value read
Dealloc: Lcnt is decremented
Free: Lcnt goes from 1->0
Page Manager
Notes: <number>
www.chelsio.com
<number>

## Slide 8
<number>
Free List Manager Assertions
Page once allocated, will not be reallocated, until freed (safety)
All page allocation requests will eventually be satisfied (liveness)
Input constraints
All outstanding allocated pages will eventually be freed (fairness)
/* Properties in LTL notation */
pg_i_alc := (alloc_srdy & alloc_drdy & alloc_pgnum=i);
pg_i_free := (free_srdy & free_drdy & free_pgnum=i);
assert G (pg_i_alc -> F (!pg_i_alc U pg_i_free));
assert G (alloc_srdy -> F (alloc_drdy));
assume G (pg_i_alc -> F (pg_i_free));
FV Strategy – first verify Free List Manager
Notes: <number>
www.chelsio.com
<number>

## Slide 9
<number>
What’s an abstraction?
Entity/Representation replacing design component
Abstraction exhibits “super-set” behavior but less stateful
Proof using abstraction holds for replaced RTL
How to abstract away state in Free List Manager?
Focus on the life of a single page
Study single page’s life, all other page activity just “noise”
A
Foo
Bar
B
C
D
E
{0,1}
How to ‘Abstract’ away Statefulness
Notes: <number>
www.chelsio.com
<number>

## Slide 10
<number>
Abstraction’s Characteristics
Environment maintains the notion of a magic Page
Abstraction maintains state only for magic Page
Utilize magic Page state to determine behavior
  magic Page is allocated, allocate (random page)
  magic Page isn’t allocated, allocate (random page != magic Page )
Behavior is a superset of the actual Free List Manager
How is magic Page generated?
Randomly set by env. at reset & kept rigid within path
Assertions study life of only magic Page, ignoring other pages
Free List Manager Abstraction
Notes: <number>
www.chelsio.com
<number>

## Slide 11
<number>
ALCD
IDLE
LCNT3
LCNT2
LCNT1
ERR
INJ ALLOC
RCV magicPage
INJ ENQ (LCNT=3)
INJ ENQ (LCNT=2)
INJ ENQ (LCNT=1)
INJ DEALLOC
INJ DEALLOC
INJ DEALLOC
RCV Free
INJ DEALLOC
!RCV Free
Magic Page Lifecycle
Notes: <number>
www.chelsio.com
<number>

## Slide 12
<number>
The FV scaffolding, putting it all together
Notes: <number>
www.chelsio.com
<number>

## Slide 13
<number>
Assertions cast in terms of trkState (in LTL notation)
  /* We should never be in ERROR state */
  assert G ( trkState!=ERROR);
  /* We’re in IDLE and allocated magic page -> goto ALC state */
  assert G (
  (trkState=IDLE & alloc_rsp & alloc_pgnum=magicPage) -> (trkStateNxt=ALC)
  );
  /* We’re not in IDLE state and (re)allocated magic page -> goto ERROR */
  assert G (
  (trkState!=IDLE & alloc_rsp & alloc_pgnum=magicPage) -> (trkStateNxt=ERROR)
  );
  /* We’re in LCNT1 state and issue a dealloc for magic page -> goto IDLE and see free */
  assert G (
  (trkState=LCNT1 & dlloc_rsp & dlloc_pgnum=magicPage) -> (trkStateNxt=IDLE & free_valid & free_pgnum=magicPage)
  );
Examples of assertions used
Notes: <number>
www.chelsio.com
<number>

## Slide 14
<number>
Data-Independence
Control signals not derived from data contents
Proved integrity of FIFO type modules by using Wolper’s Theorem
Manual Abstractions/Refinements
Replaced stateful sub-modules with abstractions
  E.g. RRA/Free List Manager replaced with abstractions
Exploit symmetry for data-type reduction
Symmetry: any 2 values of this type => semantics identical
Proofs against “reduced” (protocol model) design
  E.g. FIFO - data-integrity can be proven for a reduced depth
General FV techniques used
Notes: <number>
www.chelsio.com
<number>

## Slide 15
<number>
FV effort started alongside design and lasted 6 months
Average module level FV proof run-time ~ 1 hour
Average number of assertions per module ~ 15-20 properties
The 3 bugs found in DV, slipped through FV
  Missing properties
  Incorrect assumptions (constraints too tight)
No bugs found later in emulation/bring-up
FV’ed block first to withstand significant data-integrity
FV’ed deemed tape-out ready 2+ months before other blocks
Verification Platform | # Bugs found
FV | 55 (52 critical + 3 non-critical)
DV simulation | 3 (3 critical + 0 non-critical)
Emulation/Bring-up | 0
Results
Notes: <number>
www.chelsio.com
<number>

## Slide 16
<number>
Future Work (model checker improvements)
Abstractions need to be proven “sound”
Data-Independence needs to be proven
Data type reduction safety check
Limitations
This isn’t a silver bullet!
  White-box study required to deduce abstractions – risks bias
  Module level FV sensitive to interface changes
  Very good cooperation needed between Design/DV
  Design Experience needed for Verification Engineer
Future Work and Limitations
Notes: <number>
www.chelsio.com
<number>

## Slide 17
<number>
“The use of clean, debugged components saves much more time in system testing than that spent on scaffolding and thorough component testing”
- Frederick P. Brooks Jr, “Mythical Man Month”
FV done early, can serve as ‘first line of defense’
Debugging FV failures at module level very efficient compared to DV
  FV Engineer could root-cause analyze in ~ 5-10 minutes
  Design Engineer confirmed/denied analysis
Cost-effective when FV is integrated into the design flow early
  FV’ed block first to be deemed robust
  Proven FV reference models serve as concrete specs
Overlap between FV/DV always good
Summary
Notes: <number>
www.chelsio.com
<number>

## Slide 18
<number>
DAC organizers, for this forum
Asgeir Eiriksson, CTO, Chelsio Communications
Bin Ju and the Cadence IFV team, tools support
Thank you!
Notes: <number>
www.chelsio.com
<number>