## Slide 1: Logic Modeling and Formal Equivalence Checking of Analog-based Design
Moshe Emmer
moshe.emmer@intel.com
Microprocessor and Chipset Development, Intel Architecture Group, Intel Corporation
DAC 2010 User Track

## Slide 2: Agenda
Motivation
Methodology & Flow
Design Example
Results
Summary
<number>

## Slide 3: Motivation
1. Microprocessor design becomes more similar to System-on-a-chip (SoC) design
  Multiple cores, many traditional off-chip features are implemented on-chip (e.g. memory controllers, graphic engines)
  Significant enlargement in the amount of I/O design cells on the chip (DDR channels, PCIE lanes/links)
   The usage of analog-based design (with digital control) has increased proportionally
2. Traditional handling of analog-based design:
  Abstract artificial RTL description is simulated in pre-silicon RTL verification environment
  black-box in the formal equivalence checking flows
   Verification hole, the actual behavior is never checked
<number>
1 & 2  Risk for verification hole consistently increases
 A new methodology for handling analog-based design in the front-end environment was developed

## Slide 4: Stage 1: Define circuit building-blocks
<number>
I/O design circuit cell
Analog-based
Circuit
building block-1
.
.
.
.
.
Analog-based
Circuit
building block-2
Analog-based
Circuit
building block-n
Notes: I/O analog-based design cells are hierarchically built in circuit
These cells are multiply-instantiated, containing small common analog-based building blocks:
Level-shifters, differential Amplifiers, pull-up/pull-down drivers
<number>

## Slide 5: Stage 2: Write RTL descriptions
<number>
I/O design circuit cell
Analog-based
Circuit
building block-1
.
.
.
.
.
Analog-based
Circuit
building block-2
Analog-based
Circuit
building block-n
RTL module
block-1
RTL module
block-2
RTL module
block-n
Logic modeling (RTL module per building block)
(for each building block)
.
.
.
.
.
Notes: Logic modeling: A low-level, high-detailed RTL module is manually written (in Verilog, using 4-value semantics) for each of the building blocks to describe its functional behavior.
Must be zero-delay RTL (PLLs and ring-oscillators are outside our scope)
<number>

## Slide 6: Stage 3: Formally verify building-blocks
<number>
I/O design circuit cell
Analog-based
Circuit
building block-1
.
.
.
.
.
Analog-based
Circuit
building block-2
Analog-based
Circuit
building block-n
RTL module
block-1
RTL module
block-2
RTL module
block-n
Formal Equivalence Checking
Verilog RTL vs. SPICE circuit
(using an EDA vendor tool)
(based on symbolic-simulation techniques)
.
.
.
.
.
Notes: Each of the RTL modules is formally verified against the real SPICE circuit of the building block using an EDA vendor tool (based on symbolic-simulation techniques)
<number>

## Slide 7: Stage 4: Formally verify top-level I/O cell
<number>
I/O design circuit cell
Analog-based
Circuit
building block-1
.
.
.
.
.
Analog-based
Circuit
building block-2
Analog-based
Circuit
building block-n
RTL module
block-1
RTL module
block-2
RTL module
block-n
I/O design RTL module
.
.
.
.
Formal Equivalence Checking
Verilog RTL vs. Verilog netlist
(all Analog blocks are black-boxed)
To pre-silicon RTL environment for logic simulation
Notes: A top-level RTL module is written and formally verified against the top-level SPICE circuit (all internal building-blocks are black-boxed).
The new RTL module is used for RTL simulations
<number>

## Slide 8: I/O DDR Output-Buffer: Top-level circuit
Traditionally, the whole Output-Buffer was black-boxed
<number>

## Slide 9: The Actual driver (analog-based design)
Split to pull-up and pull-down drivers
<number>

## Slide 10: The Pull-up driver, top-level
<number>
Analog level-shifter
Drivers
ODT
Notes: ODT – On Die Termination
<number>

## Slide 11: A single pull-up driver
<number>
Analog level-shifters

## Slide 12: The analog level-shifter (building block)
Matching RTL module:
Additional constraint:
<number>
module x8cppuppredrvbit (in, outhv, pwrnotgood, s3onb, vcc1p1xx, vccddq);
input in, pwrnotgood, s3onb, vcc1p1xx, vccddq;
output outhv;
assign outhv = (vcc1p1xx & s3onb) ? ~in : (((~vcc1p1x | vcc1p1xx & pwrnotgood & ~in) & ~s3onb) ? 1'b1 : 1'bz);
endmodule
No_Contention_During_Powerup: $forbidden(vcc1p1xx & pwrnotgood & in);
Notes: <number>

## Slide 13: Results
The verified RTL descriptions of all I/O buffers were assimilated in the pre-silicon RTL environment
RTL simulation revealed a real design bug in the I/O reset-buffers
  There was a real logical contention inside the level-shifters of the I/O reset-buffers
  This bug could not be found in any other design activity
  It would have resulted in a fatal silicon bug
  Few design bugs were found and DDR channel architecture was revised following the functional behavior of its I/O buffers in the RTL environment
Using the new methodology, we were able to see the how the ODT (on-die termination) affects the DDR channel (during a normal read transaction)
  In the past: Z  Driver drives the bus  Z (end of transaction)
  Now: Z  X (ODT is on)  Driver drives the bus  X (ODT again)  Z (end of transaction)
<number>

## Slide 14: Summary
Analog-based design is a significant challenge to the FE design world
  Traditional approach: “ignore” this design type in the front-end flows (using dummy abstract RTL modules and black-boxes)
A new methodology for logic modeling and formal equivalence checking for analog-based design was developed
  Full and accurate RTL description of these design blocks
  Pre-silicon logic verification activity of I/O design is significantly improved
  Complex analog design (e.g. PLLs, ring-oscillators) is not covered here
This methodology was successfully used as part of a highly integrated CPU design at Intel
  Considered as an integral part of the RTL design work in the I/O teams
The flow is currently built using a specific EDA vendor tool, but can be in-use with other vendor tools
  The methodology itself is independent of the tools
<number>
Analog-based design in the front-end environment:
Not necessarily a black-box!

## Slide 15: Q&A Thank You