## Slide 1
Formal verification of multi cycle overrides on a
Graphics chip
Chunduri R Mohan(chunduri.r.mohan@intel.com)
  ASDG HIP team, Intel corp, Folsom, CA, USA
Vadivel Ramalingam(vadivel.ramalingam@intel.com)
Bharathi V(v.bharathi@intel.com)
Sreejith Pillai(sreejith.pillai@intel.com)

## Slide 2
Types of MCPs
Risk of an MCP failure to silicon
Flow for Formal verification of MCPs
Analysis of various types of MCPs by the formal tool
Results
Improvements required

## Slide 3: Types of MCPs
- Unit level, partition level or full chip level MCPs

## Slide 4: Why MCPs
As the chipset/integrated graphic designs moved from 90nm to 65nm and then to 45nm, number of MCPs have gone up by nearly 6x
Primary causes for increase in MCPs
  Need for multiple performance modes
  Complex IOs and provision for meeting various board specs
  Support for legacy modes
  More globalized clock crossings
  Use of inter-unit cross clock config signals
Key message – As guidelines to define an MCP are becoming tighter for a designer, need for formal methods to verify an MCP defined at partition/unit level was clearly identified

## Slide 5: Impact of MCP failure to silicon : one real example
Nature of design: integrated graphics design with mix of control and datapath logic.. Around 16Mgates
MCP
set_multicycle_path -setup 4 -start -to [ get_cells sunit1/sunit_io1/io_hhsclkgatefub/ggvhiox4clk*_gate*/rtl_gate* ]
Silicon violation
  Setup timing violations of upto 1ns were observed in silicon on vhiox4clk
Rootcause
Since start point is not specified in the MCP, it got applied to all three source clock domains(hclk, hrawclk and vhiox4clk). The designer did not intend it to be applied to vhiox4clk
PV with the MCP had a positive 1800ps margin but had a negative 1012ps margin after removing it
Impact
Re-synthesis was not possible as the project was in a late stage
Ended up with a late fix with some schedule impact
Key message – Some of the MCP failures, particularly those that get
incorrectly applied between partitions, are observed on the silicon
very late in the project cycle and have huge impact

## Slide 6: Methods to address MCP problems
Reduce the MCPs where possible
  Re-structure logic, add flops, duplicate config bits
  Trade-off some gatecount where applicable
Manual reviews
  Uarchitect reviews of the MCP
    Is it really an MCP ? What makes it an MCP etc
    Have a checklist prepared for an MCP review
Simple rule based checks on RTL
    Identify high risk MCPs by expanding clock domains, expanding wild cards, identifying overlapping MCPs etc
Assertion based verification
    Extract assertions for an MCP and run them through RTL simulations
Complete formal verification of the MCP

## Slide 7: MCP Verification Flow through formal method
Constraint Verification
Architecture
Full-Chip
RTL
Unit-Level
MCPs
Constraint Promotion
Chip-Level
MCPs
Full-Chip
Clocks
HTML Debug
Environment
Notes: <number>

## Slide 8: Fast to Slow Clock Multi-Cycle Paths
Clock Gen.
Control Logic
2xclk
clk
clk
1
0
Fast clock launches data
Fast clock holds data
Slow clock captures data
clk
2xclk
2 cycle path
Formal and Assertion-Based Verification
  always @ (posedge fastclk)
  if (startpoint != prev(startpoint)) ->
    next (endpoint == prev(endpoint);
Notes: <number>

## Slide 9: Slow to Fast Clock Multi-Cycle Paths
Control Logic
1
0
Clock
Gen.
clk
2xclk
2xclk
clk
Slow clock launches data
Path is disabled
Fast clock captures data
2 cycle path
Formal and Assertion-Based Verification
  always @ (posedge clk)
  if (startpoint != prev(startpoint)) ->
  !(sensitization condition);
Notes: <number>

## Slide 10: Same Clock Multi-Cycle Paths
Control Logic
1
0
1
0
Data launched
Path is disabled
Startpoint is held stable
Data captured
clk
2 cycle path
Formal and Assertion-Based Verification
  always @ (posedge clk)
  if (startpoint != prev(startpoint)) ->
  !(sensitization condition);
Notes: <number>

## Slide 11: Clock Gating Multi-Cycle Paths
clk
2xclk
en
capture_clk
2xclk
clk
en
capture_clk
Slow clock launches data
Fast clock is disabled
Fast clock captures data
2 cycle path
Formal and Assertion-Based Verification
  always @ (posedge clk)
  if (startpoint != prev(startpoint)) ->
  !(clock-gate enable);
Notes: <number>

## Slide 12: Functional False paths
set_false_path –from [get_cells startpoint_reg] \ –through [get_pins pin]
–to [get_cells endpoint_reg]

## Slide 13: Scalable Formal MCP Verification
Tool scales to handle full-chip RTL for SoCs
Functional Abstraction is key enabling technology
  Design Pruning
    Design representation operated on only contains the subset of the full design required to verify MCPs in a user constraint file
  Control Identification
    Boolean equations are simplified so that only the impact of control signals is considered when computing path propagation conditions
  Logic-Cone Simplification
    Logic cones that feed control signals are simplified by factoring out the impact of unessential subcones

## Slide 14: Functional Abstraction: Design Pruning
ht_sb_wrpend_reg
Logic that does not impact an MCP is pruned out prior to building the design

## Slide 15: Functional Abstraction: Control Identification
Approach to identify control signals on a design
  Control signals enable or disable the propagation of a transition along a timing arc
  Control identification simplifies path propagation conditions and reduces complexity of formal proof
Timing Arc:
bufavail  arc_IDLE_LCKPND
Propagation Condition:
(hdqvalid & ~hqd_wXrB & ~hqd_hlock_b)

## Slide 16: Functional Abstraction: Logic-Cone Simplification
1
0
ht_ho_fsb_db_bpsel_qw01_i
htrdsel_sb
Approach to simplifying logic cones leading to control signals
  Logic that is peripheral to computation of a signal value is factored out
  Logic-cone simplification prevents formal proof from blowing-up

## Slide 17: Formal verification of MCPs: pilot deployment results
Design – integrated graphics project with around 20+M gates
Type of special constraints verified by formal flow
  Fast clock to slow clock MCPs
  Slow clock to fast clock MCPs
  Same clock MCPs
  Functional false paths
Total number of MCPs + FPs = 2641
80% of the special constraints were carried over from previous project due to logic re-use

## Slide 18: Pilot deployment results
Run times/memory requirement
  Machines used – 1X 64G and 2X32G machines
    Peak memory usage is typically during constant propagation
  Total run time for formal flow to complete verification of all special
  constraints with waivers - ~ 96 hours
Verification results
  Total number of MCPs + FPs passed with design waivers – 2109
  Number of MCPs + FPs dropped by the tool – 311
      No paths, unmapped
  Number of MCPs + FPs reported ‘fail’ by the tool but waived
  due to low risk(after simulation or manual reviews) – 221
  Number of real incorrect MCPs found – 31
    5 of them had major timing impact and considered high risk
Key learnings
  Design engineers need to spend good amount of effort in coming up with proper waivers for majority of the MCPs ‘failed’ in formal runs
  Formal tool had to be run at the highest level to minimize the manual
  work in dispositioning the failures
  Although very few real MCP failures were found, considering the risk
  level of the real failures, there is justifiable ROI in performing formal verification on MCPs

## Slide 19: Improvements required
Formal verification runs on MCPs is still taking a long time and support for parallelization to improve run times should be explored
Counter examples derived from failed MCPs of formal runs should be used as coverage points for simulation of MCP assertions to assess the risk of the specific failure
Defining waivers for MCP formal failures is still a major investment of design engineer time. Designers should specify some of these constraints as a part of high level specs if the waiver is a result of architectural assumption.
When the tool reports “NO PATHS” it is difficult to understand whether it is due to an unconstrained port or
the traversal hit a blackbox.