## Slide 1: Reducing Dynamic Power with Gate-level Clock-Gating Optimization
  Subrangshu K. Das, Texas Instruments
  Aishwarya Singh, Post-graduate student at ISB*
  Mohit Sharma, Texas Instruments
  Sarveswara Tammali , Texas Instruments
  Rajesh Gottumukkala, Texas Instruments
  Amit Singh, Azuro
* Work done during her tenure in Texas Instruments

## Slide 2: Introduction
Reducing power consumption to improve battery life is key care-about in digital design today
Gate-level Clock-Gating can reduce clock and FF power by ~20-30% over and above RTL-level clock-Gating
  Clock / FF consumes ~40-50% of total dynamic power

## Slide 3: Challenges in Gate-level Clock-Gating
Gate-level clock-gating introduces new logic paths in the design, which are redundant and added at the end of the data-path
New redundant paths can introduce functional / testability / timing-closure / verification challenges
In this presentation, we describe robust methodology to prevent bad design due to newly added redundant paths

## Slide 4: Basic RTL-Level Clock-Gating
q
d
EN
CLK
Low-Power Clock-Gated FF
D
Q
CG
always @(posedge CLK)
begin
if (EN)
Q <= D;
end

## Slide 5: Gate-Level XOR-based Clock-Gating
Gates clock to a cluster of FFs if value written is same
as the value already stored
Supported in Azuro’s PowerCentric tool

## Slide 6: Functional Challenges
If D-input of FF is un-timed, sampling that in XOR cloud could result in meta-stability related issues to other flops in the same cluster
  E.g., FF3, which is a clock-domain crossing flop should be excluded from XOR gating
Spyglass was used to identify clock-domain
crossing FFs and then dont-touched in PowerCentric

## Slide 7: (Async) Reset domain-crossing FF must not be XOR-gated
Primetime Tcl scripts were written to identify
reset-domain crossing flops and then dont_touched in
PowerCentric

## Slide 8: Timing-exception FFs must not be XOR-gated
FF having false-path / Multi-cycle exceptions to them should also be excluded from XOR-gating
  Assumption used to waive timing check on particular FF may not hold true for rest of the FFs in the XOR cluster
Primetime Tcl scripts were written to identify such flops
and then dont_touched in Azuro

## Slide 9: Testability Challenges
Stuck-at-one (SA1) faults at outputs of XOR cone are not observable
Required condition for SA1 detection is not observable!
  Next state equal to current
  Should be true for all flops in cluster
SA1 on XOR output cone only affects power (and not functionality)
Test coverage hit is up to 1% on industrial designs
However, a simple design change with a negligible over-head can resolve test coverage issue
  see next slide for details
st1
d
q
d
q
d
q
dft_az_te
func
clkin
clkout
en
te
func
func
st1
st1
st1
Notes: <number>
07/30/26
<number>
07/30/26
<number>

## Slide 10
Design Change to recover Coverage Loss
OR gate added at output of Cluster Control Flip-Flop (CCFF) within the cluster
CCFF selected based on timing slack / placement
Enables to create equivalent states on XOR inputs while D =1 and Q=0
CCFF captures ‘1’ if there is a SA1 fault on XOR output cone and hence fault become observable
Note: Functional / Scan-shift fanouts from CCFF does not go through the OR-gate
st1
d
q
dft_az_struct[n]
d
q
d
q
dft_az_te
func
clkin
clkout
en
te
func
func
st1
st1
st1
0
0
1
1
0
1
1
d
q
CCFF
Notes: <number>
07/30/26
<number>
07/30/26
<number>

## Slide 11: Timing Closure Challenges
XOR gating generates high fanin logic cone to the enable pin of a clock gate. This can result in local congestion and timing closure issues in some cases
PowerCentric automatically identifies problematic FFs and excludes them from XOR-gating

## Slide 12: Design Sign-off
CDC / RDC Check
Equivalence Check
Functional Gate simulation

## Slide 13: Clock/Reset Domain-Crossing Checks
No good tool available today to comprehensively verify CDC and RDC in netlist
Primetime Tcl scripts written to verify XOR-gating did not introduce any new CDC / RDC path

## Slide 14: EC Constraints
st1
d
q
Test point control
d
q
d
q
SCANEN
func
clkin
clkout
en
te
func
func
st1
st1
st1
0
0
1
1
0
1
1
d
q
CCFF
d
q
d
q
d
q
func
func
func
CCFF
clkin
Pre Azuro
Post Azuro
EC steps to verify Pre and Post Azuro netlists
  functional mode: SCANEN = 0 and Test point control = 0
  Shift mode : SCANEN = 1
sd
sd
sd
sd
sq
sq
sq
sq
scanin
scanout
d
q
sd
sq
scanin
sd
sq
sd
sq
sd
sq
scanout

## Slide 15: Gate-level Simulation - Problem
G
X
X
en
clk
0 → 1
0 → X
All FFs in GLS power-up as “X”
Post asynchronous reset, only non-resetable FFs still remain “X”
Even after clocks start, non-resetable FFs still remain “X” because of the feedback loop
  XOR gate output is “X” if one input is “X”
This is purely a simulation artifact and not a real silicon problem
  Irrespective of FF powering-up as “1” or “0”, it will follow the D-input
Notes: <number>
07/30/26
<number>

## Slide 16: Gate-level Simulation - Solution
To eliminate “X” pessimism, PowerCentric exports a verilog file with force/release statements to ensure FF is updated with D-input when clock starts to toggle
  “force” condition applies only if X’s appear on comparator gate inputs
    If one XOR input is X then comparator output forced high
    If both the XOR inputs are X, then it doesn’t matter if the comparator output is high or low so we set it low
  Once the X’s are gone the “release” returns the circuit to normal operation
0 1 X
0 0 1 X
1 1 0 X
X X X X
0 1 X
0 0 1 1
1 1 0 1
X 1 1 0
Default XOR truth table
Forced truth table for
structural gating comparator gates
Notes: <number>
07/30/26
<number>

## Slide 17: Gate-level Simulation - Handling XOR re-mapping
Post-CTS tools may eliminate comparator outputs from the netlist, e.g:
 No longer possible to safely force/release the netlist
Solution:
  Constrain downstream flow to not re-map comparators
  Consistent naming pattern for comparators so this is easy:
  set_dont_touch or set_map_only *AZ_encmp*
Notes: <number>
07/30/26
<number>

## Slide 18: Results
Design Stats |  | Power Improvement (%)
45 nm low-power process ~1.6 million instances Multiple clocks (>20) Highest freq. = 266 MHz | Clock Power + Register Power | 22
 | Total Power | 7.5
Area overhead of 0.8%

## Slide 19: Summary
Robust design methodology required to ensure redundant paths (added during XOR gating) do not cause any design issue
XOR-based Clock-Gating saved ~22% of Clock+FF power over RTL-based Clock-Gating