## Slide 1: An Efficient Multi-voltage Timing Sign-off Methodology
Domain B
Domain A
CK
1.2
1.6
1.6
1
1.5
1
1.5
1.5
1.5
2
Junichi Mano, Kimihiro Ogawa
{mano.junichi , ogawa.kimihiro}@starc.or.jp
Motivation
The number of STA runs needed for signoff is increasing
  # of independent power supplies is increasing
  # of sign-off corners is increasing
  Where m: # of operating modes, 24 for our test chip
  c: # of process, temperature and wire corners
  n: # of independent supply voltages
Our purpose is to limit this explosion of STA runs
Number of STA runs
45nm
m=24
c=9
n=3
For Example
1512 STA runs
STARC Method
144 STA runs
45nm node
m=24
c=6
n=3
The brute force method
Number of STA runs
Vdd domain 1
Vdd domain 2
…
For a single power supply there are 9 corners as shown below on left
If we have 2 independent supplies, then using the brute force method, we need to expand 1 HV corner to (HV, HV), (HV, LV) and (LV, HV), since one of the 2 voltages may fall to LV
Note that generally speaking
Process and wire conditions are different for HV and LV
Sign-off corners correspond to D2D variation, so process and wire conditions should be the same for a chip at a corner.
3
Why So Many STA runs?
STARC Methodology
STARC reduction methods
# of STA runs increases very quickly along with # of supplies, assuming m=24. c=9 and 6, respectively
Cause of STA Run Increase | Reduction Method | Explanation
Multi Vdd | IPD (Inter Power Domain) treatment | This presentation
Process variation | VTC ( Variation tolerant clock) | In future
n: # of Independent Power Supplies | 1 | 2 | 3 | 4
Brute Force Method 24*9*(2**n-1) | 216 | 648 | 1512 | 3240
IPD method 24*9*1 | 216 | 216 | 216 | 216
IPD + VTC 24*6*1 | 144 | 144 | 144 | 144
IPD Method for PBA at a HV corner
  Calculate launch and capture path delta delays (increment from high V to low V) in each Power Domain separately.
  For hold time checks, if capture path delta delay > launch path delta delay, then add the delta delays to all cells along the clock net in that domain.
  For setup time check, if capture path delta delay < launch path delta delay, then add the delta delays to all cells along the clock net in that domain.
  If it is judged that all the interface paths need delays to be added, then this case should be analyzed in the other corners which have low Vdd conditions, so we skip this STA run.
IPD Method Example for PBA - Holdtime Check
IPD Coefficients for Various Cells
Single-IPD may not be accurate enough.
we need more accurate method (Each-IPD,Multi-Lib)
IPD Method - 3 Possibilities
The Each-IPD and Multi-Lib methods are quite similar, the only difference is that in Each-IPD, pre-characterized IPD coefficients are used to calculate delta delays
On the other hand, in Multi-Lib LV and HV libraries are used to calculate them instead.
We recommend using Multi-Lib, however, it is not always possible to obtain all the necessary library variations.
Summary
Example for hold time check | Domain A (IPD coeff. =1.1) |  |  | Domain B (IPD coeff. =1.2) |  | 
 |  | with delta | Delta |  | with delta | Delta
Launch path delay [ns] | 7 | 7.7 | 0.7 | 1.2 | 1.44 | 0.24
Capture path delay [ns] | 3 | 3.3 | 0.3 | 3.2 | 3.84 | 0.64
Launch < Capture ? | No (0.7 > 0.3) |  |  | Yes (0.24< 0.64) |  | 
Domain B
Domain A
CK
1.2
1.6
1.6
1
1.5
1
1.5
1.5
1.5
2
Launch
Launch
Capture
Capture
Acknowledgements
The authors would like to thank A. Sadahiro for his previous effort. This work is supported by NEDO (New Energy and Industrial Technology Development Organization) in Japan as part of the project for the Development of Next-generation Process-friendly Design Technologies.
IPD Method for PBA ( Path Based Analysis)
Analysis Steps ( for HV corner , HV=VDD+ΔV)
  Along the launch path in domain A, the path delays are 7 and 7.7 with the delta delay. Along the capture path in domain A, those are 3 and 3.3 respectively.
  The delta launch delay (0.7) is larger than the delta capture delay (0.3) so that nothing is added.
  Along the launch path in domain B, the path delay is 1.2 and 1.44 with the delta delay. Along the capture path in domain B, it is 3.2 and 3.84 respectively.
  The delta launch delay (0.24) is smaller than the delta capture delay (0.64) so that the delta delays are added.
Extracting IPD coefficients
Quite simple, this is basically the delay ratio between different voltage supplies.
IPD coefficient = Delay(LV) /Delay(HV) -1 , (HV=VDD+ΔV , LV=VDD-ΔV )
  Target cell with 2 stage buffers at in and out for natural waveform and load.
  Wire resistance 0, assuming wire resistance has no voltage dependency, load R = 0 is the worst case for voltage dependency check.
  Load Cap.=0.5* MaxCap, fixed, because delay ratio doesn’t depend on Cload as shown right.
  Input Slew is fixed by the circuit, because delay ratio doesn’t depend on Slew as shown right.
trapezoidal waveform
For natural
waveform
For natural
load
Example
  Corner FF, 1.2V, -40C
  Power Domain Voltage Spec VDD=1.1V±0.1V
  Voltage range: 200mV（1.2V→1.0V）
  IPD coefficient: +0.5
cell
Delay measurement
for each Vdd
8
1
2
4
5
6
7
9
(HV=VDD+ΔV , LV=VDD-ΔV )
IPD coefficient = Delay(LV) /Delay(HV) -1
(HV=VDD+ΔV , LV=VDD-ΔV )
Note that,
IPD coefficient is different at different Vth or different operating voltage for the same kind of cell.
ーー＞ for better accuracy ,each cell has its own IPD coefficient.
Note that IPD method can reduce (2**n-1) of STA runs To 1
The reason is that this method can analyze worst slack of signal paths which run through different domains (both in low/high Voltage) by adding incremental delay as IPD coefficient and can skip all the other possible voltage combinations.
IPD Method - Basic Concept
The Inter Power Domain (IPD) method adds necessary incremental delay to the interface paths between different voltage domains instead of changing Vdd value of the domain entirely.
It has different properties for GBA and PBA GBA: Graph based analysis PBA: Path based analysis
IPD Method | Merit & Demerit | Methodology
IPD Method for GBA | pessimistic fast | Choose the target paths on which incremental delay should be added simply based on the corner and the analysis (set-up, hold) type, without doing path checks.
IPD Method for PBA | accurate slow | Choose the target paths based on path analysis as explained later.
IPD Method for GBA ( Graph based Analysis)
IPD method for GBA
Add incremental delay (IPD coefficient) only on one side (the target) of launch or capture of a data path.
Capture
IPD coefficient should be added to all capture cells
Corner Voltage Condition | Target IPD Path | 
 | Hold Time Analysis | Setup Time Analysis
HV (High Voltage) | Capture | Launch
LV ( Low Voltage) | Launch | Capture
An example for high-voltage min (hold check) analysis
Rules of IPD method for GBA
Launch
(HV=VDD+ΔV , LV=VDD-ΔV )
Analysis Type | Judgment for Apply IPD | IPD | Because
Hold time check | Capture path delta delay > Launch path delta delay | Apply IPD | Worst case for Hold check
 | Capture path delta delay < Launch path delta delay | No IPD | 
Set-up time check | Capture path delta delay < Launch path delta delay | Apply IPD | Worst case for Setup check
 | Capture path delta delay > Launch path delta delay | No IPD | 
Rules of IPD method for PBA at a HV corner
Single-IPD | Only one coefficient for all kind of cells, simple but less accurate
Each-IPD | Separate coefficient for all cells, accurate but need pre-characterization effort.
Multi-Lib | Switch libraries according to operating Vdd in delay calculation, accurate but need more libraries.
Single-IPD method performance (commercial tool A)
test data (DVFS) for cpu/1run, memory usage
Performance |  | Total CPU[min] =(STA runs * cpu/1run) | Memory Usage(GB)
 | STA runs |  | 
Brute Force Method | 1512 | 9027 (=1512*5.97) | 1.466
IPD method | 216 | 1429 (=216*6.62) | 1.478
Difference |  | -7597 | +0.012
% |  | -84% | +0.8%
AMD Opteron 2.3GHz 128GB 16CPU
Red Hat Enterprise Linux AS 4 Update 7
n: # of Independent Power Supplies | 3
Brute Force Method 24*9*(2**n-1) | 1512
IPD method 24*9*1 | 216
IPD + VTC 24*6*1 | 144
Performance | CPU[min] =(cpu/1run) | Memory Usage(GB)
Brute Force Method | 5.97 | 1.466
IPD method | 6.62 | 1.478
Difference | 0.65 | +0.012
% | +11% | +0.8%
Data Outline (45nm) | 
# of independent supply voltages : | 3
Num of instances | 133k
Chip Size | 0.2mm x 0.2mm
NET | 30k
Performance Results
We have shown an efficient multi-voltage timing sign-off methodology which requires 1/(2**n-1) times fewer STA runs than conventional methodologies.
Single-IPD method already been implemented in several commercial tools.
Experimental results show that Single IPD method reduced total cpu time by 84% compared with Brute Force Method.
The Each-IPD and Multi-Lib are being implemented in commercial STA tools and will be verified its efficiency and accuracy.
10
11
12
Num. of STA runs necessary for STARC 44MG test chip
3
IPD coefficient should be added on cells in Domain B
IPD coefficient is
different for each cell.
G1
High Vth
Low Vth
G2
G3
G4
G5
G6
G7
G1
G2
G3
G4
G5
G6
G7
65nm
m=24
c=5
n=1
120 STA runs