## Slide 1: Clock Domain Crossing verification signoff in a multimillion gate SoC
Ayon Dey (a-dey@ti.com)
Shailesh Ghotgalkar (shailgg@ti.com)
Gokulakrishnan Manoharan (g-manoharan@ti.com )
Paras Mal Jain (paras@atrenta.com)
Namit Gupta (namit@atrenta.com)
Clock Domain1
Clock Domain2
Clock domain is the portion of the design driven by a single clock or clocks having constant phase relationship.

## Slide 2: The CDC Challenge – Balancing the Needs and the Risks!
Heterogeneous applications like wireless, networking, video, graphics have dozens of clocks with asynchronous crossings
Traditional STA checks or functional simulation do not adequately verify CDC problems!
Responsibility for validating CDC issues is shifting from verification engineers to logic designers
Notes: <number>
<number>
Most of you are designing complex chips that go on devices like the Blackberry, Wii, iPhone, HD Camcorders etc
These applications have heterogeneous applications like wireless, networking, audio, video etc which involves many async clock domains
Traditional methods like STA and functional simulation do not adequately catch CDC issues, since it a manual process and is typically done through design/code reviews and by writing test benches for specific protocols.
Another trend we are seeing is that logic designers are now responsible for validating and sign-off for CDC checks since they have responsibility for adding synchronizers in RTL

## Slide 3: Pitfalls of Traditional Approaches
Traditional verification tools target synchronous designs
  Coverage of asynchronous domain crossings can not be 100% in functional simulation
  Static timing analysis does not analyze asynchronous paths
The following solutions are needed:
  Automated checks to cover complete design early through static analysis of CDC issues
  A good methodology for robust constraint development for the static rule checker tool.
  Use the constraints for a focussed static analysis followed by advanced dynamic checks

## Slide 4: A Methodology for Dedicated CDC Analysis
Have constraints?
Know clocks
and resets?
SPECIFICATION
and RTL
No
Yes
Find clocks/resets
Automatically using tool
Manual Editing/Fine-tuning
of constraints
Populated
Constraints of
good quality?
(1) Secure
constraints quality
Yes
No
Reports evaluation
manual
Publish results
Automated by scripting
(3) SpyGlass-CDC
static checks
Decision to be made seeing specific violations intended for constraints enrichment
(Number) signifies the sequence of the steps.
Reduced false violations (noise) seen by following the steps in order of (1) -> (2) -> (3) -> (4)
(2) SpyGlass-CDC
structural checks
(4) Simulation based
dynamic CDC checks

## Slide 5: Secure Constraints Quality
The correct setup always ensues less noise in actual analysis.
The constraints developed for CDC checks matched with STA constraints
Setup Checks
Clock convergences (missing set_case_analysis): Clock_info05
Unconstrained flops (missing clock constraint): Clock_info03
Auto-recognition of clocks/resets: Setup_clock01/Reset_info01
Data
SYSCLK
Destination
TCK
SpyGlass-CDC reports missing set_case_analysis
on both the mux-selects so as to avoid false
clock domain crossings if select pins on both
the muxes are enabling the same clock

## Slide 6: SpyGlass-CDC Structural Checks
Structural CDC checks
Glitch-inducing logic in clock paths: Clock_check01, Clock_glitch02
Isolation latches in clock path: Clock_check01
Unexpected gates in reset tree: Reset_check09
Logic
Glitch-inducing logic
L
CLK
Glitch-free gating

## Slide 7: SpyGlass-CDC Static Rule Checks
Metastability on control and data lines
Unsynchronized crossings: Clock_sync01
Synchronized crossings: Clock_sync02
Metastability on reset lines
Synchronous reset de-assertion: Reset_sync01
Resets crossing domain: Reset_sync02 and Ac_resetcross01
Logic
Address
Control
Qualifier
Destination
FSM
FSM
Data

## Slide 8: SpyGlass-CDC Static Rule Checks
Metastability settled to logic 1 in one path and 0 in another path
Metastability settled to logic 1 in one path and 0 in another path
Ck2
D1
D0
D2
Ck1
Ck2
B1
B0
B2
Ck1
Logic
Chip Killer !!
Convergence Verification
Combinational convergence: Ac_conv02
Deep sequential convergence: Ac_conv01

## Slide 9: SpyGlass-CDC Dynamic Rule Checks
Metastable points
Convergence of 2 crossings
FSM broken due to metastability missing counter_end signal
BEFORE
Usual simulation without metastability injection
AFTER
Simulation with metastability injection

## Slide 10: Churning the Tool
Useful tool byproducts
  The synchronizer list provided by SpyGlass-CDC is used for GLS setup as the list of uninitialized flops. (Synchronizers normally don’t have resets).
  The list is also used during CTS to avoid custom clock gating on synchronizers.
  There was marked improvement in STA constraints due to availability of CDC constraints early in design cycle
Error highlighting in a schematic with constraints values to aid debug
A spreadsheet viewer for better debugging, through filtering and sorting of relevant messages.
On-the-fly creation of waivers and constraints for irrelevant errors

## Slide 11: False Violation Filtering
The cdc_false_path constraint can be generated automatically from
  The schematic
    Select a net; right click; Chose “Set SGDC constraint…”; enter the constraint
  The spreadsheet view
    Select violations in spreadsheet; click on “C”-icon, or right click to select constraint generation
Constraint generation menu
Notes: <number>
<number>

## Slide 12: Schematic to the Rescue
Source
Destination
Request (Control line)
Acknowledge

## Slide 13: Metrics
SoC
Specification
RTL
Development
Verification
STA
GLS
SpyGlass-CDC
checks
SoC
Specification
RTL
Development
Partially checks CDC issues
Dedicated CDC check
No of CDC Bugs Found
Verification
STA
GLS
3
6
Relative Effort Required at step to catch CDC issues
Traditional Flow
Enhanced Flow
3
4
10
6
14
1
0
6
1
4
3
6

## Slide 14: Current Issues And Proposed Enhancements
Issue: CDC analysis of SoC designs with full IP descriptions may have high run time and memory usage
  Solution: Hierarchical CDC checks
Proposed enhancement:
  Complete CDC analysis of the IP/module
  Automatic generation of abstracted models for use during SoC analysis
  SoC owner uses the abstracted models of the IP blocks while doing CDC verification and does not need to provide full IP descriptions
Benefits:
  SoC analysis will only see the boundary of the blocks and perform much faster analysis.
  The SoC team needs to focus on integration boundaries and glue logic; saving run time and effort