## Slide 1
ECO Methodology for Very High Frequency Microprocessor
Sumit Goswami, Srivatsa Srinath, Anoop V, Ravi Sekhar
Intel Technology, Bangalore, India
Introduction & Motivation
Solution Descriptions
Results
Summary and Next Steps
Logic Complexity is Increasing Every Year
Number of functions per chip is growing
Logic Verification Challenges growing rapidly
Chances of hitting bugs near Tape Out is increasing
Performance race is creating Si quality challenges
All not fixed by standard available EDA tools
All manual fix is expensive in terms resource and TTM
Convergence vectors evermore interdependent
ECO is Reality and Necessity
for
All High Performance Designs
Last minute change to fix bug/quality is unavoidable
ECO in Processor Design Cycle
Rev0
RTL Development
Cycle
RevF
RTL
on
ECO
Implementation Cycle
T
A
P
E
O
U
T
ECO
T
A
P
E
O
U
T
ECO comes during last phase of implementation
Extremely critical in schedule for TTM with Quality
Require an intelligent methodology which understands the ECO from design challenge perspective and optimizes all the vectors concurrently
Minimal user inputs/interventions
Lower dependency on user’s EDA tool knowledge
Optimize all vectors
API for manual ECO programming
Smart enough to switch modes automatically
  Timing
  Layout
  Power
Problem Statement
RTL ECO Engine
Tim ECO Engine
FP ECO Engine
Power ECO Engine
Manual ECO Engine
Clock ECO Engine
Surprise
In
Sign-off
Timing
Late
RTL Bug
Change
in
Full Chip
Delta
In
Power
Target
Miss
In
Clock Quality
Overall Architecture
Final
Database
Dump Netlist
New
RTL
Synthesis
Context
Optimization
Compare Netlist
Boolean
Comparison
Apply
ECO
New
Database
Final
Database
New
FC FP Collateral
Database
Comparison
Recreate
Objects
New
Database
Final
Database
LR
Downsizer
Clock
Healing
New
Database
Final
Database
Cell
Rebalance
Regenerate
Routing
New
Database
Final
Database
Timing Analysis
Implement
Fix
New
Database
Based on few basic ECO engines
ECO engines are configurable
Engines get triggered based on ECO need
Engines can be combined to make package
Routing is complementary
No routing helps to evaluate ECO impact
Centered on Boolean Comparison of netlists
Generate expressions for changes
Expressions get synthesized
Context optimization selects better gates
ECO implemented in terms of add/delete cell/net
Detects changes based on DB compare results
Implements only pin/FC route change
Generate new DB ready for routing
RTL ECO Engine
Floorplan ECO Engine
Clock ECO Engine
Can adjust clock network based on sequential add/delete
Can tweak network based on quality targets
Gets triggered automatically during RTL/Manual ECO if sequential added/deleted
Downsizes cells based on timing
Based on “Lagrangian Relaxation” algorithm
Downsizes sequential elements also
Power ECO Engine
Clock healing only if sequentials get touched
0 impact on timing and quality
Timing ECO Engine
Analysis in sign-off tool and fix in impl tools
Concurrent analysis-fix through server-client model
Address max/min/silicon quality issues
Concurrent analysis of all
Reduces manual fix for last few issues
Helps in TTM
Triggers almost after all other engines
Routing is recommended after this
Next generation Intel XeonTM Microprocessor
Server Microprocessor chip
Sub 45nm process node
Multi Giga Hz clocking
45+ blocks ranging from 5K to 280K instances
With embedded hard macros
Complex architectural features
Design Details
0 re synthesis in the project
Intercepted 100+ complex RTL ECOs
Implemented several hundreds of timing ECO
~25% power saving due to power ECO
10+ floorplan ECO
20+ clocking ECO triggered by RTL ECO and 10+ clock ECO due to quality fix
Highlights
Design | Instance Count | Complexity | Convergence Time | No. of ECO | ECO Time (average time per ECO)
Block1 | 190K | High | 12 Weeks | 15 | 1.5 Day
Block2 | 160K | High | 10 Weeks | 10 | 1 Day
Block3 | 150K | High | 10 Weeks | 6 | 1 Day
Block4 | 180K | Medium | 7 Weeks | 11 | 0.75 Day
Block5 | 40K | Low | 5 Weeks | 8 | 0.5 Day
RTL ECO Effectiveness
Original Design
Original
Pin
Original
Routing
Post FP ECO Design
Modified
Pin
Post ECO
Routing
Floorplan ECO Effectiveness
Clock Driver
Receiver
Original Design
Clock Driver
Receiver
Post Clock ECO Design
Clock ECO Effectiveness
74% Quality Viol Fix
Power ECO Effectiveness
22% Total Power Reduction
25% Leakage Power Reduction
80% Max TNS and 30% min TNS fix
70% quality violation fix
Timing ECO Effectiveness
ECO is no longer a luxury item. It is reality. So you better expect them.
Expect surprises during last mile of convergence
High performance designs requires ECOs because of complex logic and quality targets
Extremely useful to have ECO system to stay in schedule
Concurrent optimization of all convergence vectors are key to success
Using these flows we are able to stay in schedule for extreme high performance Intel server CPU
Summary
Tune CTS ECO and Timing ECO to get 100% coverage on fixing
Work with EDA vendors to tune tools for better ECO optimizations
Develop additional features in RTL ECO to insert and utilize redundant gates for future stepping
  Saves mask cost
Auto timing ECO by metal only tuning
Next Steps
Notes: <number>