## Slide 1: Low Power Verification for SoC using Formal Techniques
Ayon Dey (a-dey@ti.com)
Shailesh Ghotgalkar (shailgg@ti.com)
Jacob Joseph (jacobj@ti.com)
Shekhar Sharma (shekhars@ti.com)
PD0
VDD
SW0
PD
1
VDD
SW0
PD
2
VDD
SW0
ISO
ISO
VDD
U1
U2
U3
ISO
ISO
U4
U5

## Slide 2: Why Low Power Verification?
Tons of Power Management (PM) techniques available
Optimal combinations to achieve best power that balances with area and complexity tradeoff
Each technique requires addition of specific PM cells and design structures
Exigent task to ensure that the PM infrastructure inserted is :
  Not disrupting the functionality
  The intent of newly added structures is served
  The sequence of power controls does not break any electrical assumption
0.9V
1.0V
1.2V
0.9V
1.0V
off
1.2V
0.9V
1.0V
ret
1.2V
0.9V
1.0V
0.9-1.2V
CTRL
ACK
Multi-Voltage
Power Gating
Power Gating with state retention
DPS, DVFS, AVS

## Slide 3: Divide and Conquer: Break the Problem in Different Levels
Design
Rule
Check
DRC Report
Net-list, PM Cells Info (lib), CLP library
Power Mgmt
Rule
-
Check
Analyze
Power
Domain
PM Rule Check
Power pin definition
Validate
Dynamic PSCON
Report
Report
Design Initialization, PSCON Identification
Check
Transistor Report
Spice Library
Level 1
Level 2
Level 3
Level 4

## Slide 4: Level1: Basic Structural Issues
Structural issues like Standard DRC (Design Rule Checks) for finding un-driven inputs, bus-contention PM cells in strong combinational loops
Exhaustive analysis is performed with minimal user defined constraints, constituting primarily the power pin definition, thus ensuring that the checks are less error-prone
VDDLSW
Design
SW0
SW1
SW2
SW3
1
0
CLP Reports:
•
(CLP_STRC1.1) Strong combinational loop detected (occurrence:1)
•
Bus Property 8610 is *Fail @ 0* Gate name: VDDLSW$BUS
Type : Internal BUS
Characteristic: no floating,
bus contention
Witness: bus is driven by conflicting inputs (2nd and 22nd).
Key Points: bus: Id=8610, Name=...1/VDDLSW$BUS.
2nd bus input: Id=613437, Value 1'b1
22nd bus input: Id=613737, Value 1'b0

## Slide 5: Level 2 : Static Checks
Missing isolation cell: Invalid power domain crossing
Redundant Isolation cell detection (useful for timing critical paths, saves area and leakage power)
These static checks are centered on PM Structures targeted at functional failures due to missing isolation cells (ISO) ,missing level-shifters (LVL), redundant isolations and PM controls routed through non-always on cells.
Incorrect power pin connectivity is also identified and reported.
It requires additional constraints to identify the PM cells.
Level-1 and level-2 checks are clean  proceed for level-3 checks

## Slide 6: Level 3 : Dynamic checks
Identifies dynamic floating nodes created by improper assertion of PM controls for LVL, ISO and Retention Flip Flop (RFF).
Additional user defined constraints
  Power State Controller (PSCON) instance specification
  Design initialization state
Tool excites the design using initialization sequence, performs dynamic PM control assert checks.

## Slide 7: Level 4 : Spice Level Checks
Performs check at lower level of abstraction  Spice libraries
Detects maximum allowable transistor stack in a cell or connected cells required to support AVS
Detects any un-buffered input exposed at a power-domain boundary
Such issue can cause leakage through the forward-biased p-n junction if source domain is ON and destination is OFF

## Slide 8: Challenges and Mitigation
Risk: Performing Level-3 checks at SoC level is a tough task as the PSCON control signals may have numerous DFT overrides
  Mitigation: Understand test structures in the design and constrain appropriately to select functional paths from PSCON
Risk: For a multi-million gate design, tool can get tardy if netlist has lot of issues
  Mitigation: Target smaller design hierarchies (one PD) at a time. Resolve each PD and then move on to complete SoC

## Slide 9: Challenges and Mitigation (contd..)
Risk: Simultaneous dynamic checks for LVL and ISO is a challenge. LVL check requires to emulate voltage OFF scenario while ISO check expects the voltage to be always ON
  Mitigation: Create separate setup for LVL checks with the standby option in power pin definition.
Risk: Debugging an L3 failure or ED (Explored to Depth) can be nightmare at times
  Mitigation: Proper understanding of the design architecture along with tool’s capabilities is must for quick analysis

## Slide 10: Other Design Areas Improved
Apart from PM structural checks, CLP can be used to bring improvements in other design areas as well.
  Impact on Area, power and Timing: Detection and removal of redundant isolation cells.
  Improvements to Physical Design Flow: Basic CLP checks of L1, L2 performed early in design cycle
    Reduces iterations in Backend flow
    Identifies missing don’t-touch constraints
    Avoids design schedule impact by identifying incorrect voltage domain implementation and missing MPDR (Multi-Power Domain Region) early in the flow.

## Slide 11: Limitations & Future Enhancements
Limitations
  As CLP cannot perform Level-1, 2 and 3 checks on Spice model, Power Verilog modeling is required for analog components. Only proper modeling can ensure sanity of these checks
  Requires additional Power Aware GLS (PAGLS) for functional correctness
Enhancements
  Better ED debug capabilities
  With increasing design size/complexity, level-3 run time needs to be re-looked

## Slide 12: CLP or PAGLS – Not a Standalone Signoff
CLP | PAGLS
Finds all the issues in a single run | Many test-cases need to be coded
Pin-points the issue with location in netlist | Blind X propagation, needs extensive debug
Signoff for tape-out : Single run + few PAGLS testcases | Need to perform regression with a manually chosen suite of test-cases in absence of CLP
Not an alternative for PAGLS as sequencing related issues will be emulated exhaustively only in simulation | Need to have PAGLS for sequencing related checks.
CLP being a formal tool, has certain disadvantages which can be addressed using simulation
100% coverage is not practical using only PAGLS either.
Signoff  combination of both CLP and PAGLS