## Slide 1: Enablement of Statistical Static Timing Sign-off Methodology Using Industry Standard Liberty Timing Models for 32nm
Dileep N. Netrabile (dileepn@us.ibm.com),
Nathan C. Buck (nbuck@us.ibm.com) and Eric A. Foreman (eforeman@us.ibm.com)
IBM Systems and Technology Group, Essex Junction, VT

## Slide 2: Abstract
Relative process variation increases as technology decreases in size
Design complexity proportionally increases with newer technologies
Using deterministic Static Timing Analysis (STA) to account for growing process variation requires ever more lib corners & ever larger timing margins
Statistical Static Timing Analysis (SSTA) to account for process variation is more feasible method

## Slide 3: Background
IBM has utilized a SSTA signoff methodology for 2 generations (65nm, 45nm) using internal proprietary models called the New Delay Rule (NDR)
NDR is an analytic model that allows computation of delays at arbitrary points in the process/voltage/temperature (PVT) space
Industry standard Liberty model provides timing data at a single PVT
SSTA requires multiple Liberty models to cover process variation
We describe how our SSTA sign-off methodology was developed using industry standard Liberty models for 32nm to replace NDR
Comparative runtime data of NDR to Liberty models is shown to demonstrate that statistical timing benefits can still be obtained using industry standard models
Blue Box represents PVT space covered by NDR
Process
Voltage
Temp
Red circles represent arbitrary PVT points covered by a single Liberty model

## Slide 4: Outline
Implementation of the SSTA Timing Model
Modeling of the SOI History Effect
Modeling of On-Chip Variation (OCV)
Sensitivity Analysis
Results
Conclusion & Future Work

## Slide 5: Implementation of the SSTA Timing Model
SSTA propagates delay/slew distributions using a canonical model:
  a0 = mean of the distribution
  ai = sensitivity
  ΔXi = deviation from nominal value for source of variation
  an+1 and ΔR = random variation
Canonical model is used to account:
  Process variation
  Environmental variation
  Systematic and random OCV
[1] Visweswariah, C., et al, “First-order incremental block-based statistical timing analysis,” IEEE Trans. Computer-Aided Design of Integrated Circuits and Systems, vol. 25, no. 10, pp. 2170–2180, 10/2006.
[1]
c
MAX
Deterministic:
Statistical:
c
MAX
VS

## Slide 6: Modeling the SOI History Effect
IBM’s 32nm ASIC offering is a SOI technology and requires modeling of the history effect
Floating body of the transistor results in a body charge and potential that is dependent on the switching history
  This changes the threshold voltage and delay
For each gate (ex: AND2), 2 Liberty files model the intrinsic delay and the SOI history effect
Early Mode Delay/Slew
minSOI.lib
Late Mode Delay/Slew
maxSOI.lib
Intrinsic Delay
History Effect

## Slide 7: On-Chip Variation (OCV)
OCV includes systematic and random distributions
Represents the intra-die variation due to transistor’s gate line width variation and random dopant fluctuations
Systematic variations model portion of cell delay that correlates with each other
Random variations model portion of cell delay that is independent and uncorrelated
Random
Note: Early and Late separation is exaggerated to show all distributions
Intrinsic
Systematic
Systematic
WC
BC
-3σ
+3σ
Process
Nom
-3σ
+3σ
-3σ
+3σ
Random
L
E
-3σ
+3σ
-3σ
+3σ
L
E
-3σ
+3σ
-3σ
+3σ

## Slide 8: Modeling On-Chip Variation (OCV)
Spice Simulations using industry standard cell models
Characterization Tool
Random Multiplier
Systematic Multiplier
OCV Dotlib
Step1: Characterization
minSOI.lib
maxSOI.lib
multiply
OCV Dotlib
Random Multiplier
Systematic Multiplier
Random Delay
Systematic Delay
Step2: Computation of Random & Systematic Delays

## Slide 9: OCV Dotlib Details
Contains unitless multipliers instead of absolute delays and slews
Not stored at all PVTs, but just when the nfet/pfet are at their typical process corners
Each timing arc / test is a function of input slew and output load
Syntax complies with industry standard specifications

## Slide 10: Sensitivity Analysis
Finite Differencing is used to compute the sensitivity for each source of variation:
  T = delay time
  Xi = source of variation of interest
  Corner1, Corner2 = process distribution limits from source
  sigma = number of standard deviation points on the parameter distribution
Corner1
Corner2
µ
µ - 3σ
µ + 3σ
Delay
Parameter value



Sensitivity of delay to parameter = T/X

## Slide 11: Modeling Sources of Variation
Liberty models at 2 process corners are required for each source of variation
All sources of variation share the same Corner1 setting
To model ‘n’ sources of variation, dotlibs @ ‘n+1’ corners are needed
If there are 3 sources of variation, P1, P2, and P3, Liberty models at 4 corners are required
For each source of variation, Finite Differencing is used to compute sensitivities
P3 opposite corner setting
P1 opposite corner setting
P2 opposite corner setting
Corner1 is same base corner for P1, P2, P3

## Slide 12: Results
SSTA NDR timing runs were compared to SSTA Liberty model runs in EinsStat (IBM’s Statistical Timing Analyzer)
SSTA Slacks in both runs are projected to a process corner using canonical model:
  i = index of sources of variation being statistically combined
  j = index of sources of variation projected to their worst corner
Analysis included systematic and random sources of variation
Slack differences are < 9ps (attributed to interpolation error)
LIB slacks (nsec)
NDR slacks (nsec)
-10% slack change
+10% slack change
RSS’d Parms
Worst-Cased Parms
Comparison of NDR
vs Lib Endpoint Slacks
Mean

## Slide 13: Results
Our experiments showed that industry standard SSTA flow can be very efficient compared to custom statistical models
Relative runtime savings increased with design size due to calculation of sensitivities in the timing graph
Design | NDR | Liberty | Improvement
Chip A | 324 s | 145 s | 2.2x
Chip B | 129626 s | 48314 s | 2.7x

## Slide 14: Conclusion & Future Work
IBM enabled a SSTA sign-off methodology for 32nm using industry standard Liberty models
Comparison of Liberty timing vs NDR timing made us confident in IBM’s SSTA methodology using industry standard models
Dispelled the notion that SSTA was only possible with NDRs
The 32nm node is IBM’s 3rd generation of ASICs in which SSTA is used for signoff, our 1st with Liberty models
Future development
  Supporting current source models
  Handling non-separability and non-linear delay variations