## Slide 1: A New Timing Closure Methodology for an SoC with Multiple On-chip Regulators
Tatsuo Shiozawa, Tetsuya Fujita, Hiroyuki Hara,
Shuuji Matsumoto, Keiko Seki-Fukuda,
Toshio Fujisawa, Masanori Kuwahara,
Toshitada Saito, Yasuo Unekawa, Mototsugu Hamada
TOSHIBA Corp. Semiconductor Company,
Kawasaki, Japan
tatsuo.shiozawa at toshiba.co.jp

## Slide 2: Introduction
Recent SoCs have multiple power domains to minimize the leakage power, and some SoCs have multiple on-chip regulators to minimize supply voltage variation and power consumption.
However, there is an unaddressed issue in the design of an SoC with multiple on-chip voltage regulators using conventional CAD tool, where P&R tool cannot foresee the timing violations in the signoff STA stage.
We propose a novel timing closure methodology, which is consistent from the P&R stage to the signoff STA stage.

## Slide 3: Timing Analysis in Single-supply Design
Capture Path
Conventional methodology
  No variation of voltage between launch and capture path.
VDD
VSS
Launch
Path
FF B
Capture
Path
FF A
Capture Path
Launch Path
Setup Timing Closure
Hold Timing Closure
Launch Path
Setup Slackconv = MIN(CLK Cycle Delay + Capture Path Delay)
– MAX(Launch Path Delay)
Hold Slackconv = MIN(Launch Path Delay) – MAX(Capture Path Delay)
Min. CLK Cycle
Delay
Max. Path Delay
@ Worst Corner
Min. Path Delay
@ Worst Corner
Max. Path Delay
@ Best Corner
Min. Path Delay
@ Best Corner
Met
Met

## Slide 4: Design Space in Dual-supply Design
Design space (D/S) at conventional STA with single-supply system
Design space (D/S) at conventional STA with dual-supply system
  Difficult to close the timing due to enlarged design space.
VMIN
VMAX
VMAX
Launch Path VDD
Capture Path VDD
VMIN
(VMAX, VMAX)
Best Corner of Library
(VMIN, VMIN)
Worst Corner of Library
VMIN
VMAX
VMAX
Capture Path VDD
VMIN
(VMAX, VMAX)
Best Corner
of Library
(VMIN, VMIN)
Worst Corner of Library
(VMAX, VMIN)
(VMIN, VMAX)
Launch Path VDD
D/S w/ single-supply system
D/S w/ dual-supply system

## Slide 5: D/S in Dual-supply Design w/ On-chip Regulators
Design space can be narrowed with on-chip regulators.
VMIN
VMAX
VMAX
Capture Path VDD
V2H
V1H
V1L
V2L
VMIN
(V1H, V2L)
(V1L, V2H)
 | Output Voltage | 
 | Min. | Max.
Regulator of Capture Path | V1L | V1H
Regulator of Launch Path | V2L | V2H
VMIN
VMAX
VMAX
Launch Path VDD
Capture Path VDD
V2H
V1H
V1L
V2L
VMIN
(VMAX, VMAX)
Best Corner
of Library
(VMIN, VMIN)
Worst Corner of Library
(VMAX, VMIN)
(VMIN, VMAX)
Launch Path VDD
(VMAX, VMAX)
(VMIN, VMIN)
D/S w/ dual-supply system
D/S w/ on-chip regulators

## Slide 6: Issues to be Solved w/ On-chip Regulators
Two issues are arose with on-chip regulators.
  How can we close the timing using conventional corner libraries with less margin?
  How can we keep consistency between the timing constraints in the conventional P&R tool and signoff STA tool?
    Conventional P&R tool cannot handle with the clock tree design of multiple-supply.
Capture Path
Launch Path
Violated
CLK Cycle Delay
CLK Cycle Delay
Path Delay
@ Worst Corner
Path Delay
@ Worst Corner
Single-supply Design (P&R stage)
Capture Path
Launch Path
Met
Dual-supply Design (Actual)
VDD
VSS
FF B
FF A
Regulator A
Regulator B
Launch
Path
Capture
Path
Min. Voltage
Supplied Area
Max. Voltage
Supplied Area
Path Delay
@ Max. Voltage
Path Delay
@ Min. Voltage

## Slide 7: Proposed Timing Analysis Methodology
Worst setup timing analysis
  Voltage Conversion Factor (VCF) is newly introduced to calculate the timing using the conventional corner libraries.
Capture Path
Launch Path
Path Delay
@ Min. Voltage
CLK Cycle Delay
CLK Cycle Delay
Path Delay
@ Worst Corner
Path Delay
@ Worst Corner
VDD
VSS
FF B
FF A
Regulator A
Regulator B
Launch
Path
Capture
Path
Capture Path
Launch Path
Min. Voltage
Supplied Area
Max. Voltage
Supplied Area
x VCFCapture_su
Setup Slackdual = MIN(CLK Cycle Delay + Capture Path Delay )
– MAX(Launch Path Delay )
Path Delay
@ Max. Voltage
Single-supply Design
Dual-supply Design
x VCFCapture_su
x VCFLaunch_su
x VCFLaunch_su

## Slide 8: D/S Covered by Analysis
By introducing VCF, the condition of conventional corner libraries are shifted to that of worst corner and best corner with on-chip regulator.
VMIN
VMAX
VMAX
Capture Path VDD
V2H
V1H
V1L
V2L
VMIN
VMIN
VMAX
VMAX
Launch Path VDD
Capture Path VDD
V2H
V1H
V1L
V2L
VMIN
(VMIN, VMIN)
Worst Corner of Library
(VMAX, VMAX)
Best Corner
of Library
VCFLaunch_hd
VCFCapture_su
VCFLaunch_su
(V1L, V2H)
(V1H, V2L)
D/S Covered by Worst Setup Analysis
D/S Covered by Best Hold Analysis
VCFCapture_hd

## Slide 9: D/S of Setup and Hold Timing
By combination of setup and hold timing analysis, the design space is covered exactly.
 | Output Voltage | 
 | Min. | Max.
Regulator of Capture Path | V1L | V1H
Regulator of Launch Path | V2L | V2H
VMIN
VMAX
VMAX
Launch Path VDD
Capture Path VDD
V2H
V1H
V1L
V2L
VMIN
(VMIN, VMIN)
Worst Corner of Library
(VMAX, VMAX)
Best Corner
of Library
(V1L, V2H)
(V1H, V2L)
Incorporation of the VCF to the timing constraints of the conventional P&R tool is the key to establish the consistent design flow from P&R stage to signoff STA stage.
Best Hold Analysis
Worst Setup Analysis

## Slide 10: How to Keep Consistency in P&R
The difference between capture clock delays at the supply voltage of corner libraries and the actual voltage supplied by on-chip regulator is incorporated in the clock uncertainty value in the P&R stage.
Launch CLK Delay
Required logic delay of
conventional method
 CLK Delay
CLK Uncertainty
Required logic delay of
this work
Launch CLK Delay
Capture CLK Delay@VMAX
Conventional
Method
Capture CLK Delay@V1H
Logic delay budget of
conventional method
This Work
CLK Cycle Delay
Launch CLK Delay
Capture CLK Delay@VMIN
 CLK Delay
CLK Uncertainty
Logic delay budget of
this work
For Setup Time
For Hold Time
Slack
Met
Violated
Met
Violated
Capture CLK Delay@VMAX
Capture CLK Delay@V2H
CLK Cycle Delay
Capture CLK Delay@VMIN
Launch CLK Delay

## Slide 11: Physical Design Result
Proposed methodology is applied to the actual product design.
Application | 802.11 a/b/g/n Wireless LAN
Technology | 90nm 6-layer metal (Cu) CMOS
Supply Voltage | Core 1.2V, I/O 3.3V
Gate Count | Logic 2.0Mgates Memory 3.4Mbits
Chip Size | 4.70mm x 4.70mm
Clock Speed | 20 / 40 / 80 / 160 MHz, 32kHz
CPU | 32-bit RISC x 1
Power Domain | 6 (3 Power Domains w/ Regulators)
Power Consumption | 80mW @ Normal 10mW @ Sleep 0.01mW @ DeepSleep
Power
Domain 3
w/ On-chip Reg.
Power
Domain 1
w/ On-chip Reg.
Power
Domain 2
w/ On-chip Reg.
Chip Features
Chip Photo

## Slide 12: Results of the New Timing Closure Methodology
Improvement in the path delay distributions
  By introducing the new timing closure methodology in the P&R stage, path delay distributions of setup and hold are substantially improved.
Violated
Conventional
This Work
47% decreased
Violated
Conventional
This Work
No violation

## Slide 13: Summary
A new timing closure methodology for an SoC with multiple on-chip regulators has been presented.
By introducing Voltage Conversion Factors (VCF), the proposed methodology does not need a new tool and a specific library.
By reflecting VCF to clock uncertainty, the methodology is consistent from the P&R stage to the STA stage.
The optimization for path delay distribution of the design with on-chip regulators is achieved.