## Slide 1
Hybrid System-Level Test Generation Approach for Heterogeneous Systems
Wisam Kadry, Alex Goryachev, and Ronny Morad IBM Research - Haifa
For more information contact:
Wisam Kadry
wisamk@il.ibm.com
2. New Challenge for System-Level Test Generation
System-level verification focuses on the integration of several previously verified components
Traditionally, all stimuli are generated by the system-level generator (CSP based)
Accelerator’s complex functions (e.g. pattern matching, cryptographic) require very complicated input
  Modeling this complex input is too costly
  Complex inputs would produce an extremely hard constraints problem
Our goal is to provide rich and valid inputs for the different
accelerators
7. Summary and Future Work
Accelerators stimuli challenge
Solution: Hybrid system-level test generation
Applied hybrid approach to an IBM SoC
Future work:
  Extend hybrid approach to other components with complex behavior (e.g., address translation)
1. Heterogeneous SoCs
Heterogeneous SoCs have complex architectures that include special purpose accelerators performing software-like tasks
4. Hybrid System-Level Test Generation Approach (cont.)
3. Hybrid System-Level Test Generation Approach
Stimuli generation is divided between the system-level and the unit level generators
The system level generator is responsible for:
  Allocating memory and initializing pointers
  (accelerator input/output buffer pointers)
  Triggering the accelerator interaction with the main
  parameters
  Creating translation path
Accelerator’s unit stimuli generator produces the
accelerators’ specific input and parameters including:
  Data for encryption/decryption
  Data for compression/decompression
  Patterns and data to be searched
Test specification
Test-case
Commands
…
Execute accelerator
with input
Unit-level
generator
System-level
generator
Instructions for unit-level
generator
HDL
simulator
Users
data
5. Hybrid System-Level Test Generation Approach (cont.)
Hybrid approach main advantages:
  Generic method that can be used for various accelerators in a Soc
  Rich accelerator input (still utilize unit verification code)
  System level scenarios that involve CPU, memory , and accelerators
  Reasonable implementation efforts
  Reuse of on-the-fly-unit checkers
Hybrid approach main disadvantage:
  Lack of redundancy: The same type of stimuli is used to exercise an accelerator at both the unit and the system levels
6. Applying Hybrid Approach to IBM Test Generator
The hybrid method was implemented in X-Gen
  X-Gen is the primary IBM system-level test generator
  Used in pSeries, zSeries, PS/3 and Xbox
Applied to an IBM Soc that has XML, Crypto, Pattern Match
and Compression accelerators
Results:
  Found numerous hardware bugs related to the accelerators
Reasonable implementation efforts:
  x10 less compared to new IO bridge