## Slide 1: Migrating HW/SW Co-verification Platforms from Simulator to Emulator
Alicia Strang Marvell Semiconductor, Inc. astrang@marvell.com | Robert C. Carden Marvell Semiconductor, Inc. rcarden@marvell.com | Ron Choi EVE-USA ronchoi@eve-usa.com
Notes: <number>

## Slide 2: The need for HW/SW co-verification
<number>
Current SOC designs usually contain one or more processors, with increasingly large, complex, multi-threaded software
To properly verify these designs, we need to run tests where both hardware and software are co-simulated
The biggest bottleneck of the HW/SW co-verification is the speed of the simulation engine.
HW/SW co-verification requires billions of cycles of simulation
Emulators offer a high-performance solution for HW/SW co-verification
Emulators execute a design in real hardware – typically custom processors or FPGAs (standard or custom)
Notes: <number>

## Slide 3: Traditional emulation environments
<number>
Typically, simulation and emulation environments are completely different, and are often incompatible:
The emulation test environment utilizes test vectors, synthesizable Verilog test code, or uses real hardware to provide the stimulus
Testbenches used in the simulation environment are class based, utilize coverage driven constrained random verification methodologies, and may leverage 3rd party verification IP
Developing 2 separate environments creates redundant work, and takes up more time in the project
Divergent development effort drives the need for a unified HW/SW co-verification platform
Notes: <number>

## Slide 4: When Simulation Meets Emulation
Notes: <number>

## Slide 5: Creating a single HW/SW co-verification platform
<number>
Goal: use the same test environment for simulation and emulation, creating a unified HW/SW co-verification platform
Encryption IP block with AXI, JTAG, and other internal interfaces
Benefits:
Re-use: Leverages the work already completed for hardware verification
  HVL verification classes/components re-usable across projects as well
Deeper Verification: Emulation performance enables simulation of orders of magnitude more cycles
  Potential to hit deeper corner case bugs and provide better coverage
HW/SW co-verification: Emulators provide simulator-like debug & control
  Enables hardware debugging with software debugging
Notes: <number>

## Slide 6: Emulated HW/SW co-verification platform
<number>
ZeBu
DUT
(Array of FPGAs)
Memory
Server
Clock
Server
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
FPGA
Reconfigurable
Test Bench (RTB)
Logic
Analyzer
Dynamic
Traces
PC / Linux
PCIe
I/F
Constrained Random
Environment
HVL Testbench
TX
RX
Hardware Transactors
Smart-ZICE
JTAG
Pod
Notes: The Billion Cycle Challenge

## Slide 7: Phase 1: HW Verification & Emulation Preparation
<number>
Describe design (Verilog) and Create
constrained random simulation environment (SystemVerilog + 3rd party AXI VIP)
Model design memories and library cells for emulation (Synthesizable Verilog)
Simulate design (w/ emulation models) and original testbench
Results Match?
Debug
No
Start
Go to Phase 2
Notes: <number>

## Slide 8: Phase 2: Initial Design Migration
<number>
Compile design (with emulation models) to emulator in HDL Co-simulation mode
Co-emulate design with original
testbench at cycle-level
Results Match?
Debug
No
From Phase 1
Go to Phase 3
Notes: <number>

## Slide 9: Phase 3: Performance Optimization
<number>
Optimize testbench performance (Replace AXI VIP with emulator transactor, modify testbench for parallelization & performance)
Compile design for transaction-based emulation. Co-emulate design with adapted testbench
Results Match?
Debug
No
From Phase 2
Done
Optimize design performance (Resource utilization/placement, clock handling)
Notes: <number>

## Slide 10: Memory modeling
<number>
Challenge: ASIC/IP Vendor simulation models may need to be re-modeled for emulation
Emulators use real HW to implement memories, while simulation models have non-synthesizable code, e.g. initial blocks, UDPs
Emulators need to handle bit/byte enables, active low/high control signals which may differ from the actual hardware
Mitigation: Commercial emulators usually have automatic/semi-automatic memory modeling tools, and accept some non-synthesizable code, e.g.
Memory inference and UDP in synthesis
Scripted memory modeling
Notes: <number>

## Slide 11: Clock Handling
<number>
Challenge: Generating the primary clocks in emulation;
Emulators must prevent clock/data races in hardware
Emulators need to handle sarious synchronous/asynchronous clock domains/phases
Mitigation: Commercial emulators typically have automatic clock generation and handling features
Can take clock input from simulator, or generate clocks internally
Automatically minimizes skew and handles clock/data races
Notes: <number>

## Slide 12: Example Clock Network in FPGA-based Emulation
<number>
The clock generator drives the primary clocks of the design
Maintains the original clock tree; no internal clock scheduling
Primary clocks are routed on a low skew network
Relative clock frequencies and duty cycles are defined at run-time
16
Clock Server
System Clock
FPGA Boards
Route to
FPGA Clock
Buffers
DUT
FPGA
Clock
Generator
Run-time clock
definitions
Delay and Filter insertion prevents races/glitches
Notes: <number>

## Slide 13: Testbench Adaptation
<number>
Challenge: Improved performance requires testbench adaptation
HVL environments (e.g. VMM, OVM) are transaction-based, but are not written for emulation
  Testbench drivers and VIP are non-synthesizable, and TB is sequentially in-sync with the design
  Higher performance in emulation requires synthesizable drivers, parallelization between TB/design
Mitigation: Leverage emulation specific transactor IP
Replace simulator VIP with emulator transactors (e.g. AXI master/slave) that separate the transaction-level API from the synthesizable driver
Synthesizable drivers and parallelized TBs can be used in pure simulation environments as well
  Future projects can use a single implementation with no adaptation required
Notes: <number>

## Slide 14: Results
Performance
2X better than simulation (Phase 1) with cycle-level co-emulation (Phase 2)
2000X improvement after design and testbench optimization (Phase 3)
Coverage
Hit functional coverage goals earlier than anticipated
Debugging
Emulator provided full waveform dumping for hardware debugging
<number>
Notes: <number>

## Slide 15: Conclusion
<number>
Creating a single HW/SW co-verification environment:
Reduced our development time
Removed the need for separate simulation and emulation testbenches
Bridged the critical gap between software tests and hardware verification
Notes: <number>

## Slide 16: Potential future improvements
<number>
Future improvements to this flow:
Develop HVL testbench environments with future emulation in mind
Improvement suggestions for EDA vendors:
Reduce need for design & testbench re-modeling
Improve integration of emulator transactors with testbench environments
  Show activity of transaction level models
  Present verification sessions in high level
Give an intuitive feel of the both software and hardware of a SOC design
Notes: <number>