## Slide 1
Reuse OVM based verification IP in a VMM environment.
Developing a typical VIP from scratch is still time-consuming and error-prone
combining component created in one methodology allowed to be used in second methodology saves time and efforts
Both VMM and OVM components are different.
Phasing in OVM and VMM are different.
Challenges
end_of_elaboration
start_of_simulation
run
extract
check
report
Elaboration
Simulation
connect
Report
build
reset_dut
cfg_dut
report
build
gen_cfg
start
wait_for_end
stop
cleanup
stop
ovm_build()
ovm_report()
User declares a wrapper that instantiates ovm_env.
OVM phase methods called explicitly by VMM.
Transparent to OVM.
Requires user intervention in the wrapper
VMM-on-Top Phasing Control
VMM Sub Env
OVM Top component
VMM Xactor
VMM Channel
VMM Channel
OVM Top component
VMM Channel
Avt_analysis_channel
OVM wrapper component
OVM Txn
VMM Txn
Instantiating OVM Component in VMM Environment
Converter class Passed in as to adapters like channel to TLM etc
Create the Mapping between fields
Static convert() method gets called w/out instantiating the converter
class ahb_rw_convert_ovm2vmm ;
static function vmm_vip_ahb_master_transaction_t convert (ahb_single_transfer_t from, vmm_vip_ahb_master_transaction_t to=null);
if (to == null)
convert = new();
else
convert = to;
case (from.m_slave_request.m_read_or_write)
AHB_READ : convert.m_enXactType = vmm_vip_ahb_transaction::READ;
AHB_WRITE : convert.m_enXactType = vmm_vip_ahb_transaction::WRITE;
endcase
convert.m_bvAddress = from.m_slave_request.m_address;
..
endclass
Static function
Data Conversion Between OVM and VMM
Converts from vmm_channel to analysis_port or analysis_export to vmm_channel
If analysis_port is connected, automatically gets from channel and writes to analysis_port
write() method sneaks transaction into channel
class ovm_top_component extends ovm_component;
typedef avt_analysis_channel #(ahb_single_transfer_t,vmm_vip_ahb_transaction_t,
ahb_rw_convert_ovm2vmm
) ahb_analysis_channel;
ovm_analysis_port #(ahb_single_transfer_t) top_wrdata_ahb_single_transfer_analysis_port;
ahb_analysis_channel ap_adapter;
virtual function void connect();
top_wrdata_ahb_single_transfer_analysis_port.connect(ap_adapter.analysis_export);
endfunction
task run();
forever
begin
top_wrdata_ahb_single_transfer_analysis_port.write(transaction);
end
endtask
endclass
Instantiate avt analysis channel
Connect analysis port to avt analysis channel
Write to Analysis port
Analysis Channel Adapter
OVM VIP Configuration
Required if OVM components needs to be configured.
If static configuration, Create the configuration class and configure at the start of configuration.
If dynamic configuration or configuration from VMM environment, then wait for VMM configuration to be generated.
Extract the configuration from VMM environment, create a corresponding OVM configuration class.
function void VMM_Xactor::configure_vip_config();
// Configure VIP as OTG
if (m_VmmUsbCfg.m_DutMode == UsbSubCfg::OTG)
`TOP.m_usb_vip_config.m_is_otg_device = 1'b1;
if ((m_VmmUsbCfg.m_UsbSubenvMode == UsbSubCfg::HS_OTG_A) ||
(m_VmmUsbCfg.m_UsbSubenvMode == UsbSubCfg::FS_OTG_A))
`TOP.m_usb_vip_config.m_is_otg_a_device = 1'b1;
else if ((m_VmmUsbCfg.m_UsbSubenvMode == UsbSubCfg::HS_OTG_B) ||
(m_VmmUsbCfg.m_UsbSubenvMode == UsbSubCfg::FS_OTG_B))
`TOP.m_usb_vip_config.m_is_otg_a_device = 1'b0;
case(m_VmmUsbCfg.m_UsbSubenvMode)
UsbSubCfg::HS_HOST, UsbSubCfg::HS_OTG_A :
// Configure Vip as HS host
`TOP.m_usb_vip_config.m_usb_interface_type = USB_SERIAL;
`TOP.m_usb_vip_config.m_usb_dual_mode_device = 1'b1;
........
`TOP.m_usb_vip_config.set_structural_index(1);
endcase
// Timing parameters
if (m_VmmUsbCfg.m_DutMode != UsbSubCfg::OTG) begin
if (`TOP.m_usb_vip_config.m_master_map == mgc_usb_v2_0_pkg::TLM) begin
if (`TOP.m_usb_vip_config.m_usb_dual_mode_device == 1'b1) begin
`TOP.m_usb_vip_config.m_usb_total_reset_interval_count = 120000/rdn_factor;
........
end
mvc_config_updated = 1’b1;
endfunction : configure_vip_config
Configuration info
From VMM
Configuration info
to OVM
initial
begin
m_usb_vip_config = new();
m_usb_vip_config.m_bfm = usb_if;
set_config_object( "*.usb_agent.*", mvc_config_base_id, m_usb_vip_config, 0);
set_config_object( "*usb*", mvc_config_base_id, m_usb_vip_config, 0);
wait (`USB_ENV != null);
wait (`USB_SUBENV != null);
wait (`USB_SUBENV.m_VMMXactor != null);
wait (`USB_SUBENV.m_VMMXactor.mvc_config_updated == 1'b1);
m_usb_vip_config.configure_interface();
end
Used when OVM configuration used in multiple components
Waiting for
VMM
Configuration
to be
created
OVM components and adapters must be wrapped together when instantiated in a VMM parent
VMM xactors instantiate and connect children in new()
  channels are constructor arguments
OVM Wrapper handles channel connections in new()
class ovm_top_component extends ovm_component;
vip_wrapper_t vip_top;
vmm_channel_typed #(vmm_vip_ahb_transaction_t) monOutChan;
function new(string name, ovm_component parent = null,vmm_channel_typed #(vmm_vip_ahb_transaction_t) monOutChan=null);
super.new(name, parent);
this.monOutChan =monOutChan;
endfunction
virtual function void build();
vip_top =new("vip_top",this);
endfunction
…
endclass
Instantiate lower ovm components
Make VMM channels as part of constructor arguments
VMM on Top – Create OVM Wrapper
vmm_env
vmm_ral_env
avt_vmm_ovm_env
user_env
ENV Class Hierarchy
Defines required
Setting +define+OVM_INTEROP on the command line will define `VMM_ENV to be avt_vmm_ovm_env instead of vmm_env
  `define VMM_ENV avt_vmm_ovm_env
If user env extends from vmm_ral_env ,we have to define VMM_OVM_ENV_BASE before vmm.sv is reading
  `define VMM_OVM_ENV_BASE vmm_ral_env
OVM can be instantiated in vmm xactor/subenv/env/ralenv
Channels will be passed through constrctor
OVM components will be created in new phase of VMM
class my_vmmSubenv extends vmm_subenv;
ovm_top_component my_vmm_dma_ahb_xactor;
vmm_vip_ahb_transaction_channel my_vmm_dma_ahb_tr_ch;
function new(vmm_vip_ahb_transaction_channel my_vmm_dma_ahb_tr_ch);
my_vmm_dma_ahb_xactor = new( "ovm_top_component",null,
my_vmm_dma_ahb_tr_ch
);
endfunction
…
endclass
Instantiate ovm top comp
Pass and connect vmm channel
Explicit call to ovm_build will call ovm phases from VMM phases
class MyvmmEnv extends vmm_ral_env;
….
….
function void build();
super.build();
`vmm_note(log, "..Entering into build method..");
`vmm_note(log, "..Exiting from the build method..");
ovm_build();
endfunction: build
endclass
User explicitly calls ovm_build() in vmm_env::build()
VMM Instantiating OVM
There was a Fatal error from the reset_dut task ,which was caused because of the thread issue in OVM kit
Interoperability guide should mention about vmm_ral_env on top as well
While changing compiler directive VMM_VERBOSITY should also reflect to OVM_VERBOSITY
  Automatic conversion OVM set_verbosity to VMM set_verbosity
Limitations/Improvements
Authors : Manoj Kumar Manu (manoj_manu@mentor.com), Ashish Kumar (ashish_kumar@mentor.com), Adam Erickson (adam_erickson@mentor.com).
The SystemVerilog functional verification community has two open-source libraries and accompanying methodologies: the Open Verification Methodology (OVM) and Verification Methodology Manual (VMM). Both OVM and VMM are intended to help designers more quickly develop verification IP (VIP) that is inherently interoperable with other IP developed in a homogenous environment. Even with these libraries’ benefit, developing a typical VIP from scratch is still time-consuming and error-prone, and integration of immature components injects significant risks to a project. To mitigate those risks as much as possible, the verification architect is compelled to find and integrate existing VIP. The choices can be very limiting if one is forced to work in homogenous environments—OVM or VMM, but not both. So, when Accellera VIP Technical Steering Committee released a beta version of the OVM-VMM Interoperability Kit [1], it theoretically expanded the pool of VIP available for integration in a functional verification environment. This poster describes the effort and results of testing that hypothesis in the real world.