## Slide 1
Quickgrade Impact
Quickgrade : An Efficient Algorithm for Managing Coverage Grading in Complex Multi-Core Microprocessor Environments
James Young Michael Sanders Vernon Lee Paul Graykowski
AMD. AMD Synopsys, Inc. Synopsys, Inc.
james.young@amd.com michael.sanders@amd.com vernon.lee@synopsys.com paul.graykowski@synopsys.com
Required for signoff
Sanity check on functional coverage points
Checkpointing progression of project
Internal tool input
Test priority list
What is Code Coverage Good For?
A Prototype Solution
Read data directly from Synopsys db (UCAPI)
Team effort between AMD and Synopsys to develop a new grading algorithm
Results:
  Incremental contribution of each test
  Cumulative running total
  Weed out tests that add no coverage
Need Prioritized Test List in 1 Month
40K+ tests
‘Greedy’ grading would take 5 months (x^2)
Would be happy with ‘good enough” results
Coverage Database
Test is loaded from list of tests
Coverage metric (toggle) is loaded
Source instances (instances)
Sum up the covered and coverable for the instance
Delta calculated and compared / summed
Repeat for each metric …
A Sample Run
Quickgrade results of 100 tests
Tgl
Incr Total
60.20 60.20 test0
7.65 67.85 test1
4.82 72.66 test2
…
0.00 83.42 test91
…
0.00 83.42 test99
Incremental value
for each test
Cumulative Total
Zero value test
Quickgrade in the Real World
40K + tests ran in 18 days – beats 5 months !!!
Graded tests used to identify test of 1k tests
  >90% toggle coverage (required)
  92.4% (actual) i.e. ‘good enough’
Usage of 1k tests
  Pattern generation
  Overnight/weekend high coverage regressions
  Picking gate simulation suite
Future Work - Ordering
Test list is order dependent
More passes in different orders improve results
  Identification of this sweet spot
Can list be sorted for better results in one pass?
  What are the criteria?
  Sorting must be linear to maintain performance / linearity of grading
Ungraded tests
Quickgrade
Coverage Database
Coverage Database
Coverage Database