## Slide 1: Synthesizable Testbench Constraint Solver: Let’s See You Simulate This!
Matthew A. Hsu Consulting
consulting@mhsu.com
www.mhsu.com
408-439-8798

## Slide 2: The Design: Synthesizable Constraint Solver
The synthesizable constraint solver is a synthesizable testbench block that solves this problem:
25% of the time generate: 0
25% of the time generate: random( 10, 1)
50% of the time generate: random( 100, 11)

## Slide 3: Algorithm: Two Randomizations Required
First we must randomize a bin
  Use tables with locations 0 to 7
  minTable and maxTable hold minimum and maximum values for each bin
  Randomize address from 1 to numValidEntries
Next, must randomize between minimum and maximum value from tables
Both randomizations require this solution
  random( M, N ) where M ≥ N
Hard part is random is non-even power of 2

## Slide 4: Block Diagram
100
100
0
10
X
X
X
X
11
11
0
1
X
X
X
X
address/data bus
3
minTable
maxTable
numValidEntries
0
LFSR
random
random
LFSR
Csolved

## Slide 5: Random Core Inputs and Outputs
Constraint Maximum
Constraint Minimum
Random Value
Solution
16
16
16
16

## Slide 6: The Math
Csolved = (Cmax – Cmin) * $random / 2^16 + Cmin
  Where:
Cmax – Cmin normalizes range to 0
$random / 2^16 is a fraction between 0 and 1
+ Cmin shifts value back up within Cmax and Cmin
Multiplier implemented with shift-accumulator
  Block takes number of cycles = highest set bit of Cmax – Cmin plus constant

## Slide 7: How to Verify With Simulation?
Given
  Cmax ≥ Cmin
For
  all values of random
  all minimum constraint values
  all maximum constraint values
Want to simply prove that
  Cmin ≤ Csolution ≤ Cmax

## Slide 8: Problems with Simulation
It will take too long
  2^16 * 2^ 16 * 2^16 combinations of inputs
Even if you wrote a ‘C’ algorithm it would take too long
The conditionals as easy, it’s the LFSR that gets you
Then the multiplier gets you

## Slide 9: Using Jasper
With default engines took overnight
Finding the right engine, solved problem in 2 hours
Found other problems while constructing constraints
  Needed to latch constraints
  Problem with reset

## Slide 10: The Magic Constraint
// hold valid until solve
reg pending_valid;
always @( posedge clock ) begin
if ( reset ) pending_valid <= 1'b0;
else if ( constraint_solve ) pending_valid <= 1'b1;
else if ( constraint_valid ) pending_valid <= 1'b0;
end
// hold constraints constant
reg [15:0] constraint1_reg;
reg [15:0] constraint2_reg;
always @( posedge clock ) begin
if ( constraint_solve & ( ~pending_valid | constraint_valid ) ) begin
constraint1_reg <= constraint1;
constraint2_reg <= constraint2;
end
end
// the property
property value_within_constraints_P;
@( posedge clock )
disable iff ( reset )
( constraint_valid |-> ( ( constraint_value <= constraint2_reg &&
constraint_value >= constraint1_reg ) ||
( constraint_value <= constraint1_reg &&
constraint_value >= constraint2_reg ) ) );
endproperty
value_within_constraints_A : assert property( value_within_constraints_P );