## Slide 1: Power Shaping Methodology for Supply Noise and EMI Reduction
Fabio Campi, Davide Pandini
STMicroelectronics, Central Cad & Design Solutions,
Agrate Brianza, Italy
Tobias Bjerregaard, Mikkel Stensgaard
Teklatech,
Copehaghen, Denmark
Notes: <number>

## Slide 2: Outline
<number>
Introduction
  Power Supply noise and EMI Interferences
  Front-End level estimation and mitigation of power supply noise
  Power Shaping
Case Study: deployment of power shaping on a supply critical microcontroller chip
  Static/Dynamic Voltage Drop analysis
  EMI behavior assessment
Conclusions

## Slide 3: Power Supply Noise
Technology scaling leads to increasing cell and power densities
  Power Integrity becomes a significant issue
Voltage scaling reduces noise margin
  Sensibility to noise peaks increases in terms of timing and reliability
Source:ITRS 2007

## Slide 4: Electro-Magnetic Interference
Growing concern for Electromagnetic Interference
  Susceptibility
  Emission

## Slide 5: Emission: Coupling Methods
Conducted noise
Radiated noise
EM wave propagates through the air
Noise propagates along supply line

## Slide 6: Single-Chip Mixed-Signal System
In RF mixed-signal designs, high frequency noise is important
D
A
Analog world Frequency domain
Digital world Time domain
Noise optimization needed in digital tool chain!

## Slide 7: Dynamic Power Shaping
February 2010
<number>
Optimizing the current demand profile
I
IC Current demand
[StdCells, Macros]
Power Delivery Network (PDN)
[Board / package / IC PG-Grid]
Power Source
Notes: Many approaches view digital circuit as a ’rigid black box of noise’ (an evil you must live with).
Hence noise reduction methods focus on optimizations in the physical domain.
The PDN is a passive filter.
By actively using Dynamic Power Shaping to change the dynamic current profile of the circuit, the noise and dynamic voltage drop characteristics of the system is improved, for any given physical PDN implementation.
As such, Power Shaping optimization is orthogonal to existing optimization
<number>

## Slide 8: Dynamic Power Shaping (2)
Power Shaping allows automated dynamic current analysis and optimization, driving the CTS process
Optimization is applied post-synthesis or after placement
Front-end current optimization is available both in time and frequency domain
Provide good correlation with post-layout results, aiding in closing the FE to BE gap
Front-end full clock cycle estimation in the standard (red) and power-shaped (green) version
Note: reference corner for FE current estimation is wc_1.2V

## Slide 9: Trial Design Description
Test Case: jtd_m10_70
Dual Core Microcontroller
Technology CMOS090 6ML
Area: 1.89x1.65=3.12 mm2
StdCells (Final): 0.283 mm2 (65 Kgates)
ClockDomains:
6408 Sinks @100 Mhz
98 Sinks @40 Mhz
Package: Lead Wing Quad Flat Pack
Due to pkg / board constraints, the design can support MAX 3 Package pins for power supply: 1 Gnd, 2 Vdd Pins, hence becoming supply-critical, especially in dynamic conditions

## Slide 10: Power Integrity Analysis
Power integrity is performed with Apache RedHawk vectorless analysis
Both static IR-drop and dynamic voltage drop are verified at wire and instance level
Modeling makes use of package spice models extracted with Ansoft’s HFSS and Q3D
Purpose of the Power Shaping deployment is to minimize static/dynamic IR-drop across the die and voltage noise transmitted to the board
<number>

## Slide 11: Back End
Back-end was performed with Cadence Encounter
Standard EXTRACTION / TIMING ANALYSIS performed @100 MHZ with Synopsys StarRC / PrimeTime, all violations were resolved
Design | Setup Margin (ps) | Hold Margin (ps) | BE StdCells Area Overhead | CT Buffers
Standard | 50 | 34 | 4.8% | 140
Power-Shaped | 18 | 2 | 4.4% | 152

## Slide 12: Power Analysis
Power Analysis was performed with Apache RedHawk
  Bc_1.32V_125C, RCMax
  Vectorless Analysis, toggle rate 20%
 | Power | Clk Power | Clk Tree Bufs | FF Clk Pins | FF Data Pins | Comb | Memory
Standard | 51.90 | 24.32 | 7.38 | 16.94 | 6.6 | 10.29 | 10.7
Power Shaped | 51.03 | 23.61 | 6.58 | 17.03 | 6.6 | 10.10 | 10.7

## Slide 13: Static IR-Drop Analysis (Wires)
Vdd,
Standard
Gnd,
Standard
Gnd,
Power
Shaped
Vdd,
Power
Shaped
Standard P&R caused congestion in the SW corner, opposite to the only gnd supply
Power Shaping induces uniform spatial spreading of ClkTree buffers and flops, resolving the issue

## Slide 14: Dynamic Voltage Drop Analysis (Wires)
Vdd,
Standard
Gnd,
Standard
Gnd,
Power
Shaped
Vdd,
Power
Shaped
Due to high package impedance, and small number of supply pads, PG-grid is inadequate in terms of DvD
Power Shaping allows local resolution of the issue during P&R, with no impact on PG-grid, package and board design

## Slide 15
Critical margin for DvD was fixed at 500mV (37.8% of reference value) Severe criticalities appear in SW corner of standard case
After Power Shaping: worst DvD value 478 vs. 630 (25% gain), no criticalities
Dynamic Voltage Drop Analysis (Instances)
Standard
Power Shaped

## Slide 16: Max Dynamic Voltage Drop Summary
Design | Instance (mV) | % of ref | Vdd (mV) | Gnd (mV) | Package Vdd (mV) | Package gnd (mV)
Standard | 629.84 | 48% | 324.1 | 310.9 | 273 | 198
Power-Shaped | 477.74 | 36% | 262.9 | 216.2 | 201 | 115

## Slide 17: Domain Current Demand & Pad Response
Power Shaping induces evident smoothing of the cells current demand (55%), leading to a consequent smoothing of the relative pad currents (28%)
Power is comparable, hence the integral of the I(t) currents is ~ same, but peak is smaller. This leads to better DvD behavior and smaller EMI

## Slide 18: Voltage Fluctuations at IC Supply Pads
Quick approximation of the EMI aggressiveness of a given IC can be provided evaluating harmonic content of voltage fluctuations at the die supply pads.
This analysis may feature only rough package modeling and no board modeling. It does not provide quantitative results but significant qualitative indications before correct package and board-related information is available

## Slide 19: Voltage Harmonic content at supply pads
The Power Shaped design provides small gains at low harmonics, that become significant after the GHz mark
Only even harmonics are reported as they are more significant due to the doubled frequency of the clock tree
 | 2F | 4F | 6F | 8F | 10F | 12F | 14F | 16F | 18F | 20F
Standard | 72.3 | 73.5 | 75.3 | 73.8 | 73.6 | 72.2 | 70.4 | 68.5 | 66.2 | 64.5
Power Shaped | 71.3 | 72.7 | 72.9 | 70.4 | 67.3 | 63.4 | 60.0 | 51.5 | 41.9 | 45.0
Magnitude (dBµV)

## Slide 20: EMI Modeling Flow
Spice-Level Simulation
Design Database
Board Database
CPM
model
Package
Dbase
HFSS
RedHawk
PowerSI
Pkg
model
V(t)
Waves
FFT
Board
model
EMI SPICE-level
compact model

## Slide 21: Voltage Fluctuations at EMI Measurement Pins
According to IEC regulations, conducted EMI is measured as the frequency spectrum of the voltage fluctuation at a specific measurement pin of a standardized board
The spice model of the board, extracted by SIGRITY tool suite, is plugged in a spice macro-model comprising Chip Power Model generated by Apache RedHawk and Package model extracted by Ansoft’s tools
The plot shows time-domain voltage fluctuations at the board pin representing EMI measurement at power supply pad

## Slide 22: Voltage Harmonic content at EMI Measurement Pins
Full EMI simulation confirm the expected trend: EMI behavior of the Power shaped design shows advantages, that become significant after the GHz mark
 | 2F | 4F | 6F | 8F | 10F | 12F | 14F | 16F | 18F | 20F
Standard | 77.7 | 65.5 | 64.8 | 61.6 | 57.9 | 62.7 | 61.5 | 54.2 | 50.9 | 47.5
Power Shaped | 77.1 | 64.7 | 62.9 | 56.7 | 52.7 | 53.1 | 50.0 | 36.6 | 19.8 | 21.8
Magnitude (dBµV)

## Slide 23: Conclusions
Power Shaping proved an interesting design option for limiting digital core supply Dynamic Voltage Drop and Electromagnetic Interference
Experiments on a reference design provided
  28% reduction of IC pad current peaks
  25% reduction of Max Dynamic Voltage Drop
  55% reduction of IC pad voltage fluctuations
  3 to 20 dBµV reduction of digital core conducted EMI harmonics (with maximum effect in the 1 to 2GHz range)
From the EMI standpoint results are encouraging but only relevant at high frequencies
For this reason Power Shaping completes well with Spread Spectrum Clock, or Decap insertion, that reduce the lower harmonics
Power Shaping showed small impact on the physical design quality, and no impact on PG-grid, package and board design, so that it can be applied as non-invasive mitigation technique or “last-minute life-saver” in case of DvD/EMI issues
This is especially true in case of strict board-package-pad frame specifications which are usual for low-cost, average-low volume products