## Slide 1: Power Noise Mitigation Strategy from RLT Perspective on MTCMOS Design
Presenter: Yong, Lee Kee (lee.kee.yong@intel.com)
Tan, Fern Nee (fern.nee.tan@intel.com) Lee, Chee Siong (chee.siong.lee@intel.com)
Penang Design Center (PDC) Intel Inc. Penang, Malaysia
Notes: <number>

## Slide 2: Disclaimer
The flow results discussed have been simulated and are provided for informational purposes only. Results were derived using EDA software tool that run on an Intel’s VLSI design. Any difference in VLSI design or software tool or configuration or flow may affect actual results.
No computer system can provide absolute security under all conditions. Intel® Trusted Execution Technology (Intel® TXT) requires a computer system with Intel® Virtualization Technology, an Intel TXT-enabled processor, chipset, BIOS, Authenticated Code Modules and an Intel TXT-compatible measured launched environment (MLE). The MLE could consist of a virtual machine monitor, an OS or an application. In addition, Intel TXT requires the system to contain a TPM v1.2, as defined by the Trusted Computing Group and specific software for some uses. For more information, see http://www.intel.com/technology/security.
Intel and the Intel logo is a trademark or registered trademark of Intel Corporation or its subsidiaries in the United States and other countries.
Performance tests and ratings are measured using specific computer systems and/or components and reflect the approximate performance of products as measured by those tests. Any difference in system hardware or software design or configuration may affect actual performance.
Intel does not control or audit the design or implementation of third party benchmark data or Web sites referenced in this document. Intel encourages all of its customers to visit the referenced Web sites or others where similar performance benchmark data are reported and confirm whether the referenced benchmark data are accurate and reflect performance of systems available for purchase.
*Other names and brands may be claimed as the property of others.

## Slide 3: Agenda
Introduction & background
Power gating Management Controller
In-Rush Current Prediction
Power Delivery Network Modeling
Pre v.s. Post Silicon Correlation
Summary and conclusion
Notes: <number>

## Slide 4: SOC Power Gating Scheme
Shut off / Power Gate un-used logic to save stand-by power
Notes: <number>

## Slide 5: Leakage And Power Gating
Header Cell
(PMOS)
To pkg, pcb, battery
From Power Management Controller (PMC)
Gated Vdd
Post 90nm technology SOC low power dominated by sub-threshold leakage.
Decreasing the length of transistors from transistor scaling reduces the depletion channel length and hence increases the leakage current.
Sub-threshold leakage current also increases with temperature at each process node hence created a compounding effect.
Power Gating using MOS devices to form a switch between an external and internal power network is a well known and very effective technique to control leakages of logic gates.

## Slide 6: SOC with Distributed Power Gating FloorPlan
Un-used blocks can be shut off to save power based on usage model.
Need to control power ungate noise rippled to adjacent ON logics.
nvm_core_pgd1
Dynamic On-Off
IO-ring

## Slide 7: Simulated Power Bin-split Modeling
High Power bucket
Medium Power bucket
Low Power bucket
Power are inversely proportional to speed.
Platform cooling solution most of the time are different for High/Medium/Low Power parts (market segment driven).
Applying Power Gating to reduce standby power is essential
to adjust targeted volume
Notes: <number>

## Slide 8: Power Integrity Design Challenges on Power Gating Implementation
Static IR drop
  On / Off stage
Dynamic Power Noise
  Instantaneous power ungate Noise
ST1ENB
Vcc
ST2ENB
Vcc
Vcc
ST3ENB
PGDST1
PGDST2
PGDST3
Vcc
PGD2
. . .
CORE
2ENB
V1ENB
VccA
VEENB
VccA
VccA
V3ENB
PGDV1
PGDV2
PGDV3
VccA
PGDE
. . .
EENB
ASW
PGDE
PGDV3
PGDV2
PGDV1
1.1
VASW
PGD2
PGDST3
PGDST2
PGDST1
VCCMIN = 0.93

## Slide 9: Agenda
Introduction & background
Power Gating Management Controller
In-Rush Current Prediction
Power Delivery Network Modeling
    Pre v.s. Post Silicon Correlation
Summary and conclusion
Notes: <number>

## Slide 10: Power Gate Design Implementation
The distributed power gating methodology used are header cells (PMOS) where the source are connected to the external power network
PGDST1, PGDST2, and PGDST3 are isolated to be turn on/off independently.
The power enable signals are routed from the PMC (Power Management Controller) where it centrally controls the ON/OFF of the respective Power gates with dedicated logics.
Header Cells PMOSes are replicated and placed evenly within the power gated region to reduce localized IR drop.
Each Power enable signals daisy-chain connected to the PMOSes to reduce the di/dt impact.
ST1ENB
VccD1
ST2ENB
VccD1
VccD1
ST3ENB
PGDST1
PGDST2
PGDST3
. .
DOMAIN1
VccD1
ST
DD
Pkg Cap
Pkg Cap
ME
Pkg Cap
SI Die
Board
PKG
DOMAIN1
DOMAIN2
. . .
VRM
VE
ST1enb
ST2enb
ST3enb
PMC

## Slide 11: Central Arbiter Implementation
VccC
Biggest guy
8ns
VccA
VccB
VccD
VccF
VccG
VccH
VccI
5us
Sleep State
8ns
8ns
8ns
8ns
8ns
8ns
8ns
Wake State
VccE
Notes: There will be one power gating controller instance per power gate domain. Hence, there can be several instances of this local power gate controller depending on project implementation. Figure 4 illustrates a simplified FSM employed by local power gate controller to sequence a particular power domain into and out of power gating mode. The central power management controller (PMC) acts to grant power transition requests from various power gate domains such that power delivery noise is minimized through a programmable request grant spreading mechanism. In a simplistic implementation, the grants can be spaced to be one clock apart, as illustrated in Figure 5. However, the implementation is not restricted to one clock grant spacing. It can be set to other grant spacing, as determined by the pre-Si simulation of power delivery noise during power gating/ungating event.
<number>

## Slide 12: Agenda
Introduction & background
Power gating Management Controller
In-Rush Current Prediction
Power Delivery Network Modeling
Pre v.s. Post Silicon Correlation
Summary and conclusion
Notes: <number>

## Slide 13: CPT Power Ungating Rush Current Design
STAGE1
Behavioral Model
-75% Confident
-RTL based.
STAGE2
Physical Model
85% confident
Physical placement and unrouted.
Delay
Delay values from
8ns to 80ns
FINAL/ECO
Optimized Physical Model
-95% confident
- Physical Optimized
 | Behavioral Modeling | Physical Model | Optimized Physical Model
Availability | As soon RTL coded with Pfet instantiation and gated region gate count available | Post placement, unrouted DB. PreCTS PV. Manual overrides on daisy chain timing. | Post timing optimized. Physical Chain stitch timing propagated. Enable slope calculated from PT.
Accuracy | 75%. Typical corner @ room temp only | 85%. Fast & slow with Hot and cold | 95%. Fast & slow with Hot and cold
Simulation Time | 1-2 days | 3-4 days | 1 week +
Ease of integration to Pkg analysis | same | same | same

## Slide 14: PFET Stitch & Optimize Flow
Pfet stitching Flow Inputs:
  Target buffers need to be inserted
    More #buffers meaning more time delay in daisy chain.
    Need to trade off with congestion and area utilization overhead and tune from milestone to milestone.
  Pfet order list based on physical placement
    Extract from partition level floorplan.tech
Buffer inserted are SIR type which will auto route to ungated rails
  Buffers are magnet placed close to it’s Pfet_enb pins
  Buffers are pre-placed on optimized location but legalized together with other logic cells.
Screen shots of pfet order are auto saved.
Netlist Release
FloorPlan
PS
CTS
PostSyn
PostCTS
PFET
Auto-Buffering
Pfet list
FloorPlan
PFET Auto-Buffering
Re-stitch
Pfet list
PS
Pfet checks
Pfet checks

## Slide 15: Example Daisy Optimization Results
Trial3
Final
fast
slow
Current
Time

## Slide 16: Agenda
Introduction & background
Power gating Management Controller
In-Rush Current Prediction
Power Delivery Network Modeling
Pre v.s. Post Silicon Correlation
Summary and conclusion
Notes: <number>

## Slide 17: Characterization of PDN Z(f)
Silicon
Package
Motherboard
Voltage Reg.
Notes: <number>
Today, what we are good at is performing the modeling of a full package and motherboard platform. Modeling the physical design is not tough. Each models can be broken down into components, and discretely modeled as LRC parameters.
The major components can be either modeled as lumped or distributed. For accuracy enhancement, 2.5D models have been widely applied. Micro level details on package such as vias, voids and pitch changes are studied to an extend our understanding on their impact, on both AC inductance and DC IR drop.

## Slide 18: What-if Power Noise with Various Package Options
Vmin1
Vpp
No DSC, No Runway
DSC + Runway
Runway Only
DSC Only
Vmin2
 | Vmin (Ungate) (V) | Vpp (Ungate) (mV)
No Cap | 0.892 | 152.07
Runway Only | 0.954 | 132.43
DSC Only | 0.957 | 117.61
Runway+DSC | 0.967 | 111.45
Design Spec

## Slide 19: What-if Scenario on Various Turn on Time
Central controller
Clk period = 8ns
Clk period = 32ns
Clk period = 48ns
Clk period = 70ns
Lowering Peak-2-Peak voltage noise from Configuration Adjustment

## Slide 20: Agenda
Introduction & background
Power gating Management Controller
In-Rush Current Prediction
Power Delivery Network Modeling
Pre v.s. Post Silicon Correlation
Summary and conclusion

## Slide 21: Full Chip Power Map
 | (default all PGD are enable) | U3 PGD disable | U2 PGD disable | P2 PGD Disable | ST2 PGD disable | ST3 PGD disable | V PGD disable | N PGD disable | All PGD disable
VCC(A) Silicon Mea. | 100.00% | 91.84% | 95.16% | 74.54% | 99.73% | 99.73% | 92.04% | 86.74% | 47.41%
VCC (A) Simulation | 100.00% | 81.04% | 89.50% | 80.54% | 99.40% | 99.53% | 92.89% | 93.76% | 48.66%
Infrared Emission Microscope
Before Power Gating
After Power Gating
Good correlation for overall power saving from simulation to silicon measurement

## Slide 22: Measurement Setup
07/30/26
<number>
Test probe pads are prepared on package
On package Probing needs Micro-Probing system (Camera Video with Arm Station)
2-Port VNA Micro Probe setup for Cdie Measurement
High bandwidth and High Impedance Scope

## Slide 23: On-Die Voltage Sampling Methodology
VCC, Gated:
Voltage sampling is done by placing an inverter with input tide low (output driven High) with-in the high IR drop risk region. No buffering on output signals to MUX at IO
MUX select are programmed through DFT register via JTAG interface.
MUX output signal are traced out at board and probed with High Impedance Scope.
VCC, Ungated:
Package Trace out with test landing zone for probing at package level.
Silicon Measurement Setup
[0:29]
30-to-1 MUX
JTAG Interface
To High Impedance Scope observability
SUS
CORE
SUS
AW
CORE
-
PG
CORE
With Internal Pwr Gating
AW
-
PG
Board PS
SUS
CORE
PFET
PFET
VR
CORE-PG
CORE-PG
CORE-PG
CORE-PG
PFET
PFET
PFET
PFET
Probe Point

## Slide 24: Silicon Correlation – VCC,Gated Power Up
Notes: <number>

## Slide 25: Silicon Correlation - VCC,Ungated Power Up With Daisy-Chain and Central Control Staggering
Silicon Measurement
Simulation
52.64ns
44.25ns
Design Spec
Design Spec
Silicon Measurement
Simulation

## Slide 26: Putting It All Together…
Design Spec
10X Reduction in effective Peak-2-Peak Voltage Noise

## Slide 27: Agenda
Introduction & background
Power gating Management Controller
In-Rush Current Prediction
Power Delivery Network Modeling
Pre v.s. Post Silicon Correlation
Summary and conclusion

## Slide 28: Summary and Conclusion
  To save power, many SOC products are employing Power Gating within its core partition. It causes
    increase in DC IR drop
    power un-gating events cause sufficiently large power delivery noise droop
  This paper presented a complete design and analysis methodology and presents the simulation results for a low power design starting from early planning stage to physical implementation.
  Performance improvements of about 10X were seen through the design optimizations.
  Various Design techniques has been successfully presented to scale the di/dt to meet performance goal.
  This paper has successfully illustrated a comprehensive top down design methodology to enforce power savings on a computing system; which could be leveraged across the industry aiming with similar interest.
  Last but not least, the post-silicon validation data has shown a very good match to as close as 96% correlation

## Slide 29: Next Step
Enhance detail on-die Cap modeling especially the substrate Cap which causes the rise time discrepancy.
Investigate on more details 3D package modeling instead of Quasi-static 2.5D model.
Investigate on AC voltage droop to timing impact during power ungate event on Always on logics.

## Slide 30: Thank you

## Slide 31: Acknowledgement
Thanks to all members of the project team who has contributed directly or indirectly to the success of the PCH core current development method

## Slide 32: Legal Disclaimer
No computer system can provide absolute security under all conditions. Intel® Trusted Execution Technology (Intel® TXT) requires a computer system with Intel® Virtualization Technology, an Intel TXT-enabled processor, chipset, BIOS, Authenticated Code Modules and an Intel TXT-compatible measured launched environment (MLE). The MLE could consist of a virtual machine monitor, an OS or an application. In addition, Intel TXT requires the system to contain a TPM v1.2, as defined by the Trusted Computing Group and specific software for some uses. For more information, see http://www.intel.com/technology/security.
Intel and the Intel logo is a trademark or registered trademark of Intel Corporation or its subsidiaries in the United States and other countries.
Performance tests and ratings are measured using specific computer systems and/or components and reflect the approximate performance of products as measured by those tests. Any difference in system hardware or software design or configuration may affect actual performance.
Intel does not control or audit the design or implementation of third party benchmark data or Web sites referenced in this document. Intel encourages all of its customers to visit the referenced Web sites or others where similar performance benchmark data are reported and confirm whether the referenced benchmark data are accurate and reflect performance of systems available for purchase.
*Other names and brands may be claimed as the property of others.