## Slide 1
DAC 2010 User Track
Ringing In and Out:
Automated Creation of the SoC I/O Ring
Ayon Dey a-dey@ti.com
Bob Maaraoui bmaa@ti.com
Sean Boylan sean.boylan@duolog.com
David Murray david.murray@duolog.com
Notes: <number>

## Slide 2: What is an I/O Ring?
I/O Ring
Test
MUX
Functional
MUX
CTRL
&
CFG
BSR
Chain
Power
Isolation
I/O Cell Control
Slew,
Power,
Reset,
DFT
All logic/wiring between Core and Chip Pins
  Logic and wiring for pin muxing
  Logic and wiring for I/O cell DFT, PVT and slew control
  Logic and wiring for boundary scan
  Power isolation logic
  Chip I/O configuration
  Wiring for I/O cell daisy chains
  Timing critical paths
  Logic and wiring for input protection
Core Interface
Functional and test pin data
BSR control
Pin DFT control
I/O cell control
Pin configuration
DaisyIn
DaisyOut
100s of Pins
1000s of signals
Single Pin’s I/O Logic
Notes: Explains what is an I/O Ring and the types of logic which is automatically generated.

## Slide 3: Increasing Complexity and Multiple Constraints
Increasing complexity
  More pin sharing
  Complex I/O cells
  More granular I/O cell control
Multiple constraints
  Constraints from multiple sources need to be captured and managed
I/O
Specification
I/O Integrator
Complexity
Gordon Moore
DFT
Package and
Timing Constraints
Software
I/O Configuration
Marketing
Design For Test
Scenarios
STA / Layout
Multiplexing
Scenarios
Architect
Power, Reset, Control
Requirements
IP Integrator
Complex I/O Cells
Notes: More pin sharing
  Complex I/O cells
  More granular I/O cell control
    Design for test (DFT)
    On-the-fly tuning to account for process, voltage and temperature (PVT) variations
Constraints : Unless constraints are properly managed, they may conflict or be omitted

## Slide 4: Current Design Flows
Manual or semi-automated I/O flow
  No centralized view
    Everyone working from a different specification
  Every project uses ad-hoc flows
    Large investment required to maintain flow
Consequences of current design flows:
  Critical path/Critical bugs
    Design bugs at I/O level halt/slow system validation
    Silicon bugs can kill the chip
  Resource drain due
    Multiple spins of I/O Logic
  Reuse is tough
Notes: <number>
<footer>
<header>
<date/time>
Problems with the current design flow

## Slide 5: From simple to highly complex pin logic
CORE
BSRs
Simple
Muxes
Test
MUX
Functional
MUX
CTRL
&
CFG
BSR
Power
Isolation
I/O Cell Control
Slew,
Power,
Reset,
DFT
CORE
Notes: The slide initially shows how simple mux logic used to be in the past. A few simple muxes and BSR cells. Today we see more usage for I/O cells, more multiplexing which can also lead to a large increase in complexity within the I/O cell handling electrical characteristics such as power, skew, test, timing etc. We will look at some of these problem areas.

## Slide 6: Handling Complex Pin Multiplexing
Pad c
Pad a
Pad b
Pad d
Problem
  Many-to-many multiplexing
  Functional and test muxing
  Selectable mode priorities per pin
  Full input, output and bidirectional
  Stringent power constraints
Solution
  Full functional and test muxing capability
  Partition mux logic based on core power domains
  Flexible timing versus control priority
  Input protection ensures default value input when core input has no source pin
  Allow custom mux insertion for critical paths
CORE
Module1
Module2
Module3
Notes: Pin multiplexing is one of the primary features in an I/O Ring.

## Slide 7: Handling Complex BSR Control
Problem
  1000s of BSRs with multiple control signals needed
  Multiple chains needed for more granular BSR Cell control of critical I/O cells.
Solution
  Allow insertion of BSR cells on any I/O cell signal. Allow custom BSR cells to be inserted
  Allow a range of BSR chains
    Multiple master chains
    Multiple sub-chains per master chain
    Segmented, parallel chain architecture
  All BSR control can be shared

## Slide 8: Handling Complex Cell Control
Problem
  Large volume of I/O cell + increasing control on each I/O cell
  Single wire per I/O control port is not practical
  Difficult / error prone to insert DFT glue logic manually
  Complex daisy-chain requirements
Solution
  Group I/O cell control
    Single register control for a group
    Based on I/O cell placement in I/O Ring or Pin level properties
  Use Rules-based connectivity to connect and auto-insert DFT logic.
  Fully configurable daisy chain solution
CTRL
&
CFG
I/O Cell Control
Slew,
Power,
Reset,
DFT
Daisy-Chains
Notes: Reducing I/O Congestion through the use of grouped I/O Cell control.
Grouped control of the I/O cell ports is enabled through the use of pin level properties and the I/O cell’s placement on the I/O Ring. These properties are then be used in rules based connectivity to automate the connectivity. DFT mux equations can be inserted on the connectivity path so that the I/O cell control signals can be modified for test purposes.
Signal congestion in the I/O ring is a common problem for back-end flows. This problem is reduced by allowing “group control” over the I/O, depending on I/O placement. The automated flow supports “rules-based” connectivity where the placement information is exploited to create groups of I/Os belonging to a common functionality/protocol. These groups are assigned a common control from the core, based on the order of the I/O pad, thereby making the entire I/O integration process “placement-aware”. This method of tactical I/O grouping and rules-based connectivity reduces the number of control signals and thus the amount of congestion in the I/O ring.

## Slide 9: Flow Integration Using IP-XACTTM
Core
Module 1
Module N
I/O
Configuration
1) Import IP-XACT Core signals as core pins
BSR
PWR
IO
2) Package IP-XACT
IP interfaces for I/O,
BSR, PWR cells
3) Generate IP-XACT I/O configuration registers
4) Generate IP-XACT flat synthesised
I/O logic
Hierarchy Creation
and Power Cell
Insertion
out
oen
in
Core Pin
Notes: Standardized Interface with IP-XACT™
Use IP-XACT™ as a standardized communication mechanism
It is the best standard for Capturing I/O Cell primitives (I/O, BSR, PWR)
Easily exchange data it depend flows
  I/O Configuration Register Definitions
  Power And Voltage Domain Properties
  SoC Core Definition
Import/Export IP-XACT™ 1.1, 1.2,1.4
  Import - Components, Ports
  Export - Components, Ports, Connectivity, Registers, Bitfields

## Slide 10: Coherent Data
Excel
I/O Specification
User Interface
IP-XACT
VHDL / Verilog
Import
IP -XACT
VHDL / Verilog
Export



Capture
  On the fly checks when entering data in the GUI
  Run Coherency Checks suite at any time
Generate
Fix Coherency Check errors before generation

Documentation
Software
BSDL
Test bench
Custom Generators
Import/Export data checked for errors
Cannot import bad data
Cannot export bad data
Notes: Correct-by-Construction methodology, ensures coherent data on import, data entry and generation.
No output can be generated unless the Coherency checks pass.
Coherency Checks can be run at any time.

## Slide 11: Generator Framework
Users can create
their own generators
T(X)
T(X)
T(X)
T(X)
T(X)
T(X)
Pre-synthesis Coherency Checks Ensure that the captured I/O Specification is coherent
Post-synthesis Coherency Checks
Ensures HDL is well constructed
E.g. Are all Inputs connected?
Synthesised I/O Logic
SMART
Templates
Generator API
Access both I/O specification and synthesised I/O logic
Published
System TB
Infrastructure
Die Diagram
I/O Ring TB
Package Diagram
I/O Configuration
RTL, C Code, IP-XACT
BSDL
Documentation
Excel, RTF
Notes: Smart template are used to create any type of generator output
The generator API has been published allow access to both the captured I/O Ring specification data as well as the synthesised I/O Ring logic.
Users are free to modify existing templates or else create new templates in order to generate different types of output.

## Slide 12
Results
Notes: <number>

## Slide 13: Statistics
Device description
  Application processors for general purpose, multimedia and graphics processing targeting OEMs who wish to have advanced user interfaces, web browsing, enhanced graphics and the multimedia experience
Outputs
  ~240K lines of I/O Ring RTL
Generation times
  Coherency checking time < 2 minutes
  Generation time = average 3 minutes / generator

## Slide 14: Metrics
Effort savings due to automated I/O integration flow:
No of I/O Specification bugs caught in I/O control logic:
SoC | Total # I/O pins | Total # I/O control signals | Man month effort | Savings vs manual flow
SoC1 | 423 | 3144 | 6 MM | 7 MM
SoC2 | 385 | 7472 | 7 MM | 12 MM
SoC | % of I/O specification bugs caught by verification | % of I/O specification bugs caught due to inbuilt coherency checker
SoC1 | 16% | 84%
SoC2 | 8% | 92%
Notes: The automated flow has been used on approximately 20 SoC designs at TI to-date. These designs typically have between 50 and 150 blocks of IP with many thousands of connections between the IP cores and the SoC pads. Some teams have used the solution primarily for automatic generation of the I/O fabric RTL and for power management integration, including the automatic insertion of isolation cells and level shifters based on the power and voltage domain in which the I/O pad resides. Others have made extensive use of the built-in generator framework to generate other collateral such as verification testbenches and specification documents, or to translate data from csv, xml or excel formats to IP-XACT.
This slide shows the results from two recent SoCs.

## Slide 15: Planned Future Enhancements
Power / Voltage Domain Flows
  Hierarchy creation based on voltage domains
    Automatic association of voltage and power domain controls of the I/O control and I/O pads based on power/voltage domains of the interacting IP present in SoC core
  Support for UPF and CPF power standards
Generation of formal verification properties
Notes: Automatic association of voltage and power domain controls of the I/O control and I/O pads based on power/voltage domains of the interacting IP present in SoC core will facilitate hierarchy creation based on Voltage and Power domains. The hierarchy manipulation flow can be seamlessly integrated with the SoC core integration flow if both are based on IP-XACT. For legacy flows not based on IP-XACT this can be a significant integration challenge.
Formal verification based on the generation of formal verification properties from the actual connectivity within the SoC using languages such as PSL (Property Specification Language) from Accellera. These properties could be generated automatically from the I/O fabric database and therefore help to reduce the overall verification effort.

## Slide 16: Conclusions
There is increasing pressure to provide an early and robust I/O Ring of ever more complex systems.
A single-source, executable specification can be utilised to provide a correct-by-construction methodology
Current focus is on auto-generation of I/O Ring RTL allowing rapid design change turn-around
Increasing the automatic creation of system validation collateral will accelerate the time to market
A good solution can ensure fewer bugs @ less cost in less time and with less resource drain

## Slide 17: Thanks for your time!