## Slide 1: An automated flow for high performance asynchronous digital controllers
Enea Dimroci - STMicroelectronics

## Slide 2: Motivation
Asynchronous design is a unique technique to reach high performances in digital controllers
Handshake protocol bounded on a specific region
Static Timing Analysis automation to allow a faster timing closure
Reduction in design time while meeting the strict timing constraints
Notes: Asynchronous Logic Design is a unique technique to reach high performances in digital controllers for some analog IPs in Analog-On-Top applications.
Automated regioning flow for the asynchronous digital controller with timing constraints definition allow the SoC for high performances while reducing the design time of this kind of circuits.
Static Timing Analysis has to be properly defined for asynchronous digital controllers and the automation of this process may allow a faster timing closure for these kind of control logic.
This automated flow is resulting in a significant reduction in design time while meeting the strict timing constraints.
The automation of this flow is critical in order to obtain a tailored block for the final application.

## Slide 3: Main idea
Analog designers provide the specification of the controller
The automated flow deeply analyzes the inputs
Generate scripts for:
RTL description
Synthesis with timing constraints
Regioning scripts for the digital implementation
Static Timing Analysis for Sign-Off
Notes: Analog designers provides the specification of the controller:
  Flow Chart for the Controller
    Used to define the behavior of the asynchronous controller.
  Timing Specification
    Used to set the timing constraints of the architecture in order to meet the specifications.
The Automated Flow generates the needed files to implement the timing constraints, Regioning and STA:
  RTL Description
    SystemVerilog description of the asynchronous controller architecture.
  Timing Constraints Definition
    Constraint definition for the synthesis phase to meet the timing specifications.
  Regioning scripts for the digital implementation
    Scripts definition for the Back-End phase implementing a soft Regioning of the submodules in order to reduce as much as possible parasitics due to the implementation.
  Static Timing Analysis scripts with PrimeTime
    Scripts definition to check the timing performances of the post-layout netlist.

## Slide 4: Automated flow outputs
RTL definition
The architecture of an asynchronous digital controller is made by three main elements:
Timing constraints definition
The timing constraint is defined setting the maximum delay from point to point in the design
Regioning technique in digital implementation phase
The handshake protocol is confined to a specific region minimizing the parasitics effect related to the routing
STA for asynchronous logic
The technique used is the unrolling of the netlist from input to output pins for all possible input-output paths
Notes: RTL Definition:
  The architecture of an asynchronous digital controller is made by three main elements:
    Input Logic : to trigger transitions between states under some logic condition.
    Handshake Control Logic : to implement the 4-phase handshake protocol in order to evolve properly between states
    Output Logic : to drive the output signals
Timing Constraints Definition:
  The timing constraint are defined setting the maximum delay from point to point in the design
Regioning Technique in Digital Implementation Phase:
  This technique divide the chip into different regions
  These different regions can be optimized for high performances
  Regioning in asynchronous digital controllers fit well the achievement of maximum performances in terms of latency
  The handshake protocol that makes this architecture working can be confined to a specific region minimizing the parasitics effect related to the routing
  The input and output logic are placed closed to the I/O buffers to minimize latency
STA for Asynchronous Logic:
  Static Timing Analysis can be applied to asynchronous logic although it is full of combinational loop
  The technique used is the unrolling of the netlist from input to output pins for all possible input-output paths

## Slide 5: Tools and key evidence
Front to back with Synopsys Design Compiler:
Regioning technique with Cadence Innovus during digital implementation:
Static timing analysis for asynchronous circuits with Synopsys PrimeTime:
Chart: I/O Latency [ns], BCD8 5V
| Best Condition | Nominal Condition | Worst Condition
No Regioning | 11.2 | 15.1 | 20.7
With Regioning | 9.3 | 13.7 | 19.2
Notes: Front To Back with Synopsys Design Compiler:
  Timing constraint are put in .tcl file and given to the synthesis tool.
  The specific command used is “set_max_delay -from [from_list] -to [to_list]”.
  Check with report_timing command after synthesis.
Regioning Technique with Cadence Innovus during Digital Implementation:
  Placement without Regioning has shown a violation on the timing constraint.
  Regioning of the submodule can overcome the issue because it minimize the parasitic delay added by the routing of the standard cells.
Static Timing Analysis for asynchronous circuits with Synopsys PrimeTime:
  STA and timing closure is implemented automating the generation of primetime scripts that set the case analysis in order to break the combinational loops and find out the I/O latency of the post layout netlist and check if constraints are met.

## Slide 6: Summary
The handshake protocol is enhanced in terms of latency
This automated technique allows high performances while also saving design time
This approach has been successfully applied to a large number of designs, resulting in a significant reduction in design time and effort to meet constraints
1
2
3

## Slide 7: Thank You