## Slide 1: Novel Numerical Hardware Design Methodology From machine readable specification to optimized RTL
Theo Drane, Bill Zorn, Samuel Coward
Accelerated Computing Systems & Graphics

## Slide 2: Motivation
C++
Model
Optimized
RTL
What if we could
specify, simulate, model, implement & optimize
1000s of designs in a day?
Specification
Natural Language
Non-Bit Accurate
Hand Crafted
Machine learning has introduced
a zoo of number formats.
Typically, one design will be refined over weeks/months.

## Slide 3: Specify
We need to be able to specify: multiple number formats float/fixed/integer…
multiple precisions FP32, FP16, BF16, FP8…
the right answer infinitely precise values
and execute machine readable specification
FPCore
Open-Source Numerical Specification Language
X
+
+
X
+
+
a*b+c
a*b+c+d
a
b
c
d
a
b
c
d
a
b
c
d
a
b
c
d
FP8
FP16
FP16
(FPCore f1 (a b c d) :precision (float 5 8) (! :precision (float 5 16) (+ (* a b) (+ c d))))
(FPCore f2 (a b c d) :precision (float 5 8) (! :precision (float 5 16) (+ (fma a b c) d)))
(FPCore f4 (a b c d) :precision (float 5 8) (! :precision (float 5 16) (cast (! :precision real (+ (* a b) (+ c d))))))
(FPCore f3 (a b c d) :precision (float 5 8) (! :precision (float 5 16) (cast (! :precision real (+
(! :precision (float 5 16)
(* a b)) (+ c d))))))
FP16
FP16
FP16
FP16
FP16
(float 5 8)
Exponent Width
Total Float Bit-Width

## Slide 4: Simulate
4
(FPCore f1 (a b c d) :precision (float 5 8) (! :precision (float 5 16) (+ (* a b) (+ c d))))
Uses MPFR - arbitrary precision
floating-point reference library
(FPCore f2 (a b c d) (+ (* a b) (+ c d)))
FPCore
Simulator
Golden Reference
Current
Proposed, precision=5
Current
Golden Reference
Proposed, precision=12
Application-Level Visualization
(FPCore f3 (a b c d) :precision prec1 (! :precision prec2 (cast (! :precision prec3
(+ (! :precision prec4
(* a b)) (+ c d))))))
How do we know
how to set internal
precisions?
Average
number
of correct
bits
Dummy Cost Metric = Sum of All Precisions
FPCore1
FPCore2
These plots came from simulating ~100,000 designs in <2 hours.
Pareto frontier forms in <10 mins.
Provides numerical property feedback in minutes.
10
10
16
Adding 100s of bits of extra internal precision doesn’t help get above 10 correct bits
=> Numerically Unstable
[prec1,prec2,prec3,prec4]

## Slide 5: Model
5
Bit-accurate, Simulation & Formal Verification friendly,
optimized C++ atomics or look-up tables for unknown functions
(use ac_int for large integer types)
C++
ASL
SystemC
Simulator
(FPCore ((! :precision (float 5 16) x)
(! :precision (float 5 16) y))
(! :precision (float 8 32)
(- (! :precision (float 11 64) (+ x y))
(! :precision (float 11 64) (- x y)))))
ifp::UFloat<8, 32> f(const ifp::UFloat<5, 16>& x, const ifp::UFloat<5, 16>& y,ifp::RoundingMode rnd_out) {
return ifp::fp_sub<ifp::UFloat<8, 32>>(
ifp::fp_add<ifp::UFloat<11, 64>>(x, y, rnd_out, false), ifp::fp_sub<ifp::UFloat<11, 64>>(x, y, rnd_out, false),
rnd_out,
false);
}
Precision Tuner
Compiler
FPCore
RTL
Application
Level Viz
iFP
Architecture Specification Language
(emerging industry machine readable specification language)
FPCore
C++

## Slide 6: Implement
6
Infinite
Bit-Widths
6
Estimate
HDL
Reasonable
Bit-Widths
Reasonable
Performance
Best
Performance
Spec
C++
Model
Final
HDL
initial
Manual
HLS
Media Kernel
-30% area
-20% delay
Using modelling SW in HLS typically produces extremely poor results
HLS tools typically can’t match expert designers on Datapath intensive designs

## Slide 7: Optimize
7
ROVER: Datapath High-Level Synthesis
[l,h]
[l,h]
[2,2]
[l,h]
[l,h]
[l,h]
[l,h]
[l,h]
[l,h]
[1,1]
[2,2]
[l,h]
Extractor
Initial
RTL
Value
Range
Analysis
Final
RTL
Compact representation of 1000s designs
(E-graph)
Delay/
Area/
Power
RTL1
RTL2
RTLn
…
FV
FV
FV
FV
FV
FV
Rewrites
Competitive Manual Datapath Design = Value Range Analysis + Rewriting
FP16 Floating-Point
Adder
33% faster
41% smaller
Runtime: 22 mins
# rewrite passes: 11
Node Growth: 110-40,000
Infinite
Bit-Widths
Final
HDL
sum [276:0] = (a << shift) + b;
renorm[276:0] = Renormalize(sum);
y [ 23:0] = renorm >> 253;
a[22:0], b[22:0],
a[22]=b[22]=1
sum [24:0] = a + (b>>shift);
renorm[24:0] = Renormalize(sum);
y [23:0] = renorm >> 1;
Core
FP32 Adder
Optimisation

## Slide 8: Full Flow
8
Simulator
Precision Tuner
Compiler
FPCore
Application
Level Viz
iFP
C++
Model
Estimate
SystemC
/HDL
Final
HDL
Application-Level Testing
HLS
Power/ Performance/Area
Estimates
ROVER
What if we could
specify, simulate, model, implement & optimize
1000s of designs in a day?
Progressive Interim Feedback
~1 Day

## Slide 9
9
Summary
Multiple number formats, multiple precisions, the real answer in an executable way:
FPCore https://fpbench.org
iFP simulates FPCores and does precision tuning to detect numerical instabilities
iFP then compiles the finalized FPCore into bit-accurate sim & FV friendly C++
The C++/SystemC can be used to provide HW cost estimates via HLS
ROVER can optimize behavioral SystemC/RTL to produce competitive RTL
- generates its own formal verification story
Specify
Simulate
Model
Implement
Optimize
These tools have achieved a novel numerical hardware design methodology
From machine readable specification to optimized RTL.
Session: Leading Developments from the Frontier of High-level Synthesis and Neighborhoods
Automating Constraint-Aware Datapath Optimization using E-Graphs
Time: Wednesday 12th 11:10 - 11:25
Location: 3002, 3rd Floor
Learn more
about Rover: