## Slide 2: Sophisticate Performance Verification Of SOC BUS By IP-XACT And Model
Hyungtae Park, Hyunjin Kim, Taehwa Ko,
Hyunjae Woo, Youngsik Kim, Seonil Brian Choi
Samsung Electronics Co., LTD.

## Slide 3: Agenda
Motivation
Overall Concept of Flow
Detailed technics and automation
Evidence
Summary

## Slide 4: Motivation
Requirement of SOC bus performance verification
  Existing design verification alone cannot find performance-related bugs, and if performance-related issues are found, they are often very serious.
  There was a performance analysis method using an existing TG (Traffic Generator), but it was difficult to interpret the results or precise analysis was often impossible, so improvement was needed.
  To ensure high-performance SOC chips, various combinations of performance tests and precise performance measurement methods are required.
Limitation about performance verification for current SOC bus fabrics
  The number of data paths to be tested is increasing, and in the case of premium chips, there are more than 100.
  As the SOC becomes more complex and the bus layers increase, the data path from master to Slave (mostly DRAM) becomes longer.
  The time required for RTL development is decreasing, and it is not easy to allocate time for performance verification after function verification.

## Slide 5: Main Idea (Overall Concept of Flow)
The performance evaluation (PE) is based on the systemC model and tests to configure the BUS fabric that satisfies the performance specifications. At this time, various tests are performed, from a stand-alone performance test to a test in which several masters operate in combination.
  Performance verification (PV) is performed with real RTL to test the performance of BUS fabric and Memory controller to verify and confirm.
  The most important concept is whether the test performed by PE can be performed in the same way in PV. IP-XACT and TG configuration automation enables to use the exact same traffic pattern and test point for RTL tests.

## Slide 6: Main Idea (Re-use of Model simulation environment)
PE/PV consecutive executions
  PE(Model simulation)
    Simulation using model is performed in various ways by adjusting Scenario, QoS, and Performance knob (over 1000ea)
  PV(RTL simulation)
    Previously,
      one or two Scenarios performed by PE were selected and performed. Difficult to run scenarios of various combinations.
      Difficult to interpret and pass/fail decisions on the results performed
    Now,
      Reuse the same test list of PE which enables to run over 1000ea.
      QOS configuration can be re-used.
      !!!Exact same performance result is expected

## Slide 7: Main Idea (Use of IP-XACT)
IP-XACT for the TG insertion
  For the same scenario test of RTL and model, it is necessary to have TGs operating in the same hierarchy location.
  TG insertion information for RTL verification can be extracted by using IP-XACT that has design information.
  TG instance can be automatically created by parsing the IP-XACT with the model's hierarchy/instance information. More than 100 masters is created in the SOC without manual operation.

## Slide 8: Main Idea (Automated TG configuration)
TG parameter configuration
  For precise verification of BUS fabric RTL, it is necessary to use the traffic pattern used in the model as it is.
  More than 1000 tests are performed, from stand-alone tests to more than 100 master combinations.
  TG (Traffic generator) parameter configuration of AMBA AXI/ACE protocol is shared from Model test
  The Scenario Manager unit is designed to automatically configure the parameters of each TG in the system.

## Slide 9: Evidence (#1)
Very precise test result
  The result of DUT (BUS Fabric RTL) can be directly compared to result of model within an error of less than 5% in performance metrics like BW, Latency, and MO (Multiple outstanding) numbers.
  ARQ buffer size bug and long latency issue caused by clock gating were detected by comparing the result of RTL and Model which was not previously easy.
BW result comparison
(RTL vs Model)

## Slide 10: Evidence (#2)
Efficient execution
  As we can have seamless process from architecture to RTL development by using the IP-XACT and TG automation, we can enhance the efficiency of tests.
  Reduced human error in TG insertion and configuration.
  By recycling the previously confirmed scenarios, the time required to configure the scenarios has been reduced. Enables to execute more test scenario in early stage and verify the performance before the RTL freeze.

## Slide 11: Summary
Developed sophisticate SOC bus performance verification flow
  A precise methodology for measuring the performance of BUS topology has been developed by directly comparing the performance results of the SystemC model and RTL.
  BW and latency, which are major performance indexes, can be measured at an error rate of less than 5%.
Expand the coverage of performance verification
  Reduces human errors through IP-XACT and automation and reduce the TAT.
  Numerous combinations of scenarios can be tested, increasing the coverage of performance verification.
Helps to design performance-satisfied SOC
  Sophisticated performance verification can detect performance bugs related to BW, Latency, and MO numbers and it helps to design a performance-satisfied SOC.