## Slide 2: Debug Accelerator & Performance Validator
                Samsung Semiconductor India Research
                Ratan Deep (ratan.deep@samsung.com)
                Harsh Setia (harsh.setia@samsng.com)
                Shashank N (shashank.n@samsung.com)
                Sudhakar Bansal (s.bansal@samsung.com)

## Slide 3: Motivation and Problem Statement
Debugging is always a challenge at SOC level verification:
  Difficult to catch corrupted transactions flowing through multiple levels of components
  Time Consuming Manual analysis using wave-dump
  Big size waveform dump- Slow response from waveform tool
  Prone to human error - Manual protocol analysis at each stage
  Addition of Monitors can impact simulation performance
If unwanted latency at some stage is causing performance degradation
  Manual analysis of throughput in any given time window
  End to End Performance checks – impacts simulation time
Master
Corrupted Stage

## Slide 4: Main Idea
Augment debugging by having a time accurate transaction list [as in-hand guide] by using wave dump [without any manual effort]
  Saves a lot of time in mapping transaction trace
  Identification of corruption becomes very easy and fast
  Does not require re-simulation with additional components
Debug process using DAT [Debug Accelerator Tool]:
  Wave dump is created
  Signal list is fed to tool
  Desired time window is provided
  Tool provides complete transaction list in xls format
Performance Validation
  Throughput visualisation in a given time window
  Latency calculation w.r.t protocol channels
  Identification of stage causing unwanted delay
Wave Dump
Signal List
Tool
Tool Configurations
TOOL
.xls file

## Slide 5: Tool Realization [For AXI Protocol]
.fsdb file
VCD conversion
.vcd file
.rc file
TB Automation
AXI VIP
Monitor.txt
vcd.sv
module
vcd.sv
module
Stimulus from VCD
Monitor.txt
Monitor output
Data extraction
.xls file
LEVEL-1
LEVEL-3
LEVEL-2
Test Bench
AXI VIP
AXI VIP
Inputs
Outputs
TB class
Intermediate generated Test Bench

## Slide 6: Results
Debug Tool Deployment on a Sub-system level wave dump [8GB, 1 ms simulation time, multiple stages] where 5 AXI stages were traced over a time span of 20us
  3 Minutes : The average time taken by the tool over 10 iterations
  Extracted 1000+ AXI transactions
  Much easier to point out the faulty transaction from a given list
  Improvement factor [Average from a number of debug efforts]
    3x-5x Improvement [Manual debug –> 45-50 minutes; Tool –> 10-15 minutes]
    >5x Improvement compared to interface monitors technique

## Slide 7: Conclusion/Summary
Tool Advantages:
  Post simulation process
  Selection of only required interfaces
  Simulation run time is small
  Transactions information in xls format
  Analysis on higher abstraction level.
  Performance Analysis
  Protocol checking
  Validity analysis w.r.t transaction attributes
  Protocol agnostic: Can be extended for any protocol
Really helpful in real-time debugging application and saves a lot of man hours
Saved man hours in-turn can be invested in enriching DV quality by brainstorming corner case scenarios
With growing design complexity and completion in time to market where DV takes around 70% of overall chip cycle it becomes very essential to have robust and efficient DV methodology process and this tool supports in realizing this fact.

## Slide 8: Thank You