## Slide 2: Emulation Based Automation Platform For SoC Performance Verification
Jisu Yang Jeonggu Lee
Seolgyeong Jeong Hyunjae Woo
Youngsik Kim Seonil Brian Choi
Samsung Electronics Co., LTD.

## Slide 3: Motivation (1/2)
Millions of combinations of configurations for SoC Performance Verification
  To perform *PV test for several scenarios including not only many multi-media IPs such as sensor model, image processing, display but also Bus and memory controllers, there are too many combinations of set values
  Receiving inappropriate settings among engineers or manually setting up numerous configurations used to cause serious problems of having to redo the experiment due to incorrect settings
  In addition, the scattered configurations here and there took a lot of time when we had to set up the experimental environment to reproduce issues
  *Performance Verification

## Slide 4: Motivation (2/2)
Long PV test execution time
  Despite the long experiment time, there was no environment
  where we can see various logs or performance figures
  at once during runtime
  So tuning point could be determined only after the test was over,
  which was a waste of time
More and more monitors by design complexity
  As the types and number of monitors for PV have increased drastically,
  post-processing processes are required to analyze meaningful results from massive outputs
  Usually, the results are reported more than hundreds of times per projects,
  it is impossible to manually convert and analyze them on time without an automated platform
  SYNC
  RUN
  REPORT
Manage and
Automatically Set
Configurations
Reproduce Experimental Environment
Profile Data
during Runtime
Enable Regression
Environment
Support Customizable Function
Post-process
for Outputs from
Lots of Monitors
Figure 1. Platform Composition

## Slide 5: Main Ideas (1/3)
Function 1 : SYNC
  Each verification engineer uploads data for their blocks corresponding to each scenario
  SYNC manages millions of configuration sets according to project/scenario/version
  When top engineer selects options and downloads data,
  SYNC sets automatically for selected components
  This enables to minimize human error and save time by
  reducing iteration between engineers and simply
  reproduces the last experimental environment
Figure 2. Data Managing Diagram of SYNC
  *MEDIC is the name of this platform

## Slide 6: Main Ideas (2/3)
Function 2 : RUN
  For each test list, you can get the profiling data whenever you want while the test
  Factors that can be critical issues for scenario performance such as bandwidth, latency, MO, SLV / DEC error and interrupt can be seen at a glance
  This is a great help in getting insight for analysis and enables to respond immediately when an issue occurs
  In addition, various pre/post tasks provided by the emulator are supported in the form of customizable command function to increase test convenience and facilitate analysis during runtime
Figure 3. Concept of RUN

## Slide 7: Main Ideas (3/3)
Function 3: REPORT
  Once you select a performed test, REPORT analyzes raw data from various monitors and parses logs to convert the experiment outputs into performance measurement indices such as latency distribution, DRAM utilization, fps and buffer level depending on monitors
  This not only reduces post processing time to get meaningful results from very massive data, but also allows you to strengthen the basis for the cause of weak performance
  As new monitors continue to be added as designs become more complex and emulators diversify, REPORT is also improved to support them
Figure 4. Performance Summary Report
Figure 6. Burst Length Distribution Chart
Figure 5. Latency Distribution Chart
Performance Index

## Slide 8: Evidence
Figure 7. SYNC Download UI
Figure 9. Bandwidth Timeline, MO Distribution Graph and Information Windows by Parsing Multiple Logs during Runtime
Figure 8. Bandwidth, Latency, MO from REPORT

## Slide 9: Summary
This automation platform allows following features
Reduced the time required for verification and human error
  Due to the nature of PV having millions of configuration sets, a system was needed to manage and automatically set those settings
  Minimized human error due to a significant decrease in manual task
  Shorten development time due to reduced unnecessary iteration between engineers
  Made it easy to reproduce experimental conditions with simple operation through UI
Provided various performance features and logs at a glance during runtime
  Due to the long PV experimental time, catching phenomena that can have a fatal impact on performance during runtime was very important
  Various outputs and logs were scattered here and there, making it difficult to catch them at the beginning of the test
  Helped to get insight for analysis and allowed to respond immediately when an issue occurs by providing a platform where you can see the figures such as bandwidth, latency, MO, bus error, and interrupt that can be critical issues for performance at a glance
Provide output values from massive monitors and logs into performance indices
  As the types and number of monitors for PV increased drastically, the time spent for post-processing required to obtain meaningful results from a huge amount of output has become longer and longer
  Enabled to do this very simply by providing an environment where we can analyze the cause of low performance through more diverse monitors

## Slide 10: Thank You