## Slide 2: A Joint IP-XACT/RTL Design Flow for Large SoCs

## Slide 3: Authors & Presenters
[Today’s Speaker] Chouki Aktouf, CTO, Defacto, France
Maël Rabé, Application Engineer, Defacto, France
Valentin Boyer, Product Manager, Defacto, France

## Slide 4: Problem Statement
Complex SoC Integration is historically made using flows either
  Purely RTL with in-house solution
  Mix between in-house and third-party solution around proprietary format
The main integration challenges for SoC Integration are
  Runtime : For all the solution runtime is a key parameter
  Design size : As Soc Design are relatively big, solutions should handle the complexity.
    IP-XACT 2014 is not able to fully describe the complexity of design needed for integration. (E.g., user defined type, struct, package libraries)
    RTL alone will increase the effort of making connection between groups of ports belongs to same architecture protocol
Need from SoC Integration to improve the current methodology to be able to consider IPs in any format
  Solution needed also includes a complete RTL and IP-XACT version support (Verilog, System Verilog, VHDL, IP-XACT 2009, IP-XACT 2014)
  Implement the missing information in IP-XACT using VendorExtension is not suitable as this make the generated IP-XACT not vendor-agnostic.

## Slide 5: Current Solutions & Need
Current available solutions
  Current workaround was to redesign IP dropped advance System Verilog construct for datatype and use of package to align with what IP-XACT 2014 can support or making connection pin to pin.
  This workaround is tedious, risking of breaking existing design, time consuming and hard to maintain.
Motivation
  Front-end design teams need a simple yet comprehensive integration flow. The solution must be generic to handle both SoC and subsystem requirements.

## Slide 6: Presented Solution Requirements to have a successful flow
IP design shouldn’t have any restriction in using any synthesizable user defined datatype for ports and using these ports for bus interfaces connection as well as pin to pin connection.
IP design shouldn’t have any restriction in using any synthesizable datatype for parameters and using these parameter for design configuration during integration
IP design shouldn’t have any restriction is using package that defines parameters and datatype.
Joint IP-XACT & RTL flow need to be able to combine design information from both IP-XACT view as well as pure RTL view without conflict and enable seamless RTL integration flow

## Slide 7: Presented Solution Flow using Defacto’s SoC Compiler
The joint IP-XACT & RTL flow will first read in component and design IP-XACT and based on IP-XACT’s fileSetRef read in the corresponding RTL files. This include top level RTL files as well as package files if required.
During elaboration, any conflict between IP-XACT and RTL that cannot be resolved will be reported out.

## Slide 8: Presented Solution Joint Flow/Design Methodology at the Front-End
Conciliate RTL with variety of multi-domain design standards:
  LEF
  SDC
  UPF
  IP-XACT
Front-end SoC Integration
Structural Verification and Design Exploration
Multi-format IP Insertion & Connectivity Insertion
Generation of full chip views
Design centric checks based on unified database

## Slide 9: Presented Solution Interface with Defacto APIs
All IPs designs to be integrated need to provide component IP-XACT with proper fileSets. I.e., all path used in fileSet should be related to location of IP-XACT. Same integration with hierarchical IP-XACT.
All IP-XACT are loaded with extra option to provide macros to be used when reading RTL files from fileSets if required.
During elaboration, option is given whether RTL files from fileSets are required.
If there’s conflict between IP-XACT and RTL that SoC Compiler cannot resolved (E.g. port present in RTL is not in IP-XACT or vise versa), error will be reported. Integration flow will stop if there is error otherwise it should proceed with normal integration

## Slide 10: Typical Example
Example of RTL design with user define type which has definition in package file. These type of information is not able to represent in current IP-XACT 2014.
  Without RTL information, there no way to know the content of the struct datatype and there’s no way to make connection with element in a struct.
    E.g. making connection with p2c_st.intfPort and p2c_st.intfBus separately.
    E.g. mapping p2c_st.intfPort and p2c_stintfBus to different bus interface logicalPort.
  Without knowing of struct content, there’s no way to have wire between to connection point still maintain as struct datatype
module ipxA import mypkg::*; #(
parameter …
)
(
input mypkg::stIntf c2p_st,
output mypkg::stIntf p2c_st,
..
package mypkg;
…
typedef struct packed {
logic [3:0] intfBus;
logic intfPort;
} stIntf;
…
endpackage
Component IP-XACT - ports
…
<ipxact:port>
<ipxact:name>p2c_st</ipxact:name>
<ipxact:wire allLogicalDirectionsAllowed="false">
<ipxact:direction>out</ipxact:direction>
<ipxact:vectors>
<ipxact:vector>
<ipxact:left>8</ipxact:left>
<ipxact:right>0</ipxact:right>
</ipxact:vector>
</ipxact:vectors>
<ipxact:wireTypeDefs>
<ipxact:wireTypeDef>
<ipxact:typeName constrained="false">mypkg::stIntf</ipxact:typeName>
<ipxact:typeDefinition>libA.mypkg</ipxact:typeDefinition>
<ipxact:viewRef>RTLsource</ipxact:viewRef>
</ipxact:wireTypeDef>
</ipxact:wireTypeDefs>
</ipxact:wire>
</ipxact:port>
<ipxact:port>
Component IP-XACT - fileSets
<ipxact:fileSets>
<ipxact:fileSet>
<ipxact:name>fs-RTLsource</ipxact:name>
<ipxact:file>
<ipxact:name>./mypkg.sv</ipxact:name>
<ipxact:fileType>systemVerilogSource</ipxact:fileType>
<ipxact:isIncludeFile externalDeclarations="false">false</ipxact:isIncludeFile>
<ipxact:logicalName default="false">libA</ipxact:logicalName>
</ipxact:file>
<ipxact:file>
<ipxact:name>./ipxA.sv</ipxact:name>
<ipxact:fileType>systemVerilogSource</ipxact:fileType>
<ipxact:isIncludeFile externalDeclarations="false">false</ipxact:isIncludeFile>
<ipxact:logicalName default="false">libA</ipxact:logicalName>
</ipxact:file>
</ipxact:fileSet>
</ipxact:fileSets>

## Slide 11: Evidence
The flow has been experimented in several Customer’s SoC projects
In one of customer’s SOC design, there are
  794 IP designs from 110 IP team and instantiated to 3900 instances which scatter across 69 hierarchies each has 2 levels.
    Out of 794 designs, 646 of them are with IP-XACTs
  There are cross to 3k bus interface connections 45k adhoc connection
  The runtime for the complete integration process is 35 mins
  The flow can be mainly scripted using the Defacto’s Tcl APIs
  The enablement of joint IPXACT-RTL integration is seamless on top of existing Defacto Tcl based integration flow as the capability was handle in existing Defacto APIs

## Slide 12: Summary
This joint IP-XACT and RTL methodology allows integration and connection between different IP nature without changing of flow
  IPs with complex user defined datatype use in both bus interface and pin-to-pin connection
  IPs with common package that defined complex user defined datatype
  IPs with RTL only
  IPs with IP-XACT only and connect with only bus interface
This new methodology helped simplify RTL integration flow without changing IP designs and without extra coding in the flow to handle information that’s not defined in IP-XACT 2014
  The scalability of the solution also brings high transferability across different designs.
  With simple API interactions, overall scripting process to integrate the features into custom flow is smooth.
This solution is now used in customer’s multiple SoC integrations